DRAFT

Regulation Impact Statement

for

Underrun Protection

A draft statement inviting discussion and comments from

parties affected by the proposed heavy commercial vehicle safety initiative

January 2007

Report Documentation Page

| Report No. DOTARS VSS 01/2006 | Report Date January 2007 | File No. | ORR Reference No. 7317 |
| --- | --- | --- | --- |
| Title and Subtitle Regulation Impact Statement for Underrun Protection |
| Organization Performing Analysis Standards and International Vehicle Safety Standards Branch Department of Transport and Regional Services GPO Box 594 Canberra, ACT 2601 |
| Regulatory Agency Department of Transport and Regional Services Vehicle Safety Standards Branch GPO Box 594 Canberra ACT 2601 |
| Abstract The aim of this Regulation Impact Statement (RIS) is to examine whether there is a need for government intervention, to be directed towards new vehicle construction, in order to reduce the trauma from road crashes involving heavy commercial vehicle underrun. These crashes are often severe, because of the incompatibility in both mass and geometry of heavy vehicles and other road users such as passenger cars, motorcycles, bicycles and pedestrians. The need for some type of Underrun Protection (UP) was identified. Costs and benefits were estimated for eight possible non-regulatory and regulatory options to introduce UP. Although self-regulation is very much on the agenda of the road freight transport industry, it was concluded that the level of competition within the industry and the externality of any benefits achieved would not make this an effective option. It was demonstrated in line with the Council of Australian Governments (COAG) principles for making national standards that there would be a maximum net benefit in mandating an Australian Design Rule (ADR) for front UP for new rigid and articulated heavy commercial vehicles with a Gross Vehicle Mass (GVM) greater than 7.5 tonnes. The ADR would adopt the United Nations Economic Commission for Europe (UNECE) standard R 93. It was assumed that the state and territory road authorities would raise the current 6 tonne steer axle limit to at least 6.1 tonne to account for the extra mass of the UP system. It was also concluded that the rear bumper requirements for semi-trailers in ADR 42/04 should be withdrawn, without mandating replacement rear UP. It was not recommended that side UP be mandated. |
| Key Words Underrun, trucks, crash protection, fatality reduction, UP, UPS, FUP, FUPS, FUPD, RUPS, RUPD, SUPS, SUPD | Distribution Statement Document is available to public through the web site: www.dotars.gov.au |
| Security Classification Unclassified | No. of Pages 129 | Price No charge |

Submitting Comments

The Department of Transport and Regional Services invites comments from interested parties and parties affected by the provisions of this Regulation Impact Statement.

Comments should be submitted using the attached format.

Comment Form A should be used by heavy commercial vehicle/trailer manufacturers, heavy commercial vehicle importers and bull bar manufacturers.

Comment Form B should be used by state and territory government agencies having responsibility for road transport safety.

Comment Form C should be used by motoring clubs and other road user agencies representing the interests of motorcycle riders, bicycle riders and pedestrians.

Comments would be preferred by email and sent to: standards@dotars.gov.au

Comments may be sent by fax to: 61 2 6274 7714

Comments may be sent by post to the following address:

The General Manager

Vehicle Safety Standards Branch

Department of Transport and Regional Services

GPO Box 594

Canberra  ACT 2601

For further information please contact:

Standards and International Section

Vehicle Safety Standards

Maritime and Land Transport Division

Department of Transport and Regional Services

GPO Box 594, Canberra, ACT 2601

Telephone: 02 6274 7440

Fax: 02 6274 7714

Email: standards@dotars.gov.au

Comment Form A

To be used by heavy commercial vehicle/trailer manufacturers, heavy commercial vehicle importers and bull bar manufacturers

- Please provide details of your organisation

| Name of Organisation |  |
| --- | --- |
| Address |  |
| Postal |  |
| Telephone |  |
| Fax |  |
| Email |  |
| Contact Person |  |
| Position |  |

- Please indicate which option you support

| Option | Yes | No |
| --- | --- | --- |
| Option 1 – Self-Regulation by Heavy commercial vehicle Manufacturers/Importers |  |  |
| Option 2 – National Heavy Vehicle Accreditation Scheme |  |  |
| Option 3 - Industry Code of Practice |  |  |
| Option 4 - Australian Standard |  |  |
| Option 5 – State and Local Government Fleet Purchasing Arrangements |  |  |
| Option 6 – Business as usual |  |  |
| Option 7 – ADR adopting FMVSS, UNECE Regulations, EEC Directives and Brazilian Regulation |  |  |
| Option 8 – ADR adopting UNECE Regulations 93 for rigid and articulated trucks with a GVM greater than 7.5 tonnes |  |  |

- Please respond to the following questions

| 1 | Can heavy commercial vehicle manufacturers and importers confirm if any models offered to the Australian market are fitted with front, rear or side Underrun Protection (UP)? | Yes | No |
| --- | --- | --- | --- |
| 2 | If NO, does your company intend to fit UP? | 1-2 years | 3-5 years |
|  |  | Yes | No | Yes | No |
| 3 | Can heavy trailer manufacturers confirm if any models offered to the Australian market are fitted with side UP? | Yes | No |
| 4 | If NO, does your company intend to side fit UP? | 1-2 years | 3-5 years |
|  |  | Yes | No | Yes | No |
| 5 | Has voluntary provision of UP had any impact, positive or negative on your sales volumes? | Positive | Negative |
|  |  | Yes | No | Yes | No |
| 6 | If fitted, can heavy commercial vehicle and trailer manufacturers confirm whether UP meet UNECE Regulations 93, 73 and 58? | Front |
|  |  | ECE R 93 | Other |
|  |  | Yes | No | Yes | No |
|  |  | Side |
|  |  | ECE R 73 | Other |
|  |  | Yes | No | Yes | No |
|  |  | Rear |
|  |  | ECE R 58 | Other |
|  |  | Yes | No | Yes | No |
| 7 | Can heavy commercial vehicle and trailer manufacturers and importers provide any costs for UP that meet requirements of UNECE R 93, 73 and 58 |
|  | Rigid front UP | AUD |
|  | Development cost (design + prototype + testing + production engineering + production equipment + production tooling) |  |
|  | Production material and labour cost (material + labour used for production of device) |  |
|  | Unit price (if obtained from supplier) |  |
|  | Rigid side UP |  |
|  | Development cost (design + prototype + testing + production engineering + production equipment + production tooling) |  |
|  | Production material and labour cost (material + labour used for production of device) |  |
|  | Unit price (if obtained from supplier) |  |
|  | Rigid rear UP |  |
|  | Development cost (design + prototype + testing + production engineering + production equipment + production tooling) |  |
|  | Production material and labour cost (material + labour used for production of device) |  |
|  | Unit price (if obtained from supplier) |  |
| 8. | Can bull bar manufacturers identify any impact in sales, costs or other areas if bull bars for new vehicles must be designed and tested to meet UNECE R93 requirements? |

- Any other comments

Comment Form B

To be used by State and Territory transport and road safety agencies

- Please provide details of your organisation

| Name of Organisation |  |
| --- | --- |
| Address |  |
| Contact Person |  |
| Position |  |

- Please indicate which option you support

| Option | Yes | No |
| --- | --- | --- |
| Option 1 – Self-Regulation by Heavy commercial vehicle Manufacturers/Importers |  |  |
| Option 2 – National Heavy Vehicle Accreditation Scheme |  |  |
| Option 3 - Industry Code of Practice |  |  |
| Option 4 - Australian Standard |  |  |
| Option 5 – State and Local Government Fleet Purchasing Arrangements |  |  |
| Option 6 – Business as usual |  |  |
| Option 7 – ADR adopting FMVSS, UNECE Regulations, EEC Directives and Brazilian Regulation |  |  |
| Option 8 – ADR adopting UNECE Regulations 93 for rigid and articulated trucks with a GVM greater than 7.5 tonnes |  |  |

- Please respond to the following questions raised in the RIS

- Do you have data giving the number of underrun collisions with a breakdown into frontal, side, rear end and front/side swipe between heavy commercial vehicles with passenger cars, SUVs, motorcycles, bicycles and pedestrians,  itemising each road user category between 1998-2006.

- Do you have data giving the number of fatal, serious injuries (hospitalized) and minor (not hospitalized) injuries from underrun collisions for each road user category identified above and/or for different types or configurations of heavy vehicle?

- Any other comments

Comment Form C

To be used by motoring clubs and other road user associations

representing motorcycle riders, bicycle riders and pedestrians

- Please provide details of your organisation

| Name of Organisation |  |
| --- | --- |
| Address |  |
| Contact Person |  |
| Position in the organisation |  |

- Please indicate which option you support

| Option | Yes | No |
| --- | --- | --- |
| Option 1 – Self-Regulation by Heavy commercial vehicle Manufacturers/Importers |  |  |
| Option 2 – National Heavy Vehicle Accreditation Scheme |  |  |
| Option 3 - Industry Code of Practice |  |  |
| Option 4 - Australian Standard |  |  |
| Option 5 – State and Local Government Fleet Purchasing Arrangements |  |  |
| Option 6 – Business as usual |  |  |
| Option 7 – ADR adopting FMVSS, UNECE Regulations, EEC Directives and Brazilian Regulation |  |  |
| Option 8 – ADR adopting UNECE Regulations 93 for rigid and articulated trucks with a GVM greater than 7.5 tonnes |  |  |

- Any other comments

Important Notice

This Regulation Impact Statement is an exposure draft document that is released for feedback and comment. Its contents should not be cited or published and no responsibility is accepted for unauthorized disclosure. The release of this paper for comment does not in any way constitute a commitment on behalf of the Australian Government to adopt the approach outlined nor is any undertaking given as to the extent to which comments received may be adopted. The Australian Government does not endorse products or manufacturers. Trade or manufacturers names appear only because they are considered essential to the objects of this statement.

# Abstract

The aim of this Regulation Impact Statement (RIS) is to examine whether there is a need for government intervention, to be directed towards new vehicle construction, in order to reduce the trauma from road crashes involving heavy commercial vehicle underrun. These crashes are often severe, because of the incompatibility in both mass and geometry of heavy vehicles and other road users such as passenger cars, motorcycles, bicycles and pedestrians.

The need for some type of Underrun Protection (UP) was identified. Costs and benefits were estimated for eight possible non-regulatory and regulatory options to introduce UP.

Although self-regulation is very much on the agenda of the road freight transport industry, it was concluded that the level of competition within the industry and the externality of any benefits achieved would not make this an effective option.

It was demonstrated in line with the Council of Australian Governments (COAG) principles for making national standards that there would be a maximum net benefit in mandating an Australian Design Rule (ADR) for front UP for new rigid and articulated heavy commercial vehicles with a Gross Vehicle Mass (GVM) greater than 7.5 tonnes. The ADR would adopt the United Nations Economic Commission for Europe (UNECE) standard R 93. It was assumed that the state and territory road authorities would raise the current 6 tonne steer axle limit to at least 6.1 tonne to account for the extra mass of the UP system.

It was also concluded that the rear bumper requirements for semi-trailers in ADR 42/04 should be withdrawn, without mandating replacement rear UP. It was not recommended that side UP be mandated.

CONTENTS

Abstract	10

Summary and Recommendation	13

Summary	13

Recommendation	14

Background	16

1	Problem	18

Nature of the Problem	18

Economic Cost of the Problem	20

Types of underrun crashes and policy prescriptions	23

Responding to the problem	23

Economic Aspects of  Underrun Protection: Benefit-Cost Analysis	26

Costs for provision of Underrun Protection	26

Costs and Benefits from installing UP under a variety of scenarios	29

2	Objectives	35

3	Options	36

Option 1: Self-Regulation (of front, side and rear Underrun Protection)	38

Option 2: National Heavy Vehicle Accreditation Scheme (NHVAS)	39

Option 3: Industry Code of Practice	40

Option 4: Australian Standard	41

Option 5: State and Local Government Fleet Purchasing Arrangements	41

Option 6: Business-as-usual	41

Option 7: Australian Design Rule adopting front Underrun Protection regulations from Europe, Japan and United States	42

Option 8: Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes	42

4	Impact Analysis	42

The Affected Parties	43

Impact on Existing Regulations	44

Option 1: Self-Regulation (of front, side and rear Underrun Protection)	44

Options 2&3: National Heavy Vehicle Accreditation Scheme / Industry Code of Practice	48

Option 4: Australian Standard	48

Option 5: State and local government fleet purchasing arrangements	48

Option 6: Business-as-usual	48

Option 7: Australian Design Rule adopting front Underrun Protection requirements from other countries	49

Option 8: Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes	49

5	Consultation	53

6	Conclusion and Recommended Option	54

7	Implementation and Review	57

References and Data Sources	58

Abbreviations	61

Glossary	63

Appendix 1: VEHICE CATEGORIES in the australian design rules	64

Appendix  2: The heavy commercial vehicle assembly and wholesaling industry in australia	65

Appendix 3: SOURCES OF data collection	71

Appendix 4: review of selected studies on Underrun Protection devices	73

Appendix 5: METHODOLOGY OF BENEFIT-COST ANALYSIS	76

Appendix  6: RESULTS OF BENEFIT-COST ANALYSIS	81

APPENDIX 7: LIST OF AFFECTED PARTIES	125

APPENDIX 8: Technical liaison Group	126

APPENDIX 9: UNECE R93 Front Underrun Protection	127

Notes			128

# Summary and Recommendation

## Summary

The impact that road crashes have on society is significant, costing the Australian economy approximately $15 billion per year. Crashes involving heavy commercial vehicles (a goods carrying vehicle with a Gross Vehicle Mass (GVM) greater than 3.5 tonnes) colliding with passenger cars, motorcycles, bicycles and pedestrians have an increased likelihood of producing a severe injury or fatality.  This is mainly due of the incompatibility in mass and geometry between heavy vehicles and other road users.

This RIS addresses a subset of heavy commercial vehicle crashes, referred to as a “heavy vehicle underrun crash”.  A heavy vehicle underrun crash occurs when a passenger car, motorcycle, bicycle or pedestrian slides underneath the front, side, or rear end of a heavy commercial vehicle.  These collisions have become an increasing cause for concern in the Australian community.

In a typical passenger car fatal front or rear crash involving underrun, there are high levels of intrusion into the occupant space.  Research suggests that the usual occupant protection features built into cars such as seatbelts, airbags, energy absorbing steering columns and crush zones are not engaged, due to the incompatibility of the colliding vehicles’ geometries.

During the period 1990 to 1999, an average of about 50 people were killed annually in Australia in underrun crashes. Around 40 of these fatalities were passenger car occupants, 5 were motorcycle riders, 5 were bicyclists and an estimated 10-15 were pedestrians. The drivers of the heavy commercial vehicles are rarely killed or injured.  Where a fatal underrun crash involved an articulated heavy commercial vehicle, it was more likely to be in a rural area.  Rigid vehicles were more evenly balanced between rural and urban.  These figures may increase in the future, given an expected doubling of the freight transport task by 2020.

Heavy commercial vehicle Underrun Protection (UP) has been investigated since the 1980s in various countries and is now mandatory in the European Union (EU) for commercial vehicles exceeding a GVM of 3.5 tonnes.  Some member countries of ASEAN and the three most populous and fast growing economies of China, India and Brazil also have some form of UP requirements for heavy commercial vehicles.  Currently, Australia only has Australian Design Rule (ADR) 42/04 – General Safety Requirements, Clause 8 Rear Bumpers for Semi-trailers, to respond to the underrun problem.  This ADR applies only to the rear of semi-trailers and its geometric and test requirements are acknowledged as being inadequate.

The estimated cost (in 2005$) of heavy commercial vehicle underrun trauma is $266 million and non-trauma is $71 million resulting in a total cost of $337 million per year.

While the heavy commercial vehicle manufacturer or operator would bear the cost of fitting UP, the principal beneficiaries would be other road users and the community generally (through the reduction in the severity of injuries). Therefore, existing market arrangements are not likely to respond to the problem and government intervention of a non-regulatory or regulatory type may be needed.

Four scenarios were prepared for estimating the benefits of the application of rigid UP on new rigid and articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM) (some NB and all NC Australian Design Rule (ADR) category). A number of assumptions had to be made, including the effectiveness of UP, the discount rate and the expected vehicle life. It was also necessary to assume that a mass increase of 100 kg on the front axle would be granted by the states and territories in their steered axle limits (otherwise a rough estimate of the cost of this extra mass was shown to be significant).  Because of the assumptions, a range of scenarios and sensitivities were included.  A summary of the results is given below.

Summary of Benefit-Cost Ratios (BCR)  from the provision of UP on new heavy commercial vehicles

|  | Front | Side | Rear |
| --- | --- | --- | --- |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 6.5 | 4.0 | 1.7 | 1.0 | 0.6 | 0.2 | 0.5 | 0.3 | 0.1 |
| Articulated | 39.2 | 24.0 | 10.1 | 2.8 | 1.7 | 0.7 | 1.7 | 1.1 | 0.5 |

Best case -   discount rate 4% over 25 years, High effectiveness device.

Likely case - discount rate 7% over 15 years, Most likely effectiveness device.

Worst case - discount rate 12% over 10 years, Low effectiveness device.

The benefit-cost analysis found that there was a very strong case for the provision of rigid front Underrun Protection (UP) but little or no net benefit from the provision of side or rear UP. The front UP benefit-cost ratio was around twenty times that of rear UP and at least five times that of side UP.  UP for articulated vehicles was around six times that for rigid vehicles, demonstrating that underrun crashes are heavily represented by articulated vehicles. As a result of this, only front UP was considered further by means other than voluntary.

An ADR for UP would have to meet Council of Australian Government (COAG) Principles for National Standards Setting, demonstrating that it is necessary to achieve the government’s vehicle safety objectives and would result in a net benefit to the community. These objectives are also shared by the states and territories and the New Zealand government.

The specific objective of the Australian Government in this case would be to reduce the aggressive nature of heavy commercial vehicles in collisions with passenger cars, motorcycles, bicycles and pedestrians and thereby reduce the cost of road trauma to the Australian community.

## Recommendation

A number of regulatory and non-regulatory options were considered and Option 8 is the recommended option:

Option 8: An Australian Design Rule (ADR) adopting international standard UNECE R 93 for front Underrun Protection (UP) for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes (some NB2 and all NC category vehicles). This would apply to all new vehicles.

It is further recommended that the bumper requirements in ADR 42/04 be withdrawn, without mandating replacement rear UP. It is not recommended that side UP be mandated.

The recommendation for front UP is based on the assumption that the states and territories would at the same time raise the 6 tonne limit on steered axles to account for an additional 100 kg front axle load. Otherwise the recommendation would require further analysis and may change.

The development, implementation and review of Australian Design Rules (ADRs) is an established process.  If there is broad public agreement to the recommendations, an ADR can be determined under the authority of the Minister for Transport and Regional Services under section 7 of the Motor Vehicle Standards Act 1989.  After this,  further development of the ADR would be considered as part of the normal program of ADR review and revision.

# Background

The impact that road crashes have on society is significant. Individuals injured in crashes must deal with pain and suffering, medical costs, wage loss, higher insurance premium rates, and vehicle repair costs. For society as a whole, road crashes result in enormous costs in terms of lost productivity and property damage and cost the Australian economy approximately $15 billion (in 1995 $), or 2 percent of GDP.  This translates to an annual average of $1315 for every person in Australia.

In terms of traffic safety, issues relating to heavy commercial vehicles have drawn considerable attention from policy makers, road safety engineers and the general public. For the purposes of this Regulatory Impact Statement (RIS), a heavy commercial vehicle is defined as a goods carrying vehicle with a Gross Vehicle Mass (GVM) greater than 3.5 tonnes.  Heavy commercial vehicles have many unique operating characteristics which have an effect on crash severity, such as high gross mass, long vehicle length and relatively long stopping distances. Aggregate data and previous research has shown that crashes involving trucks colliding with passenger cars, motorcycles, bicycles and pedestrians have an increased likelihood of producing a severe injury or fatality. This increase is in a large part due to the incompatibility between vehicles due to geometric and mass differences. The compatibility of a vehicle is a combination of its crashworthiness and its aggressivity when involved in crashes with vehicles in the fleet. While crashworthiness focuses on the capability of a vehicle to protect its occupants in a collision, aggressivity is measured in terms of the casualties to occupants of the other vehicle involved in the collision. Crashworthiness is sometimes referred to as self-protection while aggressivity is sometimes referred to as partner-protection.

Crash incompatibility is of concern in all vehicle-to-vehicle collisions. Heavy commercial vehicle-to-car collisions are one specific aspect of this problem but another one relates to heavy commercial vehicle-to-vulnerable road user collisions, such as motorcycles, bicycles and non-vehicles (ie pedestrians).

This RIS addresses a particular type of crash event, which is a subset of heavy commercial vehicle crashes and referred to as a “heavy vehicle underrun crash”.  A heavy vehicle underrun crash occurs when a passenger car, motorcycle, bicycle or pedestrian slides underneath the front, side, or rear end of a heavy commercial vehicle.  Vulnerable  road users such as motorcyclists, bicycle riders and pedestrians tend to feature in side underruns with heavy vehicles. Underrun collisions in recent times have become an increasing cause for concern in the Australian community and there have been calls from various sections of the community for addressing the resultant trauma.

Heavy commercial vehicle Underrun Protection (UP) has a long history of investigation.  European research organizations as well as heavy commercial vehicle manufacturers have been studying the subject since the 80s, initially commencing with rear and side UP and followed by front UP.  Research in Australia, Canada, and the United States commenced in the late 90s and focused mainly on rear underruns, which in Australia contributes to only about 10 per cent of underrun trauma.  In recent years the member countries of the European Union have been instrumental in financing and managing research efforts directed at generating solutions for addressing front underrun trauma, which in Australia accounts for 75 per cent of underrun trauma. Protection for vulnerable road users and passenger car occupants from heavy commercial vehicle underrun is now mandatory in Europe for commercial vehicles exceeding a GVM of 3.5 tonnes.  Some member countries of ASEAN and the three most populous and fast growing economies of China, India and Brazil also have some form of UP requirements for heavy commercial vehicles.

Heavy commercial vehicles represent 3.3 percent of all registered vehicles in Australia and account for 7.5 percent of total kilometres driven on public roads (ABS 9309.0: 2001).  Appendix 1 describes the various categories of goods vehicles as listed in the Australian Design Rules while Appendix 2 illustrates the 13 types of heavy commercial vehicles operating on Australian roads. For all fatalities resulting from a fatal crash on Australian roads, approximately one in fifteen crashes involves a heavy commercial vehicle engaging with a passenger car and one in forty with a vulnerable road user such as a motorcycle, bicycle or pedestrian (ATSB 2002a).  Twenty percent of fatal crashes involve passenger cars and heavy commercial vehicles engaging with each other (ATSB 1997).  Sixty-five per cent of these crashes feature collisions with the front ends of both vehicles and less than 10 per cent feature the front end of the passenger car engaging with the rear end of the heavy commercial vehicle.

Table 1 shows the proportions of different types of vehicles and road users that have been involved in fatal underrun crashes with articulated commercial vehicles in the period 1993 to 2002. It shows that the majority (about 82%) of injured persons are passenger car occupants. Only a few percent of the collisions involving trucks result in serious injuries or fatalities to truck occupants.  This suggests that UP could be an effective tool to reduce the estimated fifty fatalities each year arising from heavy commercial vehicle underrun collisions.

Table 1: Proportion of road user groups involved

in fatal underrun crashes with articulated

commercial vehicles, 1993 to 2002

| Vehicle occupant | Pedestrian | Motorcyclist | Bicyclist |
| --- | --- | --- | --- |
| 82% | 10% | 6% | 3% |

Source: ATSB, FCD, 1993-2002

Note: Totals do not add to 100 per cent due to rounding  of figures

# Problem

## Nature of the Problem

When a heavy commercial vehicle and a passenger car, or vulnerable road user such as a motorcycle, bicycle or pedestrian collide, the results are nearly always more serious for the passenger car occupants or the vulnerable road user than for the heavy commercial vehicle occupants. This is especially true if the front of a smaller vehicle slides under the front or the rear end of a heavy commercial vehicle as happens in a heavy vehicle underrun crash. The high risk of injury to other vehicle occupants from underrun crashes is a result of the lack of compatibility between the colliding vehicles. Vehicle mass, stiffness and geometry affect compatibility. A smaller vehicle under-rides a heavy commercial vehicle to the extent that the heavy commercial vehicle’s front or rear extremity enters the occupant compartment or space of the smaller vehicle. Such occupant space intrusion frequently leads to serious injuries or fatalities.

When an underrun crash between vehicles occurs, there are two noticeable outcomes.  The first, as described above, is the trauma from the exposure of the smaller vehicle’s occupants to impacts with the interior compartment of their vehicle, occupant protection measures in the smaller vehicle being unlikely to engage.  The second is the likelihood of further collisions arising from the loss of control of the heavy vehicle.  This follows from damage to the steering or braking components of the heavy vehicle by the smaller vehicle.

During the period 1990 to 1999, an average of about 50 people were killed annually in Australia in underrun crashes. Around 40 of these fatalities were passenger car occupants, 5 were motorcycle riders and 5 were bicyclists. (ATSB 2004c).  The driver of the heavy commercial vehicle was rarely killed or injured. The number of pedestrians is difficult to estimate as crash databases do not specifically codify pedestrian injury arising from collisions. A very rough estimate would place fatalities of pedestrians in underrun collisions at 10 to 15 persons annually.

Figure 1 shows that there has been a gradual decline in underrun collisions for both articulated truck-car underrun collisions and rigid truck-car collisions from a high of 86 fatalities in 1990 to a low of 45 fatalities in 1999.  The decline could be attributed to a higher intensity in enforcement by state transport agencies, improvements to roadways and heavy vehicle accreditation programs (operated by private and public sector agencies), which target fatigue, mass limits and vehicle roadworthiness. However, it could be predicted that there will be an increase in the future, due to an expected doubling of the freight transport task by 2020.

Figure 1: Heavy commercial vehicle underrun fatalities between 1990-99

by type of heavy truck and passenger car collision

Source: FCD 1990-99

Front underrun collisions involving heavy commercial vehicles contribute to around 70-75 per cent of underrun fatalities. In the typical passenger car fatal offset front crash there are high levels of intrusion into the occupant space.  European research studies show that in 75 per cent of the cases, the usual occupant protection features built into cars such as seatbelts, airbags, energy absorbing steering columns and crush zones are not engaged.

Side underrun collisions involving heavy commercial vehicles contribute to around 15 per cent of fatalities. The collisions often occur at night but also during the day.  In Japan, Europe and some developing economies, because of the immense amount of bicycle and motorcycle traffic, heavy rigid and articulated commercial vehicles must have side Underrun Protection (UP).  This type of UP is targeted at protecting vulnerable road users or near parallel collisions with passenger vehicles (an typical example of this is on 4-lane highway where a long heavy commercial vehicle changes lanes while there is a passenger vehicle moving parallel within its blind spot).  However, it does not have the structural strength to engage the occupant protection systems of vehicles in a typical “T-bone” side underrun collision.

Rear underrun collisions involving heavy commercial vehicles contribute to around 10 per cent of underrun fatalities. These are a particularly severe crash type for a passenger car because the floor structure of most heavy vehicles is above the bonnet height of the car.  The car can run under this structure which may in turn penetrate through the car’s ‘A’ pillars and into the occupant compartment.  Again, the usual occupant protection features built into cars such as seatbelts, airbags, energy absorbing steering columns and crush zones are bypassed during these collisions.

The difference in traffic patterns around the world means that the value of fitting UP in Australia can not be assumed through the actions of other countries. However, it would be justifiable to draw from world research on the effectiveness of UP for particular road user types, and then combine this with Australian crash statistics.

In Australia, insufficient separation between traffic streams in rural areas has been a significant cause for heavy vehicle underruns. Table 2 shows that in case of articulated truck crashes involving underrun, passenger car occupant fatalities are higher in rural areas than urban areas, while for rigid trucks the fatalities are closer to being equally shared.

Table 2: Percentage of underrun fatalities by urban/rural location

|  | Rigid Truck | Articulated Truck |
| --- | --- | --- |
|  | Passenger Car occupant | Vulnerable Road user | Passenger Car occupant | Vulnerable Road user |
| Rural | 47% | 35% | 68% | 41% |
| Urban | 53% | 65% | 32% | 59% |

Source: FCD 1990-1999

Growth in freight transport task:

Fatalities from underrun crashes do not represent a large part of the crash population and are about 3-5 per cent of the total from all types of road user fatalities.  However, with the total freight transport task likely to double in the next 20 years, the role of articulated heavy commercial vehicles is likely to expand, as shown in Figure 2.  Rigid truck movements are likely to decline gradually, which will have a negative impact on sales of rigid trucks from around 2010.

Figure 2: Vehicle kilometres travelled by commercial vehicles: actual and projected

Source: BTRE Freight Measurement and Modelling

## Economic Cost of the Problem

Road crashes generally give rise to spill over costs which are spread across the parties involved in the crash, other road users and owners of public and private property.  Fatal injuries arising from crashes present a public health problem to Australian governments, as those involved initially draw scarce medical resources away from other uses, and a significant part of the cost of such resources falls on the public through the taxation system.  Those injured may suffer a loss in the quality of life and need access to disability services and facilities, which also pose a burden on the taxation and social welfare systems. Other costs to road users include extended travel time, which increases in heavily congested urban areas, and damage to vehicles and property.

These costs can be even more significant where the road crash involves an underrun type of collision with a heavy commercial vehicle. Fatalities and injuries can be expected to have a greater mean severity due to greater occupant space intrusion by the heavier vehicle, and the reduced (or non-) engagement of the lighter vehicle’s energy absorbing structures.

Operators of heavy commercial vehicles also suffer losses through deterioration of perishable product, as heavy commercial vehicles involved in the crash may need to wait for traffic police to investigate the crash.  In congested areas, overall heavy commercial vehicle movement may be severely limited leading to increased losses to road freight operators.

The annual economic cost of the problem in terms of heavy commercial vehicle underrun fatalities, serious and minor injuries was estimated for the period 1990-1999. The Australian Transport Safety Bureau (ATSB), who provided the base data, define heavy commercial vehicle underrun as “vehicles running underneath heavy rigid or articulated trucks. In the case of motorcycle and bicycles the rider must still be on the vehicle when it “ran” under the truck”.

Table 3 identifies the number and distribution of underrun crashes using 1990-1996 data and 2002 estimates, which Table 5 then further applies to 1990-1999 detailed data. The result is a summary of the annual cost of fatal, serious and minor injuries from front, rear and side underrun crashes between heavy commercial vehicles with a Gross Vehicle Mass (GVM) greater than 7.5 tonnes, passenger cars, motorcycles and bicycles. Costs for pedestrian trauma due to underrun were not available.

The costs (in 1995$) for a fatal, serious and minor injury are based on estimates prepared by the Bureau of Transport and Regional Economics and which are $1.5m, $0.325m and $0.010m respectively (BTE 2000). The average costs (in 1995$) of a fatal crash, serious crash and minor crash are $1.7m, $0.41m and $0.014m respectively (BTE 2000).  The difference in costs of a crash and an injury provides an estimate for the non-trauma cost which consists of property damage, heavy commercial vehicle immobility and traffic stoppages.  The estimated cost (in 2005$) of heavy commercial vehicle underrun trauma is $266 million and non-trauma is $71 million resulting in a total cost of $337 million.  This estimation may be conservative, due to under-estimating and under-reporting of underrun crashes.

Table 3: Estimate of  the type of heavy commercial vehicle under- run crashes involving a car or motorcycle or bicycle as function

of injury severity

| Rigid Heavy Commercial vehicles |
| --- |
| Injury | Front | Side | Rear | Total |
| Fatal | 15 | 4 | 1 | 20 |
| Serious | 104 | 24 | 10 | 136 |
| Minor | 237 | 56 | 22 | 313 |
| All injuries | 356 | 84 | 33 | 469 |
| Articulated Heavy Commercial vehicles |
| Injury | Front | Side | Rear | Total |
| Fatal | 22 | 4 | 1 | 27 |
| Serious | 151 | 28 | 9 | 190 |
| Minor | 350 | 66 | 22 | 437 |
| All injuries | 523 | 98 | 32 | 654 |
| All Heavy Commercial vehicles |
| Injury | Front | Side | Rear | Total |
| Fatal | 37 | 8 | 2 | 47 |
| Serious | 255 | 52 | 19 | 326 |
| Minor | 587 | 122 | 44 | 753 |
| All injuries | 880 | 183 | 66 | 1129 |

Source: FCD 1996-1999

Fatalities from FCD database, Serious injuries estimated from Haworth et al (2002)

and NSW, VIC and QLD databases, Minor injuries estimated from Haworth et al (2002)

Table 5: Estimate of the annual cost of heavy commercial vehicle underrun crashes

(a) Cost arising from underrun trauma  (personal injury only)

| Rigid Trucks |
| --- |
| Injury | Front | Side | Rear | Total |
| Fatal | $33,990,638 | $8,050,414 | $3,130,717 | $45,171,769 |
| Serious | $49,711,308 | $11,773,731 | $4,578,673 | $66,063,712 |
| Minor | $386,956 | $72,554 | $24,185 | $483,695 |
| All injuries | $84,088,902 | $19,896,699 | $7,733,575 | $111,719,176 |
| Articulated Trucks |
| Injury | Front | Side | Rear | Total |
| Fatal | $49,989,964 | $9,373,118 | $3,124,373 | $62,487,455 |
| Serious | $73,110,323 | $13,708,185 | $4,569,395 | $91,387,903 |
| Minor | $6,007,486 | $1,126,404 | $375,468 | $1,126,404 |
| All injuries | $129,107,773 | $24,207,707 | $8,069,236 | $155,001,762 |
| All Trucks |
| Injury | Front | Side | Rear | Total |
| Fatal | $83,980,602 | $17,423,533 | $6,255,089 | $107,659,224 |
| Serious | $122,821,631 | $25,481,916 | $9,148,068 | $157,451,615 |
| Minor | $6,394,442 | $1,198,958 | $399,653 | $1,610,098 |
| All injuries | $213,196,675 | $44,104,407 | $15,802,810 | $266,720,938 |

Source: FCD, NSW, Victoria and Queensland crash statistics

(b) Cost arising from other than underrun trauma (property damage, heavy commercial vehicle immobility etc only)

| Rigid Trucks |
| --- |
| Injury | Front | Side | Rear | Total |
| Fatal | $4,623,104 | $1,094,946 | $425,812 | $6,143,862 |
| Serious | $16,927,345 | $4,009,108 | $2,227,282 | $23,163,735 |
| Minor | $96,215 | $18,040 | $6,013 | $120,268 |
| All injuries | $21,646,664 | $5,122,094 | $2,659,1080 | $29,427,865 |
| Articulated Trucks |
| Injury | Front | Side | Rear | Total |
| Fatal | $6,799,190 | $1,274,848 | $424,949 | $8,498,988 |
| Serious | $24,895,012 | $4,667,815 | $1,555,938 | $31,118,765 |
| Minor | $560,149 | $375,468 | $1,126,404 | $2,062,021 |
| All injuries | $32,254,352 | $6,318,131 | $3,107,291 | $41,679,774 |
| All Trucks |
| Injury | Front | Side | Rear | Total |
| Fatal | $11,422,295 | $2,369,794 | $850,762 | $14,642,850 |
| Serious | $41,822,357 | $8,676,923 | $3,783,220 | $54,282,500 |
| Minor | $656,364 | $393,508 | $1,132,417 | $2,182,289 |
| All injuries | $53,901,015 | $11,440,225 | $5,766,399 | $71,107,639 |

## Types of underrun crashes and policy prescriptions

Underrun Protection (UP) will not prevent crashes but it will allow the crashworthiness features of the smaller vehicle to function in the event of an underrun collision.  Saving the lives of road users depends on the ∆V (closing speed) of the crash, size of the smaller vehicle and any occupant protection features available in the vehicle.

Table 6 illustrates the main types of underrun crashes in Australia, in reality a number of combinations are possible with impact areas on the heavy commercial vehicle ranging from front bumper bars, wheels, rear chassis rails, and side chassis rails.  An impact with the chassis rail may result in greater intrusion into the space of a passenger vehicle cabin.  In case of offset frontal, the smaller vehicle may tend to rotate away from the heavy commercial vehicle thereby reducing injury potential.  Table 6 also shows that most OECD countries have some form of mandatory UP, with the European Union leading the table in the mandatory provision for front, side, and rear UP devices for commercial vehicles with a GVM greater than 3.5 tonnes.

Table 6 : Types of underrun crashes and policy responses in some countries

|  | Effects in terms of Average deceleration | Vehicle based policy prescription recommended | Major countries or regions mandating policy prescriptions |
| --- | --- | --- | --- |
|  | 55 km/h | 70 km/h | 100 km/h |  |  |
| Car or commercial vehicle full frontal head on | 20g | 35g | 45g | Front UP device | EU, Japan, |
| Car or commercial vehicle offset frontal head on | 20g | 35g | 45g | Front UP device | EU, Japan |
| Car or commercial vehicle sideswipe impact | 12g | 15g | 20g | Side UP device | EU, Japan |
| Car to commercial vehicle side impact | 8g | 12g | NA | Side UP device | EU, Japan |
| Full rear impact car to commercial vehicle | 10g | NA | NA | Rear UP device | EU, US, Japan, Canada, China, India, Brazil |
| Offset rear impact car to commercial vehicle | 8g | NA | NA | Rear UP device | EU, US, Japan, Canada, China, India, Brazil |

Notes: Heavy vehicle GVM/GCM range used in the table is from 20 tonne to 62 tonne. With lower GVMs average decelerations will be lower. In all the above cases cabin intrusion occurs. In crashes where no underrun occurs average deceleration will range from 10g to 15g. The effects have been modelled based on test conditions aligned with ADRs 69 and 73. The EU has 25 member countries and the EU directives enjoy strong following in AGCC and Mercosur countries.

## Responding to the problem

Underrun crashes present an unusual situation for extracting costs for the provision of Underrun Protection (UP).  Heavy commercial vehicle operators in most situations would not derive a great deal of economic benefits from the provision of UP on their vehicles. Other road users, particularly passenger car occupants, would be the principal beneficiaries through reduction in the severity of injuries.  It is unlikely that existing market arrangements will be able to correct this externality and influence the provision of UP, as little direct benefits accrue to the provider of such systems. Although European heavy commercial vehicles supplied to the Australian market are provided with UP, this is only because of mandatory requirements in the European Union (EU) countries. While in some cases, the front UP is removed and replaced with a standard bumper-bar, it is uneconomic for other European heavy commercial vehicle wholesalers and importers to offer heavy commercial vehicles without front UP, as it forms part of the front fascia and includes footsteps and other functional devices.

As existing market arrangements are not likely to respond to the problem, government intervention of a non-regulatory or regulatory type may be needed. However, any intervention would have to demonstrate a net benefit to the community.

Currently, Australia only has Australian Design Rule (ADR) 42/04 – General Safety Requirements, Clause 8 Rear Bumpers for Semi-trailers, to respond to the underrun problem. This ADR is relevant to rear underrun crashes between semi-trailers and other road users. This contrasts with the European Union, Japan, United States, some Latin American and Asian countries that have had regulations in place for some time for side and rear UP and more recently for front UP.

In order to reduce fatalities and severity of injuries arising from heavy vehicle underrun crashes, the UP needs to address both dimensional and strength differences between the colliding vehicles.  Properly chosen dimensional requirements restrict underruns while strength requirements prevent the system from deflecting under the impact of forces arising from a collision. This prevents underruns and enables any crash protection features in both vehicles to protect occupants.

Any of the United Nations Economic Commission for Europe (UNECE) Regulations and corresponding European Economic Commission (EEC) Directives for front, side or rear UP used in the 25 member countries of the European Union, could potentially be adopted in Australia.  As these requirements are mandatory, all European heavy vehicle manufacturers design prime-movers, rigid trucks and trailers to meet them.

The key features of the Australian Design Rule (ADR), UNECE Regulations, EEC Directives, United States Federal Motor Vehicle Safety Standard (FMVSS) and other standards relevant to underrun are listed below:

- Front Underrun Protection Standards

- UNECE Regulation No. 93 – Front Underrun Protection

- EEC Directive 2000/40//EC – Motor vehicles with trailers – Front underrun protective devices.  This directive is aligned with the requirements of UNECE Regulation No. 93

- Side  Underrun Protection Standards

- UNECE Regulation No. 73 – Lateral protection of trailers and semi-trailer goods vehicles provides side underrun requirements

- EEC Directive 89/297/EEC – Motor vehicles with trailers – Rear  Underrun Protection devices. This directive is aligned with the requirements of UNECE Regulation No. 73

- Rear  Underrun Protection Standards

- ADR 42/04 – General Safety Requirements, Clause 8 Rear Bumpers for Semi-trailers

- UNECE Regulation No. 58 – Rear Underrun Protection

- EEC Directive 70/221/EEC – Motor vehicles with trailers – Rear  underrun protection devices. This directive is aligned with the requirements of UNECE Regulation No. 58

- FMVSS 223 – Rear impact guards, and FMVSS 224

- National Council of Traffic, Brazil, Regulation Number 152, October 2003 – Rear under ride guards for cargo vehicles.

The UNECE Regulation No. 93 (UNECE R 93) ECE requirements for Front Underrun Protection (FUP) can be met through fitment of a Front Underrun Protection Device (FUPD), or by utilising the vehicle structure as a FUPD.

The test that the front UP has to pass for certification consists of three static forces applied one at a time on the centre line of the front UP beam. 80 kN is applied in the centre, 160 kN at a point where the bracket connects the front UP to the chassis beam and finally 80 kN at the corner. Under these forces, there is a limit of 400 mm displacement allowed. The geometry requirements state that the lowermost part of the front UP beam must not exceed 400 mm from the ground and the beam height must not be below 120 mm.

The requirements were originally written with a collision speed of 56 km/h. However crash tests with standard European medium family size passenger car in 60 km/h revealed that the injury values of the car occupants were rather low (below HIC 200 - Head Injury Criteria has a limit value of 1000 for survival).  The requirements state that the front UP should be "stiff", but in tests an energy absorption of about 60 kJ in the commercial vehicle front compared to about 110 kJ in the passenger car front was observed in European tests.  Crash tests performed on smaller cars at 64 km/h have returned lower energy absorption and somewhat higher HIC values, still below the 1000 mark.

Table 7 summarizes the test loads for UNECE / EEC and United States front, side and rear UP.

Table 7: Test loads for UNECE and US Underrun Standards

| Test Load (kN) | ECE R 93/ 2000/40/EC Front UP | ECE R 73/ 89/297/EEC Side UP | ECE R 58/ 70/221/EEC Rear UP ** | USA FMVSS 223/224 Rear Impact Guard |
| --- | --- | --- | --- | --- |
| Outer edge P1 | 80 kN | 1 kN | 25 kN | 50 kN |
| Centre P3 | 80 kN |  | 25 kN | 50 kN |
| Off centre P2 | 160 kN |  | 100 kN | 100 kN |
| Allowed deflection | 400 mm | 30 mm in front of wheels, 300 mm elsewhere |  | 125 mm |
| Height | 400 mm | 550 mm | 550 mm | 560 mm |

Notes: *   These test loads apply to vehicles with a GVM >16t, for other vehicles lower values are permitted and are a function of vehicle GVM.

**  These test loads apply to vehicles with a GVM >20t, for other vehicles lower values are permitted and are a function of vehicle GVM.

Australian Design Rule (ADR) 42/04 – General Safety Requirements contains dimensional requirements but no test load requirements for rear bumpers for semi-trailers. Instead it requires that the rear cross member has at least the strength of steel tubing of 100mm diameter and 8mm wall thickness, and that an equivalent force path is available from the cross member to the main vehicle members.

## Economic Aspects of  Underrun Protection: Benefit-Cost Analysis

It is difficult to estimate many of the economic costs that  Underrun Protection (UP) would impose on the construction, operation and maintenance of heavy heavy commercial vehicles. A number of different factors have to be taken into account and their influence is complex to analyse.

## Costs for provision of Underrun Protection

Front Underrun Protection

General

The design of typical rigid front Underrun Protection (UP), including that designed to meet UNECE R93, is of traditional “brackets and beam” construction. Such a  system is primarily connected to the chassis beams, but also to foot-steps and lamp brackets.  Despite the range of available chassis heights, the front UP height should not deviate beyond certain limits. This in turn necessitates a flexible production system with a modular arrangement for the brackets. The product development phase would need a few person-years of work input, during which  it would be necessary to test the front UP according to the legislative requirement.

Generally, manufacturers need between 20 and 50 tests to develop a conforming prototype. Additionally, in the product/assembly verification phase, further testing would be needed. An estimate is that this entire activity would cost not more than $4 million. This would be amortized over 100,000 to 250,000 heavy commercial vehicles until a front end redesign was undertaken for the updated model.. Over and above development and engineering costs is the marginal production cost, which is more difficult to estimate. Material prices and manufacturing cost may range from $300 to $400 for each UP device. Aggregating development, material and production costs, the cost for rigid front UP, fitted to a new heavy commercial vehicle and complying with UNECE R 93, has been estimated at $440 per vehicle (See Appendix 6 for details). Other estimates have previously put this cost at from a low of $100-150 (Haworth 2002) to a high of $1000-4000 (NTC 2005). Although the former appears to represent manufacturing costs only, and the latter covers the costs of retrofitting to all vehicles, it would be prudent to include a sensitivity analysis on front UP cost as part of any benefit-cost analysis.

Cost due to added mass

The materials used in typical rigid front UP include a steel front UP beam and steel brackets, all of which is covered with styled plastics  This is the standard look for today’s heavy commercial vehicles. A number of metal alloys may be used, adapted to the strength requirements and production methods.  The added mass of the front UP can be 50-80 kg, depending on factors such as the chassis height and construction details.

This mass may be located three quarters of a metre in front of the front axle(s) for a typical bonneted vehicle and between a metre and a metre and a half for a typical cab-over vehicle. The cantilever effect of this mass about the front axle(s) could then give a total effect of up to 110 kg added to the front axle(s) (with a corresponding 30 kg reduction from the rear axle(s)). This total effect is based on a worst case of a cab-over design with wheelbase of about 4 metres and front overhang of about one and a half metres.

One potential issue with this additional load on the front axle(s) follows on from the state and territory 6 tonne steered axle limit. In Europe, steered axle limits vary from 10.5 tonnes in the UK to 13 tonnes in France.  The most  observed limit in countries of the European Union is 11.5 tonnes. The added mass on a vehicle’s front axle(s) from front UP,  as well as increases in mass in meeting the latest engine emission standard (Euro 4), may become a problem for European heavy commercial vehicle makers supplying in to Australia.

The National Transport Commission (NTC) have estimated that raising the steered axle limit by 500 kg (to 6.5 tonnes) would more than offset such effects, while still allowing for improvements in cabin strength. Whether the limit would or should be raised is beyond the scope of this RIS. However, the potential loss in productivity and higher running and maintenance costs due to the additional mass of UP should be considered as part of any benefit-cost analysis. An indicative assessment of this has been made later in this RIS.

Future developments in other safety devices, such as UP with energy absorbing systems and deflection zones, would likely lead to further increases in the mass of existing UP, Consideration of this is again beyond the scope of this RIS. Any future proposal to fit advanced UP would be assessed on its merits at the time.

Cost due to added length

Unless part of the vehicle structure, energy absorbing UP typically increases the length of a vehicle. Rigid UP typically does not. The rigid UP covered by UNECE R93 allows for a maximum longitudinal distortion of 400mm. This distortion may occur without involving the remainder of the front of the vehicle and so rigid UP may be mounted almost flush with the front of the vehicle. Therefore, there is no need to estimate a cost relating to legally available lengths of heavy commercial vehicles. An exception to this may be where a vehicle structure has not been originally built to accept UP and it has to be added on to the front in a similar way as a bull bar. Vehicle or bull bar manufacturers are asked to comment on this by way of the feedback forms at the start of this RIS.

Side Underrun Protection

The costs for rigid side Underrun Protection (UP) for a range of rigid heavy commercial vehicles and articulated heavy commercial vehicles depend on the vehicle length and so are variable. These are presented in

Table 8 (See Appendix 6 for details).  For rough purposes only, if the relative number of the different vehicle lengths in the fleet is taken in to account, an average cost of $847 would result (a more sophisticated calculation was used for the benefit-cost analysis). The material used for construction of the systems is generally aluminium, although steel may also be used.

Table 8: Cost of rigid side UP for rigid  heavy commercial vehicles and articulated heavy commercial vehicles

| Vehicle Type | Cost Side UP |
| --- | --- |
| 3 axle semi-trailer | $872 |
| 5 axle semi-trailer | $872 |
| 6 axle semi-trailer | $872 |
| 7 axle B-Double | $1,147 |
| 8 axle B-Double | $1,147 |
| 9 axle B-Double | $1,147 |
| Double Road Train | $1,675 |
| Triple Road Train | $2,455 |
| 2 axle rigid commercial vehicle | $574 |
| 3 axle rigid commercial vehicle | $574 |
| 4 axle Twin-Steer rigid commercial vehicle | $574 |
| 2 axle rigid commercial vehicle with 2 axle dog trailer | $872 |
| 3 axle rigid commercial vehicle with 3 axle dog trailer | $872 |
| Fleet average | $847 |

Source: VBG (component supplier), Sweden and Scania, Sweden

Rear Underrun Protection

Systems for rear Underrun Protection (UP) are available in simple, foldable and removable types. The cost of the simple type has been estimated at $773 vehicle (See Appendix 6 for details). The cost for foldable and removable types is high and the foldable versions can be twice that of a simple system.

Some alternative estimates for side and rear UP are shown in Table 10. The estimates include the variation in costs arising from the use of steel and aluminium and foldable and detachable types of rear UP.  This table has been included to again demonstrate the importance of including a sensitivity analysis on protection system cost as part of any benefit-cost analysis.

Table 10: Cost for rigid type UP to UNECE regulations or EEC Directives

| Front UP* (incremental cost over normal bumper bar) | $440 |
| --- | --- |
| Side UP** (for a 3 axle semi-trailer) | $1600 |
| Rear UP** (Aluminium beam) | $310# |
| Rear UP** (Steel beam) | $450# |
| Rear UP** (Mounting assembly fixed type) | $470 |
| Rear UP** (Mounting assembly detachable type) | $650 |
| Rear UP** (Mounting assembly foldable type) | $2300 |

*Supplied by commercial vehicle maker,

**Supplied by specialist manufacturer, adjusted for c.i.f. prices and industry profitability

## Costs and Benefits from installing UP under a variety of scenarios

Four scenarios were prepared for estimating the benefits from rigid UP, which meet UNECE Regulations. Table 12 describes the various types of scenarios in terms of device effectiveness rates used for estimating benefits.  As an example of how the table should be read, for front UP under Scenario A, 25 per cent of fatal injuries are converted to serious injuries and 35 per cent of serious injuries are converted to minor injuries. There are no benefits estimated for the conversion of minor injuries to no injuries and so the scenarios may be slightly conservative.

Each scenario consists of two levels; Level 0 and Level 1. This gives eight possibilities in all. Level 0 benefit estimates are for trauma (injury reduction) alone while Level 1 benefit estimates include trauma and non-trauma related items such as reduced level of property damage, mobility of the heavy commercial vehicle after the underrun crash.

Table 12:  UP device effectiveness rates for various scenarios

| Scenario A - Low | Front | Side | Rear |
| --- | --- | --- | --- |
| Fatal injury | 25% | 20% | 35% |
| Serious injury | 35% | 30% | 45% |
| Scenario B - Most Likely | Front | Side | Rear |
| Fatal injury | 30% | 25% | 39% |
| Serious injury | 39% | 36% | 50% |
| Scenario C - High | Front | Side | Rear |
| Fatal injury | 35% | 30% | 44% |
| Serious injury | 44% | 41% | 55% |
| Scenario D – Energy Absorbing | Front | Side | Rear |
| Fatal injury | 39% | 35% | 49% |
| Serious injury | 49% | 46% | 60% |

Source: Haworth (2002), Rechnitzer (1993), VC-COMPAT studies, Elvik.

Table 14 provides an estimate of the potential annual benefits available if UP were fitted to all heavy commercial vehicles in the fleet. The table suggests potential savings of up to $111 million for energy absorbing systems (Scenario D, Level 1).

Table 14: Expected annual benefits from provision of UP for various scenarios

(if fitted to entire fleet)

|  | Front Rigid Systems ($ million) | Energy Absorbing Systems ($ million) |
| --- | --- | --- |
| Level | Low (A) | Most Likely (B) | High (C) | (D) |
|  | Rigid | Artic | Rigid | Artic | Rigid | Artic | Rigid | Artic |
| 0 | 23 | 35 | 27 | 40 | 31 | 45 | 34 | 51 |
| 1 | 30 | 45 | 35 | 52 | 40 | 59 | 45 | 66 |

|  | Side Rigid Systems ($ million) | Energy Absorbing Systems ($ million) |
| --- | --- | --- |
| Level | Low (A) | Most Likely (B) | High (C) | (D) |
|  | Rigid | Artic | Rigid | Artic | Rigid | Artic | Rigid | Artic |
| 0 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 |
| 1 | 6 | 7 | 7 | 8 | 8 | 10 | 9 | 11 |

|  | Rear Rigid Systems ($ million) | Energy Absorbing Systems ($ million) |
| --- | --- | --- |
| Level | Low (A) | Most Likely (B) | High (C) | (D) |
|  | Rigid | Artic | Rigid | Artic | Rigid | Artic | Rigid | Artic |
| 0 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 |
| 1 | 4 | 3 | 4 | 4 | 5 | 4 | 5 | 5 |

In balancing these benefits with the costs of fitting UP, the timing of both benefits and costs becomes important. Fitting of safety devices to vehicles usually requires an initial outlay that then leads to a benefit over a period in the future. Further, if the safety devices are fitted only to new vehicles, this initial outlay is staggered. This RIS is concerned with fitment to new vehicles only. Therefore, the initial outlay for installation would see the benefits occur after a period and they would increase as more of the fleet is fitted with the device. This is covered in more detail in Appendix 5, which describes the methodology used for the benefit-cost analysis. Appendix 6 lists outputs from the four scenarios assumed for estimating benefits from UP.

Results

The end of Appendix 6 includes a summary of the outputs from the benefit-cost analysis. The summary lists Best Case, Likely Case and Worst Case scenarios for each device effectiveness. It was constructed by using the longest payback period (vehicle life), lowest discount rate, and inclusion of all the possible benefits for the Best Case, with the shortest payback period, highest discount rate, and exclusion of non-trauma related benefits for the Worst Case. The Likely Case used a 15 year payback period with a 7% discount rate and included non-trauma related benefits.

The summary was further reduced by grouping Scenarios A, B and C together and D separately (as D represents a different type of UP device – energy absorbing). Table 15 below shows the results of this.

Regarding rigid UP devices, Table 15 (a) demonstrates that there is a very strong case for the provision of front UP for articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM), with a Benefit-Cost  Ratio (BCR) well in excess of one for all cases. There is also a strong case for front UP for rigid heavy commercial vehicles greater than 7.5 tonnes GVM, with a BCR reasonably in excess of one for all cases.

Also, Table 15 (a) demonstrates that there is a weak case for the provision of side UP for articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM), with a Benefit-Cost Ratio (BCR) dropping below one for some cases. There is no case for side UP for rigid heavy commercial vehicles greater than 7.5 tonnes GVM, with a BCR always below one for all cases.

Finally, Table 15 (a) demonstrates that there is a weak case for the provision of rear UP for articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM), with a Benefit-Cost Ratio (BCR) dropping below one for some cases. There is no case for rear UP for rigid heavy commercial vehicles greater than 7.5 tonnes GVM, with a BCR always below one for all cases.

Regarding energy absorbing UP devices, Table 15 (b) demonstrates that there is a weak case for the provision of front energy absorbing UP for articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM), with a benefit-cost Ratio (BCR) dropping below one for some cases. There is no case for any other energy absorbing UP for rigid or articulated heavy commercial vehicles greater than 7.5 tonnes GVM, with a BCR always below one for these cases.

Table 15 (a): Summary of Benefit-Cost Ratios (BCR)  from the provision of UP on new heavy commercial vehicles – Scenarios A, B and C combined

|  | Front | Side | Rear |
| --- | --- | --- | --- |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 6.5 | 4.0 | 1.7 | 1.0 | 0.6 | 0.2 | 0.5 | 0.3 | 0.1 |
| Articulated | 39.2 | 24.0 | 10.1 | 2.8 | 1.7 | 0.7 | 1.7 | 1.1 | 0.5 |

Best case -   discount rate 4% over 25 years, high effectiveness device.

Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

Worst case - discount rate 12% over 10 years, low effectiveness device.

Table 15 (b): Summary of Benefit-Cost Ratios (BCR) from the provision of UP on new heavy commercial vehicles – Scenario D (Energy Absorbing UP)

|  | Front | Side | Rear |
| --- | --- | --- | --- |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 0.36 | 0.22 | 0.09 | 0.08 | 0.05 | 0.02 | 0.03 | 0.02 | 0.01 |
| Articulated | 1.66 | 1.15 | 0.56 | 0.12 | 0.08 | 0.04 | 0.07 | 0.05 | 0.02 |

Best case -   discount rate 4% over 25 years.

Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

Worst case - discount rate 12% over 10 years.

It is important to note here that both front and rear UP have been based on the cost and benefits of a heavy commercial vehicle – passenger car crash. By contrast, while side UP has used the accident data for all road users, the effectiveness and UP fitment cost has been based on  UP that is best suited to the protection of vulnerable road users only. If this is taken in to account the benefit-cost ratios for side UP may be even lower.

Discussion

The benefit-cost analysis found that there was a very strong case for the provision of rigid front Underrun Protection (UP) for both rigid and articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM) (some NB and all NC Australian Design Rule (ADR) category), but that there was little or no net benefit from the provision of side or rear UP.

The analysis was based on about 50 fatalities per year due to underrun with a heavy commercial vehicle (from a total of about 200 fatalities per year from all types of heavy commercial vehicle crashes). There were about 1100 crashes per year involving underrun with heavy commercial vehicle causing some sort of injury or fatality.  The number of serious and minor injuries were estimated to be similarly proportioned to the fatalities for front, rear and side underrun. Of the 1100 crashes, around 850 were with the front of the heavy commercial vehicle, 180 with the side and 70 with the rear. Although there are varying estimates, the cost of front UP per vehicle was roughly 30 per cent less than that of rear UP and side UP was the highest at about 10 per cent greater than rear UP (although the cost of side UP dropped below rear UP for shorter vehicles).

These figures combined to give a front UP benefit-cost ratio around twenty times greater than rear UP and at least five times greater than side UP. Within this, UP for articulated vehicles was around six times that for rigid vehicles.

Assumptions

A number of assumptions have had to be made in the benefit-cost Analysis. To keep it relevant, a broad range of scenarios and sensitivities were included.

The potential benefits were based on the identified cost of a passenger car crash and a fatality. An inquiry that found that heavy vehicle crashes cost 50% more than passenger car crashes was used to extend the non-trauma part of the crash cost by 50%. Although this assumption was thought to be reasonable, the analysis was done both with and without consideration of the estimated non-trauma cost. Refer Appendix 6.

The effectiveness of the devices under the various scenarios was based on a number of studies in England and Germany.  The Likely Case was based directly on the studies while the alternatives were estimated assuming a variation of +/- 5%. Refer Appendix 6.

A range of discount rates and payback periods were used. The discount rate for the Most Likely case was 7%, in line with similar studies. However, a rate of 4% (representing a low risk government rate) to 12% (representing the auto finance rate) was used for the alternatives. Also, the expected life of a commercial vehicle was estimated at 15 years but included a range from 10 years to 25 years. Refer Appendix 5.

There were no benefits estimated for the conversion of minor injuries to no injuries and so the scenarios may be slightly conservative. However, such conversions would be too difficult to estimate with any accuracy. It has been noted that other recent reports on underrun have not included such estimates.

Only the effectiveness of the side UP devices under the various scenarios included protection of vulnerable road users, as the information for other types of UP was not available. Although motorcyclists and bicyclists were not subsequently extracted from the road crash data for other types of UP (pedestrians were not reported), they represented a small proportion only of the total and so would have a limited affect on the results.

A fleet profile was used to adjust the contribution that each vehicle fitted with a safety device would provide towards the total benefit. This contribution was based on both the proportion of vehicles in the fleet of any particular age, and the tendency for vehicles of a particular age to be involved in road crashes. The assumption was made that the heavy commercial vehicle profile would not be different to the general fleet profile. This assumption was compared to the Most Likely scenario using an alternative method. The alternative method assumed that there was no fleet profile and that provided a vehicle was fitted with a safety device it contributed towards the total benefit in the same way as all other vehicles. Refer to Appendix 5.  It also costed side UP as an average value, proportioned only for whether a vehicle was rigid or articulated, rather than the more accurate method of calculating it for each different length of vehicle as was done in the fleet profile method. The Comparison of Benefit-Costs table in Appendix 6 shows that the two methods give similar results.

The slightly higher values of the fleet profile method are likely due to two reasons:

- The fleet profile method calculates the costs and benefits at the point where the composition of the fleet has steadied, that is the initial group of vehicles fitted with UP have reached the end of their lives and are exiting the fleet. From this point onwards the full benefits will be achieved each year. The alternative method also represents this point, however it is cumulative in that it has added the costs and benefits from the start of the period. Therefore, it also reports the later years within the period, when costs have been incurred but benefits are yet to be gained.

- a real-life increase in the fleet size over the past twenty years (4% moving to 6%) beyond that of a steady replacement rate (a constant 4% for rigid heavy commercial vehicles and 5% for articulated heavy commercial vehicles). An increase in fleet replacement rate leads to proportionately more new vehicles and hence faster introduction of any safety device.

The number of new heavy commercial vehicles being registered each year was reduced by 20 per cent to exclude European sourced vehicles. No cost for fitting UP has been assumed for these vehicles. Since 2003, European built heavy commercial vehicles supplied to the Australian market have been fitted with front UP. A small number of heavy commercial vehicles imported from Europe are fitted with side UP. For the purposes of this Regulation Impact Statement, it has been assumed that all European heavy commercial vehicles are fitted with front UP as there is a mandatory requirement in the European Union for front UP. While some of these systems may have been removed prior to supply to the Australian market, it has been assumed that they would be retained if Australia introduced a similar regulation. Therefore, no cost for fitting UP has been assumed for these vehicles.

Sensitivity to cost estimates

The cost of underrun systems was highlighted earlier on as showing some variation, depending on the source of the estimation. Therefore, the Benefit-Cost Ratios (BCRs) were tested for sensitivity to changes in these estimates. The Sensitivity of Benefit-Costs tables in Appendix 6 show that in the case of front UP, a cost increase of about $1000-1,500 per vehicle could be tolerated for rigid vehicles while still maintaining a positive benefit. Also, a cost increase of about $8,000-10,000 could be tolerated for articulated vehicles.

In the case of side UP, a cost reduction of about $400 per vehicle would be needed for rigid vehicles to reach a positive BCR. Also, a cost increase of about $400-700 could be tolerated for articulated vehicles.  In the case of rear UP, a cost reduction of about $500 per vehicle would be needed for rigid vehicles to reach a positive benefit. Also, a cost increase of about $0-150 could be tolerated for articulated vehicles.

While front UP on articulated vehicles were the only systems remaining comfortably within the range of estimations discussed earlier, front UP for rigid vehicles were also tolerant to variations in the cost of these systems. Both side and rear UP were marginal at best and would not be tolerant to changes in the estimates.

Sensitivity of extra load on the axle(s)

As discussed earlier in this RIS, the 6 tonne steered axle limit may limit the payload carried by a vehicle fitted with the added mass of a front UP.

The cost of this added mass is difficult to estimate, as it may also lead to more running and maintenance costs.  On the other hand, it is unlikely that the front axle(s) of all heavy commercial vehicles (particularly rigid) would always be at this 6 tonne limit when laden. This being the case, the addition of another 100 kg or so may not be an issue.

A basic (and extremely conservative) estimation was made of this cost, at least so that an order of magnitude could be identified (Refer to the Sensitivity of Extra Load on the Axle(s) – Cost of payload reduction where axle limits are not increased table, near the end of Appendix 6). A UP mass of 110 kg was subtracted from the estimated payload of different types of heavy commercial vehicles. An average percentage payload loss was calculated using the proportion of vehicles in the fleet and their relative distances travelled per year. This percentage loss was then multiplied by the annual revenue of the transport sector in 2002. Given that the final figure is in the order of $70m per year, it could be a significant cost. However, it is a cost that would need to be estimated using more accurate techniques, and then only if the 6 tonne limit is to be preserved by the states and territories.

Another check was then made using the assumption that the 6 tonne limit would be raised by at least 100 kg (Refer to the Sensitivity of Extra Load on the Axle(s) – Summary of Benefit-Costs where axle limits are increased by 100 kg table, near the end of Appendix 6).  The estimation was used to further test the case for front UP only, as side and rear UP ratios already had insufficient margin in their Benefit-Cost ratios to be viable options. It had recently been estimated (NTC 2006) that a typical articulated vehicle travelling 170,000 km per year and on standard tyres, would cause an additional $3545 of road damage per year if given a 500 kg increase in the front axle limit. This translates to a cost of $0.0041 per 100 kg per km per year.  This cost was deducted from the expected annual benefits of underrun protection, based on the annual distance travelled laden for both rigid and articulated trucks. The effect of this was to lower the Benefit-Cost ratios.  However, only the worst case scenario became marginal using this test. This was not considered sufficient to change the recommended outcome.  See Appendix 6 for details.

For the present, this RIS will assume that the limit will be raised by at least 100 kg and this assumption will form part of the conclusion.

# Objectives

The National Road Safety Strategy for the period 2001-2010 is the Australian government’s strategy for reducing road trauma.  The strategy aims to reduce the number of fatalities per 100,000 people by 40 per cent from 9.3 in 1999 to no more than 5.6 in 2010.  This is to be achieved both by maintaining existing measures which are found to be effective, and by introducing new measures based on strategic objectives.

Introducing an Australian Design Rule (ADR) for Underrun Protection (UP) for heavy commercial vehicles is a key measure in both the National Road Safety Action Plan for 2003 to 2004 (although it has not been carried through to the 2005/06 Plan) and the National Heavy Vehicle Safety Strategy 2001 to 2010 (ATC 2003, NTC 2004). The House of Representatives Standing Committee on Transport and Regional Services Inquiry on National Road Safety (Commonwealth Parliament, 2004) also reviewed the issue of underrun trauma and recommended an ADR be developed to mandate installation of UP devices on heavy commercial vehicles.  By implementing all the measures developed in successive action plans, there is an expectation that the annual number of fatalities per 100,000 people would reduce by 40%, from 9.3 in 1999 to no more than 5.6 in 2010. This would greatly benefit the Australian community as the cost of road crashes in 1995 $ was estimated at $15 billion or 2% of GDP.

The desired outcome of all Australian governments is to reduce the cost of all types of road trauma including underrun trauma.  In pursuit of this outcome and as mentioned frequently in the statement, the Australian Transport Council endorsed a National Road Safety Action Plan 2003 and 2004 and a National Heavy Vehicle Safety Action Plan 2003-2010 to develop and implement an in-vehicle based strategy to reduce the cost of underrun trauma by introducing an ADR for UP devices.  Other solutions available for reducing the cost of underrun trauma are not discussed as these involve driver and crash avoidance measures.

In case regulatory action is required for providing UP devices on heavy commercial vehicles, the Government needs to ensure that an ADR for UP devices is developed in accordance with the Council of Australian Government (COAG) Principles for National Standards Setting and clause 5 of the Competition Principles Agreement (COAG 2004) . The COAG principles require the assessment process for development of standards to be scientifically rigorous, taking into account public health and safety protection. Key features include analysis of the impact on competition, predictability of outcomes, consistency with international standards and practices, impact on international trade, flexibility of standards and adherence to the disciplines of regulation review. Clause 5 of the Competition Principles Agreement requires the Australian Government to demonstrate that proposed regulatory measures provide a net benefit to the community and are necessary to achieve the government’s vehicle safety objectives.

The specific objective of the Australian Government’s action in relation to underrun trauma is to reduce the aggressive nature of heavy commercial vehicles in collisions with passenger cars, motorcycles, bicycles and pedestrians and thereby reduce the cost of road trauma to the Australian community.  By developing and implementing performance requirements for UP, the severity of injuries to passenger car occupants and vulnerable road users reduces.

This Regulation Impact Statement so far has reviewed existing Australian government requirements for rear UP, fitted to semi-trailers; it has also identified the need for new requirements for reducing underrun trauma through the provision of UP.  The next stage is to identify and analyse options based on intervention or market based mechanisms.  The relative benefits and costs of proposed non-regulatory and regulatory measures require an impact assessment before any of them is recommended for implementation.

The Australian Government’s objective in relation to regulatory action such as the development and application of new ADRs is to ensure that design rules are relevant, cost effective and do not provide a barrier to the entry of safe vehicles and components. These objectives are also shared by the governments of Australian states and territories and the New Zealand government.

Eight principal requirements guide the Australian government’s action when developing and applying new ADRs. These are to ensure that the proposed standard or regulation:

- provides a net benefit to the community

- does not impose excessive requirements on business;

- is cost effective when implemented;

- does not discourage competition in the heavy commercial vehicle assembly and wholesaling sector as well as in the road freight transport industry.

- effectively addresses the community’s concerns in relation to impacts on occupant and public safety arising from the introduction of new automotive technology into transport markets;

- is consistent with international standards such as the UNECE Regulations.

- does not set unique Australian requirements and standards from other countries are pursued as an exception;

- does not breach WTO requirements and does not pose as a technical barrier to trade.

# Options

The options that were identified were guided by the benefit-cost analysis (discussed in Section 1), which found that there was a very strong case for the provision of front Underrun Protection (UP) for both rigid and articulated heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM) (some NB and all NC Australian Design Rule category), but that there was little or no net benefit from the provision of side or rear UP.

The options were explored in terms of non-regulatory and regulatory approaches.

Non-Regulatory approaches for Underrun Protection

Option 1: 	Self-Regulation (of front, side and rear Underrun Protection)

Industry may be able to self-regulate the provision of all Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes Gross Vehicle Mass (GVM).  This would include deleting the current regulation of rear UP for semi-trailers in Australian Design Rule 42/04 Rear Bumpers for Semi-trailers.

Option 2: National Heavy Vehicle Accreditation Scheme (NHVAS)

Accreditation Schemes offered by states and territory governments may be useful as an existing mechanism to encourage the introduction of and monitor the use of, front Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes GVM.

Option 3: Industry Code of Practice

A code of practice could provide voluntary guidance to transport operators on provision of front Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes GVM.

Option 4: Australian Standard

An Australian standard could set technical requirements for front Underrun Protection (UP) for heavy commercial vehicles on new heavy commercial vehicles greater than 7.5 tonnes GVM.

Option 5: State and Local Government Fleet Purchasing Arrangements

State and local governments could influence the provision of front Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes GVM, when they purchase the commercial vehicles that provide the services to their rate payers.

Regulatory Approaches for Underrun Protection

Option 6: 	Business-as-usual

The current regulatory position of only having rear Underrun Protection (UP) for semi-trailers in Australian Design Rule (ADR) 42/04 Rear Bumpers for Semi-trailers, could be maintained.

Option 7:  Australian Design Rule adopting front Underrun Protection regulations from Europe, Japan and United States

An ADR could mandate technical requirements for the provision of front Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes GVM, based on regulations applied in Europe, Japan and the United States.

Option 8:	Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes

An ADR could mandate technical requirements for the provision of front Underrun Protection (UP) on new heavy commercial vehicles greater than 7.5 tonnes GVM, based on intenational standard UNECE R93 Front Underrun Protection. This standard was developed by the Global Forum for Harmonising Automotive Technical Regulations, a forum sponsored by the United Nation’s Economic Commission for Europe (UNECE).

Options are assessed for application based on their feasibility in the following paragraphs.

## Option 1: Self-Regulation (of front, side and rear Underrun Protection)

Industry self-regulation can be effective where the heavy commercial vehicle assemblers and wholesalers/importers voluntarily agree to supply Underrun Protection (UP) on heavy commercial vehicles.

The Australian wholesale operations of some European manufacturers have recently commenced promoting commercial vehicles with front UP.  This is because of a spill over effect resulting from the imposition of mandatory requirements for UP in Europe.  The current volumes sold by the Australian agents of European manufacturers although not large are healthy, and while there may be a slight competitive disadvantage to European wholesalers, it has not reached a point where European wholesalers are likely to import product without front UP.  DaimlerChrysler, a leading supplier of European trucks to the Australian market, supply rigid trucks (ATECO range) fitted with side UP. Currently, penetration rate for European articulated truck prime movers is around 20 per cent while that for rigid trucks is around 12 per cent.

However, difficulties arise in the provision of safety equipment through self-regulation where a market is small and overcrowded market and where growth is volatile and competition intense. The effectiveness of any option, including self-regulation, depends on the extent to which it achieves the Australian governments’ objectives for reducing underrun trauma in the wider community.  In such a market, this objective is can not always shared by business where the primary focus must be on improving profitability.

The extent to which self-regulation is effective in simultaneously achieving the objectives of the wider community and business depends on the precise nature and extent of market failure and the general characteristics of the market.  In transport markets, the external (social) costs arising from market failure are borne predominantly not by transport equipment firms nor their customers, shareholders or financiers, but by the wider community (and mainly through all the three levels of Australian governments).  It is unrealistic to expect business to incur the costs associated with self-regulation, unless they can directly benefit from them.

In a highly competitive market, it is difficult to ensure that the administration and operation of self-regulation is transparent. Even a proposed independent self-regulatory authority would find it difficult to administer self-regulation, let alone impose sanctions on business (its own members) that breach self-regulation requirements.

The road freight transport industry currently does have self-regulation very much on the agenda. This is to be credited and a number of government studies have found that the long distance road transport industry has made a very significant contribution to the national economy, and demonstrated its capacity for competitiveness, innovation and efficiency.  However some aspects of concern to the community still remain and they include:

- Road safety issues: including the safety of vehicles, compliance with speed limits, controls on driver fatigue, intimidating driver behaviour, and the safety and security of loads;

- Urban amenity issues, including noise and exhaust emissions and control of heavy commercial vehicle routes;

- Road damage issues: including overloading and the inappropriate use of lightly constructed roads.

Leading on from these concerns, and with pressure from the government, the industry has developed some alternative compliance schemes.  Examples include; mass management scheme, maintenance management scheme and national driving hours. No studies are available on the effectiveness of these self-regulated schemes and the legal enforcement initiatives continue to operate through vehicle inspections for mass limits, road worthiness, fatigue and others. Overall, the industry would not be at the stage of being able to implement self-regulation on the fitment of major safety systems such as those for UP.

The self-regulation option includes the deletion of the current mandatory regulation for rear UP, ADR 42/04 requirements for rear bumper on semi-trailers.  ADR 42/04 prescribes requirements for a rear bumper on semi-trailers.  It does not provide any requirements for front or side UP.  It is only applicable to semi-trailers and so other types of heavy commercial vehicles are not required to have any similar systems.

It has been acknowledged widely in research that a bumper meeting ADR 42/04 requirements would not effectively protect road users from rear underrun trauma. This is due to both strength and geometric shortcomings. Firstly, the regulation does not specify any test to prove its strength.  Many of the rigid barriers on semi-trailers bend or twist easily if they inadvertently come in to contact with loading docks. Furthermore, in attempting to accommodate loading dock clearances, the geometric requirements have proven inadequate for underrun crashes.  Having a ground clearance of up to 600 mm results in a bumper that is too high off the ground to engage effectively with occupant protection systems in other vehicles. Being up to 300 mm short of the side of the vehicle the bumper would also allow a vehicle to pass under the corner of a semi-trailer with little or no resistance.

There is a strong case for withdrawing the bumper requirements in ADR 42/04. To maintain a regulatory requirement for rear UP, which imposes costs on road transport operators without any reduction in rear underrun trauma, could not be justified. There is also a strong case for not developing a replacement. The benefit-cost analysis in Section 1 demonstrated that even a high effectiveness  rear UP is unlikely to cover the initial costs of providing it.

## Option 2: National Heavy Vehicle Accreditation Scheme (NHVAS)

Accreditation schemes are good substitutes for law enforcement strategies when the patronage is high, private agents supervising the scheme are frequently audited for compliance and sanctions are maintained at levels that prevent non-compliance. The National Heavy Vehicle Accreditation Scheme attempts to ensure transport operators comply with the law by ensuring that their vehicles are roadworthy and loaded within the relevant mass limits. The Scheme is offered in two modules, one for mass management and second for maintenance. A third module has also been added for fatigue management. The Scheme requires operators to develop an in-house assurance system and document procedures and produce sets of documents that prove compliance. By complying with the scheme which is voluntary, operators are not subject to frequent stops and checks at the road side. The Scheme operates in all three eastern seaboard states and covers commercial vehicles whose GVM exceeds 4.5 tonnes. In Victoria of the 50,000 rigid and articulated trucks with GVM exceeding 12 tonnes, only 120 transport operators comprising of 1000 drivers/vehicles were registered with the mass management scheme. This represents about 2 per cent of the drivers/vehicles. No information was available for the maintenance management scheme.

With low patronage, accreditation schemes are unable to guarantee the high field application rate of a design rule that regulatory arrangements offer. Moreover, the lack of uniform application across the fleet can produce competitive disadvantage to those accredited to a scheme.

## Option 3: Industry Code of Practice

Codes of practice are neither mandatory nor carry the force of the law.  A code of practice for Underrun Protection (UP) could set out guidelines on what constitutes industry practice.  The code would establish a common standard and expectations between different players. The Truck Safe program managed by the Australian Trucking Association is an example of an industry initiated safety accreditation scheme. Industry standards are established for four areas: health, vehicle maintenance, management and training. Operators must meet the standards set in these four areas for accreditation, be audited by an external auditor, and reviewed and accepted or rejected by an accreditation council. To date over six hundred transport companies have achieved safe accreditation. The program has been recognised as an excellent initiative and has helped operators improve their long-term viability.  However, MMI Insurance in their submission to the House of Representatives Standing Committee on Communication, Transport and Arts inquiry into managing fatigue stated that:

“Truck Safe operators are not better risks than any other group of operators; some are in fact the highest risk operators in the industry with the worst accident records to date.”

MMI Insurance felt that the key problem is that the Truck Safe audit process does not audit many aspects of road transport law such as driving hours, driver schedules and vehicle compliance. If vehicle compliance could be included in Truck Safe, then it may also be able to include the provision of UP.  Industry codes of practice are only effective if they are recognized and accepted by all concerned and if there are some rewards for complying and sanctions for non-compliance.  Accordingly, industry and government needs to pay close attention to establishing suitable incentives for compliance so as not to diminish the effectiveness of a code of practice. Currently there are an estimated 47,000 businesses operating in the hire and reward part of  the road freight industry, 98.5 per cent of which are in road freight operations and the remainder which are in the road freight forwarding sector. According to NTC estimates, there are 210,000 trucking establishments in existence of which 21 per cent belonged to the hire and reward sector and 79 per cent to the ancillary sector. It appears that Truck Safe coverage of the hire and reward segment of the road freight industry is below 10 per cent, and as such it may not be able to guarantee a high field application rate.

In an effort to reduce collisions between heavy commercial vehicles and motorists resulting from the heavy vehicle not being seen by a motorist, particularly in poor weather conditions or hours of darkness, the Australian Trucking Association (ATA) introduced a code of practice for improving the visibility of heavy commercial vehicles. The Australian Heavy Vehicle Visibility Code of Practice is voluntary, sets guidelines for operators wishing to take advantage of the added safety of high visibility markings, and provides recommendations for the use of retro reflective graphics. It is based on UN/ECE Regulation 104 - Uniform Provisions Concerning the approval of Retro Reflective Markings for Heavy Vehicles and their Trailers. As a voluntary code of practice it cannot guarantee a high field application rate and enforce negative sanctions for non-compliance. As such this option is unable to meet the net benefit test and hence it will not be analysed for impacts on affected parties. The extent of coverage of the visibility code of practice across heavy commercial vehicle establishments is unknown at this stage and it would be useful if the ATA could advise the Department on the extent of coverage.

## Option 4: Australian Standard

Standards Australia International Ltd (SAI) is a publicly listed company that develops and publishes documents setting out technical specifications or other criteria necessary to ensure that a device will perform as expected.  As SAI is a non-government organization, the standards it promulgates are voluntary unless they are specifically incorporated into regulatory frameworks by governments.  These standards are usually well-founded and comprehensive and so incorporation is not uncommon. Australian Design Rule 62/01 - Mechanical Connections between Vehicles incorporates a number of Australian Standards which include; AS 2213, AS 2175, AS 4235, AS 4177 and several others.  SAI is a member of the International Organization for Standardization (ISO), and contributes to the development of and promotes compliance with international standards developed by the ISO.  There are currently about 122,000 Australian Standards in operation.

While there is scope for making use of an Australian Standard for provision of  Underrun Protection (UP) for heavy commercial vehicles, no standard on UP is currently available.  Developing Australian Standards with requirements specific for Australia would impose additional costs, especially for European sourced heavy commercial vehicles, as these are already compliant with UNECE R 93.  The availability of UNECE R 93 for front UP makes this option redundant and so it will not be reviewed for impact analysis in Section 4.

## Option 5: State and Local Government Fleet Purchasing Arrangements

State and local governments purchase a considerable number of commercial vehicles to provide services to their rate payers. As such they are in a position to influence the configuration of heavy commercial vehicles entering their fleets. By insisting on the installation of Underrun Protection (UP) in their heavy commercial vehicles, governments would be introducing these in to the general fleet through resale, and setting a benchmark for others to follow. Currently, state and local governments purchase around 10 per cent of commercial vehicles and dedicated sub-contractors purchase another 10 per cent. Most of these are rigid vehicles. If government purchasing managers could influence the installation of UP, the uptake of front, rear and side UP could be more rapid that that which could be achieved through vehicle design rules, although what the final proportion in the fleet would be is not clear.

## Option 6: Business-as-usual

The current situation would remain unchanged and so there would not be any new regulations introduced nor any existing regulations removed. The only regulated Underrun Protection (UP) would be a rear bumper for semi-trailers as currently required by Australian Design Rule (ADR) 42/04 General Safety Requirements.

## Option 7: Australian Design Rule adopting front Underrun Protection regulations from Europe, Japan and United States

Only the European Union and the UNECE have front Underrun Protection (UP). Japan and the United States do not have any specific requirements for front UP. As Japan is a signatory to the 1958 Agreement, it is most likely to apply UNECE R 93 in the near future.  Japan, United States and Canada mandate the provision of side and rear UP.  As the provision of side and rear UP was demonstrated earlier to not provide any net benefits to the community, this option will not be assessed any further.

## Option 8: Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes

UNECE R 93 Front Underrun Protection (UP), is the relevant regulation for application to front underrun crashes involving heavy commercial vehicles. The regulation is annexed as a part of the 1958 Agreement and its requirements are available for application as an Australian Design Rule. This option meets the Australian government’s objective of adopting international standards for the construction of motor vehicles and trailers. A copy of the regulation is attached at Appendix 9.

The VC- COMPAT program, a European Union safety initiative under the EU Frame Works Research Program, is currently reviewing Regulation No. 93 and technical requirements from the research program are expected to be available in 2006.

# Impact Analysis

### Background to the Heavy Commercial Vehicle Industry

The heavy commercial vehicle industry in Australia is made up of heavy commercial vehicle assemblers, importers, and sub-assembly suppliers. Industry revenue for 2003-04 was nearly $15 billion, while for trailers it is estimated at $2 billion.

Locally built heavy commercial vehicles account for around 16 per cent of the total number retailed in 2003 with the remainder mainly from Japan and Europe.  The European Union is a key supplier of prime movers along with Australian made heavy commercial vehicles such as Kenworth, Mack and International. The industry displays a high level of globalization.  However, trailers from Japan, Europe and the USA are rarely supplied to the Australian market.

In Australia, there are five main operating classes of heavy commercial vehicles. These are:

- Rigid commercial vehicles

- Rigid commercial vehicles with trailers

- Semi-trailers

- B-Doubles

- Road trains

More detailed information regarding the industry and types of vehicles can be found at Appendix 2.

## The Affected Parties

Parties directly affected by the proposed standard are:

- Rigid and articulated heavy commercial vehicle manufacturers and importers; trailer manufacturers;

- Sub-contractors designing and supplying components used in the manufacture of rigid heavy commercial vehicles, prime movers and trailers;

- Consultants providing vehicle certification and compliance services to heavy commercial vehicle manufacturers, trailer manufacturers and road freight operators;

- State and territory transport agencies performing a regulatory, review or oversight function; and

- Road freight operators;

A detailed table listing all affected parties is provided in Appendix 7.  Several interest groups represent the affected parties and these include:

- Heavy commercial vehicle assemblers and importers are represented by the Truck Industry Council   The sector comprises heavy vehicle assemblers, heavy vehicle importers and component manufacturers/importers;

- Suppliers of trailer components are represented by the Australian Road Transport Suppliers Association;

- Suppliers of vehicle certification, design and testing services are represented by the Commercial Vehicle Industry Association of Australia;

- Heavy commercial vehicle distributors are represented by the Motor Traders Association of Australia ;

- Motorist clubs (membership drawn from passenger car owners) are represented by the Australian Automobile Association;

- Heavy commercial vehicle owners/operators are represented by the Australian Trucking Association;

- Motorcycle owners are represented by the Australian Motorcycle Council;

- Bicycle owners are represented by the Bicycle Federation of Australia;

- Pedestrians are represented by the Pedestrian Council of Australia;

- Insurance providers are represented by the Australian Transport Insurers Association;

- Other interest groups operating largely in the after market, are represented by the Australian Automobile After-market Association.

## Impact on Existing Regulations

The only current requirement in the Australian Design Rules for heavy commercial vehicles is for a rear Underrun Protection (UP) for semi-trailers in Australian Design Rule 42/04 Rear Bumpers for Semi-trailers. The retention of this standard has been discussed later in this RIS.

The introduction of any effective UP requirements would increase the effectiveness of current crashworthiness regulations for other vehicles.

### Impact of the options

## Option 1: Self-Regulation (of front, side and rear Underrun Protection)

### Likely Benefits

### Governments

##### Australian

In removing the current mandatory requirement in ADR 42/04 for fitting a rear bumper for semi-trailers (rear Underrun Protection (UP)), there would be a small benefit in no longer having to administer it. This benefit has not been estimated.

##### State/Territory/Local

By encouraging the fitment of UP devices through self-regulation, the costs of medical treatment and hospitalizations are likely to reduce following a decrease in underrun trauma. The estimated savings are approximately $7.9m per year, based on an assumed 15 per cent voluntary take up of UP.

### Industry

By encouraging the fitment of UP through self-regulation, European manufacturers may find that they have a competitive advantage over manufacturers from other countries.  This is because they would have had experience in designing and manufacturing UP. However, because Australia relies on overseas heavy commercial vehicle manufacturers for over 90 per cent of its transport equipment requirements, self-regulation may also introduce varying requirements across the fleet with some standards (including in-house) being less effective or untried. If this were to happen, all heavy commercial vehicle makers may find it difficult to sell product in to a confused or sceptical market. This benefit has not been estimated.

In case of trailers, local manufacturers are able to satisfy demand and so overseas manufacturers do not have any presence in the Australian market. In removing the requirements in ADR 42/04 for fitting a rear bumper for semi-trailers, there would be a small benefit to manufacturers in no longer having to design, manufacture and certify the bumpers. This benefit has not been estimated.

### Consumers

Installation of front UP would on average reduce downtime and liabilities for heavy commercial vehicle operators (through less trauma from road crashes). There would also be reductions in road trauma which may lead to reductions in insurance premiums for all road users. This benefit has not been directed estimated but would form part of the benefit attributed to State/Territory and Local government.

### Likely Costs

### Government

##### Australian/State/Territory/Local Governments

In removing the requirements in ADR 42/04 for fitting a rear bumper for semi-trailers, there would be no cost (in terms of a loss of a benefit) to road trauma reduction. This follows on from the argument earlier that these rear bumper requirements are ineffectual.

The Australian government may need to work with industry to identify appropriate voluntary specifications for underrun systems. This would assist in achieving the government’s objective of reducing the cost of heavy vehicle underrun trauma.  The government may also have to put systems in place to monitor the take-up of these voluntary specifications.  The cost to do this has not been estimated.

Costs may accrue to states and territories as part of the effort towards monitoring the take-up of UP for heavy commercial vehicles as well as underrun trauma costs. These costs have not been estimated.

### Business/Consumers

In encouraging the fitment of UP through self-regulation, manufacturers who are not European may find that they have a competitive disadvantage against manufacturers from Europe. These costs have not been estimated.

There would be additional costs to heavy commercial vehicle suppliers and trailer manufacturers for designing, manufacturing and installing UP. These costs may be passed on to the consumer. The estimated costs are approximately $3.4m per year, based on an assumed 15 per cent voluntary take up of UP. These may be passed on to road transport operators.

Distributional Effects

The benefits from Option 1 would be gained by the community in the reduction of road trauma and road transport operators in the reduction of downtime and liabilities. Industry and government may gain slightly on reduced certification costs and some parts of industry may gain some competitive advantage in being able to supply UP more efficiently that their competitors.

The costs from Option 1 would be incurred by business in the increase costs of supplying UP. These costs may be passed on the consumer. Industry and government may also incur some costs on facilitating and monitoring any voluntary arrangements.

Discussion and Conclusion for Option 1

Option 1 estimated that if industry is encouraged to fit front, side and rear UP through self-regulation, the benefit/cost ratio would be positive with a net return of about $4.5m per year.

However, this option would be unlikely to achieve fully the government’s primary objective of reducing costs from road trauma, and particularly those of the National Road Safety and the National Heavy Vehicle Safety Strategies. Although the benefits and costs were calculated on an assumed take up rate of 15 percent, the option would be voluntary and so in fact there would be no guarantee that UP would be fitted to any heavy commercial vehicles.

This is partly due to an environment where profits are shrinking (profit margins are around 4 per cent), competition is increasing, growth of road freight is slowing and more commercial vehicles are running empty. Operators would be looking for savings to sustain their businesses and in the main would only install equipment which is essential for meeting regulatory requirements. In addition, provision of front UP may add some extra mass to the vehicle and this may impact on operator revenue. This impact may be limited but in a highly competitive industry it may have some negative effect.  These are key factors which would determine the field effectiveness of self-regulation as a measure for providing UP.

The response of heavy commercial vehicle makers who are facing shrinking profits may be to discontinue the provision of UP. The supply of heavy commercial vehicles complying with a (say) code of practice would be a cost to road freight transport operators if their trade association or consignors insist on operating heavy commercial vehicles with UP. Although it is expected that on average there would be a reduction of downtime and liabilities for heavy commercial vehicle operators (through less trauma from road crashes) to offset this cost, this benefit would not be obvious to freight transport operators in the short term.

Table 16 provides a summary of the benefits and costs of Option 1.

Table 16:  Costs and Benefits : Option 1- Self –Regulation (of front, side and rear Underrun Protection (UP))

|  | BENEFITS | COSTS |
| --- | --- | --- |
|  | Description | Estimate | Description | Estimate |
| Business | Increased competitive advantage for some (15%) heavy commercial vehicle manufacturers meeting market demand for UP Reduced design, manufacturing and certification costs for trailer manufacturers not required to fit ADR compliant rear bumpers for semi-trailers (deletion of requirement in ADR 42/04) | unable to estimate unable to estimate | Decreased competitive advantage for some (85%) heavy commercial vehicle manufacturers not meeting market demand for UP Increased design, material and manufacturing costs for some Australian, Japanese manufacturers for choosing to meet market demand for UP . These may be passed on to road transport operators | unable to estimate $3.4m |
| Consumers | Reduced road trauma for all road users Reduced insurance premiums for all road users Reduced downtime and liabilities for heavy commercial vehicle operators | $7.9m unable to estimate |  |  |
| Government | Reduced need for public resources such as emergency services etc Reduced certification costs for not administering the approval and maintenance of ADR compliant rear bumpers for semi-trailers |  | Increased costs to assist industry with voluntary specifications for UP and monitoring application rates. | unable to estimate |

## Options 2&3: National Heavy Vehicle Accreditation Scheme / Industry Code of Practice

Options 2 and 3 were similar to self-regulation as they are voluntary and have low application rates across the national heavy vehicle fleet. The benefits would also be similar while costs can be substantially higher, as they would require operators to maintain an in-house assurance system, undergo independent audits from time to time and subscribe periodically to the membership of a scheme or program. Although Option 2 would be a cost effective substitute for enforcement, the patronage would be too low for it to be an effective altenative to regulation.  Neither Option 2 or Option 3 were considered any further.

## Option 4: Australian Standard

The impacts of Option 4 on affected parties such as governments, industry and consumers were similar to that discussed for Option 1.

## Option 5: State and local government fleet purchasing arrangements

The impacts of Option 5 on affected parties such as governments, industry and consumers were similar to that discussed for Option 1.

However, all the benefits would be slightly increased and the costs slightly increased (because the benefit-cost ratio would remain the same, a higher net benefit would result).  This is because in addition to the self-regulation forces that lead to the assumed 15% application rate of (the percentage of newly registered heavy commercial vehicles that fit) Underrun Protection (UP), there would be an added requirement to fit such systems to any heavy commercial vehicle purchased by the government. The absolute change in benefits and costs has not been estimated.

Discussion and Conclusion for Option 5:

Option 5 has a good potential for partly achieving the objectives set out in the National Road Safety Strategy as state and local governments acquire over 20 per cent of heavy commercial vehicles registered annually.  As state and local governments retire their vehicles once in three years, the net benefit could rise as relatively recent vehicles retired from government fleets replace older heavy commercial vehicles in the national fleet. Unfortunately, there are very few prime movers purchased by governments so this benefit would only apply to rigid trucks.

The risk of losing, or not getting, government contracts could motivate assemblers and importers to provide UP on their rigid trucks. However, there would be little effect in the prime mover market.

## Option 6: Business-as-usual

With this option, there would be no change in the regulatory and non-regulatory environment and so costs and benefits would remain the same. In relative terms these would be zero as it is the baseline against which the other options have been measured.

## Option 7: Australian Design Rule adopting front Underrun Protection requirements from other countries

This option was discounted earlier in the RIS in the Options section.

## Option 8: Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes

### Likely Benefits

### Governments

##### Australian

None.

##### State/Territory and Local government

By mandating the fitment of front Underrun Protection (UP) to new heavy commercial vehicles with a GVM greater than 7.5 tonnes, the costs of medical treatment and hospitalizations would be likely to reduce following a decrease in underrun trauma. The estimated savings were approximately $41.7m per year.

Business

None.

Consumers

Installation of front UP would on average reduce downtime and liabilities for heavy commercial vehicle operators (through less trauma from road crashes). There would also be reductions in road trauma which may lead to reductions in insurance premiums for all road users. This benefit has not been directed estimated but would form part of the benefit attributed to State/Territory and Local government.

### Likely Costs

### Government

##### Australian

The Australian Government operates and maintains the road vehicle certification system, which is used to ensure that vehicles first supplied to the market comply with the Australian Design Rules. There are costs incurred in operating this service. A cost recovery model is used and so these costs are recovered from business. There would be costs attributed to the addition of a new design rule for UP to the current certification system. These costs have not been estimated.

State/Territory/Local Governments

Costs may accrue to states and territories as part of the effort towards monitoring the continued compliance of front UP for heavy commercial vehicles to in-service requirements. These costs have not been estimated.

##### Business

##### Large enterprises

There would be adjustment costs to heavy commercial vehicle suppliers for installing front UP devices. While European heavy commercial vehicle makers may enjoy some commercial advantage, non-European heavy commercial vehicle makers, including three domestic firms, would need time to design, test and manufacture front UP. The cost of heavy commercial vehicles manufactured by non-European and domestic firms would need to include a premium to cover the cost of product development and testing to the mandatory standard. These costs have been estimated at $5.2m per year. These may be passed on to road transport operators.

##### Small and medium enterprises

The segment of the industry that manufactures bull bars for new (and possibly in-service) heavy commercial vehicles would need to modify their designs and carry out testing to the new vehicle requirements for front UP. UNECE R93, the proposed regulation, allows for the design and testing of devices as distinct components of heavy commercial vehicles. Potential changes to bull bar manufacturing would likely be an important issue to those involved. These costs have not been estimated. However, a copy of UNECE R93 has been attached at Appendix 9. This segment of the industry in particular is invited to provide any costs, through the comment forms at the beginning of this RIS.

### Consumers

Industry may pass on the costs of front UP devices to road transport operators. However, this would not be a certainty given the low relative percentage of a typical vehicle cost (around 0.5 per cent) and the intensity of competition.

Distributional effects

The benefits from Option 8 would be gained by the community in the reduction of road trauma and road transport operators in the reduction of downtime and liabilities.

The costs from Option 8 would be incurred by business in the increase costs of supplying  front UP. These costs may be passed on the consumer. Government would also incur some costs on administering the regulations, although these would be recovered from business because of the cost recovery  model being used.

Discussion and Conclusion on Option 8:

Option 8 estimates that if industry is required to fit front UP to new heavy commercial vehicles with a GVM greater than 7.5 tonnes, the benefit/cost ratio would be positive with a net return of about $36.5m per year.  This is about $32m greater than Option 1.

This option would enable the Australian government to implement a key element of the National Road Safety Action Plan 2003 to 2004 and the National Heavy Vehicle Safety Strategy 2003-2010.

Adopting UNECE requirements for front UP would facilitate market access to efficient and competitive suppliers of front UP. The option would allow transport operators to have a choice of suppliers and access to superior state-of-the-art transport safety technology. The community would be able to reduce the cost of underrun trauma efficiently while the Australian government would be able to provide administrative arrangements for compliance assurance at a cost far lower than Option 5 and also participate in a global forum for any future development of UP standards.

Table 17 provides a summary of the benefits and costs of  Option 8 along with the net benefits.

Table 17: Benefits and Costs: Option 8- Australian Design Rule adopting  international standard UNECE R 93 for front Underrun Protection (UP) for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes

|  | BENEFITS | COSTS |
| --- | --- | --- |
|  | Description | Estimate | Description | Estimate |
| Business | None |  | Increased design, material and manufacturing costs for (80%) Australian, Japanese manufacturers previously not building heavy commercial vehicles meeting front UP regulations . These may be passed on to road transport operators Increased design, material and manufacturing costs for those involved in bull-bar manufacture. These may be passed on to road transport operators | $5.2m unable to estimate |
| Consumers | Reduced road trauma for all road users Reduced insurance premiums for all road users Reduced downtime and liabilities for heavy commercial vehicle operators | $41.7m |  |  |
| Government | Reduced need for public resources such as emergency services etc |  | Increased costs to administer mandatory regulations for front UP | unable to estimate |

Summary of Impact Analysis

The impacts of Options 1, 4, 5, 6 and 8 on affected parties have been discussed above.

The impact analysis indicated that Option 8 would be the most efficient and effective option, that is to mandate the provision of front UP for rigid and articulated trucks with a GVM greater than 7.5 tonnes by applying an international standard.

In general terms, the benefit-cost ratios would be a value greater than one for a package of front, side and rear UP being fitted to rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes. However, as discussed earlier in this RIS, side and rear UP by themselves would have a benefit-cost ratio of less than one and so would rely on high ratios generated by front UP to raise the whole package to above one. Therefore, the ratios would always increase by adopting front UP only.

For the same fitment option (front, side, rear or any combination of UP), the benefit-cost ratios would be similar whether these were voluntary or mandated. Although there would be different costs associated with the method of implementation, these tend to be dominated by the design, manufacturing and installation costs of the UP.

However, the net benefits would increase with a higher field application rate.  This is why mandatory fitment would yield the highest net benefits.

The majority of costs are borne by the vehicle manufacturers, which may then be passed on to the operator and the consumer. The majority of benefits would be received by the community in terms of reduced road trauma.

Option 1 benefits would not reach their full potential, due to the high element of uncertainty in generating sufficient field effectiveness.  This arises out of the fragmented nature of the road freight industry. Options 4 and 5 would get closer, although Option 5 would have no additional effect for articulated vehicles. Option 6 was the baseline and so does not generate any benefits nor incur any costs in relation to the other options. Option 8 would allow the benefits to reach their maximum potential (for new vehicles) and so meet the Australian and state governments’ objectives to reduce underrun trauma

# Consultation

The Department has had preliminary consultations with the Technical Liaison Group (members include representatives of peak industry associations, state and territory governments and motoring clubs), prior to seeking public comment. The Department undertakes public consultation on behalf of the Minister for Transport and Regional Services. Under Part 2, section 8 of the Motor Vehicle Standards Act 1989 the Minister may consult with state and territory agencies responsible for road safety, organizations and persons involved in the road vehicle industry and organizations representing road vehicle users before determining a design rule.

Public consultation

The issue of an Exposure Draft for public consultation is an integral part of the Department’s due process for developing new vehicle design rules as it initiates the most extensive and interactive phase of making national standards. Publication of the proposal provides an opportunity for business and road user communities, as well as all other interested parties to respond to the proposal by writing or otherwise submitting their comments to the Department. Providing proposals with a RIS assists all stakeholders to identify more precisely the impacts of the proposals and enables more informed debate on the issues.

Following the end of the public consultation period, all responses will be collated and considered by the Department in determining what is to be included in the revised proposal for providing Front UP on heavy commercial vehicles with GVM greater than 7.5 tonnes. A discussion of the major points raised by respondents and the Department’s response to those points will be included with the revised proposal in a submission made to the Australian Transport Council.

Response from affected parties

The statement is being distributed for consideration by interested parties: - industry participants, consumer representatives, state and territory transport agencies.

# Conclusion and Recommended Option

The provision of Underrun Protection (UP) by self-regulation, as outlined in Option 1, could be a low cost option and yet unlikely to generate the high application rate for new vehicles if underrun trauma is to reduce significantly. The difficulty in achieving a high penetration rate with self-regulation is three-fold.  Firstly, there is a high level of competition in the industry. The low profit margins means that operators are forced to cut costs continuously to service debt and other operating costs which keep rising (eg fuel).  Secondly, the market power of consignors is considerable, and this also forces operators to operate at these very low margins.  These factors have led to financial distress for some operators, with constant consolidation of the industry. This stress may play a part in reports of repeated violations of regulatory arrangements by a very small section of the industry. Thirdly, while the costs of the option would be borne in the main by the vehicle manufacturer, and subsequently passed on the the operator and consumer, a significant portion of the benefits would be received by the wider community instead.

Given the environment in which the road transport freight industry operates, heavy commercial vehicle and trailer suppliers are likely to succumb to commercial pressures in a self-regulated environment.

However, there is a strong case for withdrawing the bumper requirements in ADR 42/04, without mandating replacement rear UP  Although the design requirements have been considered inadequate, the benefit-cost analysis in Section 1 demonstrated that even high effectiveness rear UP is unlikely to cover the initial costs of providing it.

The use of an such as the National Heavy Vehicle Accreditation Scheme (NHVAS) or similar, as outlined in Option 2, involved the use of an accreditation scheme to promote the installation of front UP.  As the patronage of the NHVAS is very low (about 2- 5 per cent) among heavy vehicle operators, it is likely to lack the ability to have the high application rate which would be required to reduce underrun trauma significantly.

The use of an industry code of practice, as outlined in Option 3, would also be unable to provide the high application rate required for reduction in underrun trauma owing to the reasons outlined for Options 1 and 2.

The use of an Australian Standard, as outlined in Option 4, again faces the same problems as Option 3 in providing the application rate for reducing underrun trauma. In addition, the need to develop a uniquely Australian performance standard does not exist, as there is an international standard available. This standard could be applied to Australian conditions, although there may have to be some adjustments to account for bull bar fitment and the greater use of bonneted vehicles as compared to vehicles in European countries.

The use of State and local government fleet purchasing arrangements, as outlined in Option 5, would suffer in the same way as the other non-regulatory options. However, it may be able to achieve an application rate into the fleet of 10 to 15 per cent, which over a period is likely to ramp up to a higher level. Unfortunately, there would be little effect on articulated heavy commercial vehicle numbers as few of these are purchased by government.

The business-as-usual approach, as outlined in Option 6, is not achieving the government objectives. The mandated rear bumpers for semi-trailers are not effective and so the outlaid cost of this regulation is unproductive.  There is no other UP mandated. The voluntary fitment of UP is minimal.

Adopting a range of standards from North America, Japan, UNECE, EU and Brazil for UP, as outlined in Option 7, would only add to the complexity of applying and maintaining the different standards.  This would raise the costs of administering regulation, as compared with a single international and globally accepted standard. Perhaps more importantly, when standards from various countries were revised, Australia would be unable to participate in the development process.  As such, it could find itself in the position of having to choose between accepting unsuitable updated requirements or rejecting the entire standard. This would lead to a less than optimal suite of standards, create uncertainty for business and become an increased administrative burden. It is an indication of the inefficiency of such a system that many of the major vehicle producing countries, such as in the European Union but also Japan, have signed up or are considering signing up to the internationally based United Nations (UNECE) regulatory system. The globally integrated automotive industry members in Australia have in turn expressed their support for adopting UNECE regulations to address road safety issues.

Implementing an Autralian Design Rule (ADR) based on international standard UNECE Regulation 93 for Underrun Protection, as outlined in Option 8, would be the most cost effective regulatory option available. If the provision of front UP for all new rigid and articulated trucks with a GVM greater than 7.5 tonnes was mandated, the benefit-cost ratio would be positive with a net return of about $36.5m per year.  This would be about $32m per year greater than Option 1.

Adopting UNECE requirements for front UP would facilitate market access to efficient and competitive suppliers of the systems. The option would allow transport operators to have a choice of suppliers and access to superior state-of-the-art transport safety technology. The community would be able to reduce the cost of underrun trauma efficiently, while the Australian Government would be able to provide administrative arrangements for compliance at less cost than Option 5 and also participate in a global forum for any future development of UP standards.

Option 8 would also meet the requirements of the COAG Principles for national standards-setting, the WTO’s Agreement on Technical Barriers to Trade, and it would enable the Australian Government to implement a key element of the National Road Safety Action Plan 2003 to 2004 and the National Heavy Vehicle Safety Strategy 2003-2010.

However, in the analysis it was necessary to assume that the states and territories would at the same time raise the state and territory 6 tonne steered axle limit to at least 6.1 tonne (an additional 100 kg). If this could not be done, the RIS benefit-cost analysis would have to be recalculated using more accurate techniques to capture the cost of the extra mass of the UP.

In conclusion, Option 8 is the recommended option. The benefits of front UP for all new rigid and articulated trucks with a GVM greater than 7.5 tonnes would outweigh the costs, using a discount rate of between 4 and 12 per cent over a 10 to 25 year period.  It would reduce the cost of underrun trauma by an estimated 10 per cent based on an annual cost of underrun trauma of $337m (see page 21).  Annually it would cost transport operators $5.2m (around 3 thousand prime movers and 10 thousand rigid vehicles) to fit front UP at a marginal cost of $440 per prime mover. It would satisfy all the other objectives stated in Section 2 to the extent summarised below:

Objective: Review the policy proposal in the National Road Safety Strategy Action Plan 2003 to 2005 and National Heavy Vehicle Safety Strategy 2003-2010 for reducing heavy commercial vehicle underrun trauma by developing an ADR for front, rear and side UP devices.

Achieved by:  developing an ADR for front UP (rear and side underrun not achieved).

Objective: Does not impose excessive requirements on heavy commercial vehicle assemblers and transport operators.

Achieved by: Adopting international requirements, allowing access to a wide range of FUPS ranging from rigid, deflection to energy absorbing systems. European based manufacturers in particular, such as the three local assemblers, are well placed to access the technology.

Objective: Consistent with international standards such as UNECE Regulations.

Achieved by: Adopting UNECE Regulation requirements.

Objective: Is cost effective when implemented.

Achieved by: Adopting the option that gives the highest benefit-cost ratio and the highest net benefits of the available options.

Objective: Does not discourage competition.

Achieved by: Mandating requirements based on international standards that use established and available technology.

Objective: Adhere to the disciplines of regulation review

Achieved by:   Ongoing monitoring of underrun road crash fatalities. The Australian Transport Safety Bureau has recently begun to develop a heavy commercial vehicle crash database in response to suggestions from the National Transport Commission and the state governments. This database will compile details of underrun crashes across Australian states and territories.

Objective:  Address the community’s concerns in relation to new areas of road trauma and the need for efficient and effective responses.

Achieved by:  Following the European Union’s example of mandating front UP in August 2003.

Objective:  Does not breach World Trade Organisation commitments and does not pose as a technical barrier to trade

Achieved by:  Adopting an international standard which allows manufacturers access to the Australian market and is in keeping with the Agreement on Technical Barriers to Trade.

Recommended Option

The recommended option is Option 8: An Australian Design Rule (ADR) adopting international standard UNECE R 93 for front Underrun Protection (UP) for rigid and articulated heavy commercial vehicles with a GVM greater than 7.5 tonnes (some NB2 and all NC category vehicles). This would apply to all new vehicles.

It is further recommended that the bumper requirements in ADR 42/04 be withdrawn, without mandating replacement rear UP.

It is not recommended that side UP be mandated.

The recommendation for front UP is based on the assumption that the states and territories would at the same time raise the state and territory 6 tonne limit on steered axles to at least 6.10 tonne (an additional 100 kg). Otherwise the recommendation would require further analysis and may change.

# Implementation and Review

The development, implementation and review of Australian Design Rules (ADRs) is an established process.  If the public comment exposure indicateds broad agreement to the recommendations, an ADR can be determined under the authority of the Minister for Transport and Regional Services under section 7 of the Motor Vehicle Standards Act 1989.  Any draft text of the ADR as provided during the public comment period would be reviewed and revised (provided there are no major changes) prior to this to ensure that any incorporated standards remain the latest version.

After this review is completed, further development of the ADR would be considered as part of the normal program of ADR review and revision. This program includes monitoring overseas developments and regular consultation with the Department’s key stakeholders to identify implementation issues or changes in factors affecting existing ADRs.

# References and Data Sources

Australian Bureau of Statistics (1998), Motor Vehicle Use in Australia, Catalogue No. 9219.0

Australian Bureau of Statistics (2001), Motor Vehicle Census, catalogue No. 9309.0, Canberra

Australian Bureau of Statistics (2001), Survey of Motor Vehicle Use, Catalogue No. 9208.0

Australian Bureau of Statistics (2002), New Motor Vehicle Registrations, Catalogue No. 9301.0

Australian Bureau of Statistics (2002), Freight Movements, Catalogue No. 9220.0

Australian Bureau of Statistics (2002), Year Book Australia, 2002, Transport, Transport Activity/Structure and Performance of Transport and Storage Industry

Australian Bureau of Statistics (2003), Year Book Australia, 2002, Transport, Special Article – A history of road fatalities in Australia

Australian Bureau of Statistics (2003), Year Book Australia, 2002, Transport, Domestic freight activity

Australian Bureau of Statistics (2005), New Motor Vehicle Census, Catalogue No. 9309.0

Australian Transport Council (2003), National Road Safety Strategy 2001-2010

Australian Transport Council (2003), National Road Safety Action Plan 2003 and 2004

Australian Transport Safety Bureau (2004a), Heavy Commercial vehicle Crashes at 500 to 1499 kilometres outward distance from Base 1998 to 2002, Canberra

Australian Transport Safety Bureau (2004b), Fatal road crashes involving articulated commercial vehicles, Road Safety Working Paper No. 2, August 2004, Canberra

Australian Transport Safety Bureau (2004c), Fatal Crash Database 1990-1999, Special request to ATSB, October 2004, Canberra

Australian Transport Safety Bureau (2002a), Road Crash Data and Rates for Australian States and Territories, Canberra

Australian Transport Safety Bureau (2002b), Australian Commercial Vehicle Crash Database – A Summary, January –June 2000, Road Safety Office Report, OR 24

Australian Transport Safety Bureau (2001), Articulated Commercial vehicle Crashes, Monograph 8, Canberra

Australian Transport Safety Bureau (2001), Fatal Light Commercial vehicle Crashes, Monograph 18,

Australian Transport Safety Bureau (1997) Vehicle Type and the Risk of Travelling on the Road, Monograph 17

Australian Transport Safety Bureau (2001), Fatal Light Commercial vehicle Crashes, Monograph 9

Austroads (2004),  Future Trends in Heavy Vehicle Design, Sydney

Austroads (2001), Roadfacts 2000,

Avedal, C., and Forsman, L. (2002), The unique Volvo FUP system, Volvo Truck Corporation, PR and Communications, Sweden

Bureau of Transport Economics (2000), Road Crash Costs in Australia, Report 102, Canberra

Bureau of Transport and Regional Economics (2003), An overview of the Australian road freight transport industry, Working Paper No. 60, Canberra

Cairney, P.T. (1992), The Cost of Commercial vehicle Accidents in Australia: Australian Commercial vehicle Safety Study (Task 4) (ARR204), Australian Road Research Board, Melbourne

Commonwealth Office of Regulation Review (1998), A Guide to Regulation (second edition), Canberra

Commonwealth Office of Regulation Review (1997), Grey Letter law, Report of the Commonwealth Interdepartmental Committee on Quasi-regulation, Canberra

COAG, (2004), Principles and Guidelines for National Standard Setting and Regulatory Action by Ministerial Councils and Standards-Setting Bodies, Canberra

Department of Transport and Regional Services (2002), Auslink: A Land Transport Plan for Australia, Canberra

Department of Transport and Regional Services (2002), Annual Report  2001-02, Department of Transport and Regional Services, Canberra

Department of Transport and Regional Services (2004), Regulation Impact Statement Seatbelt Reminders, Canberra

European Union (2004), Motor Vehicles with trailers: Front UP devices  in Activities of the European Union, Summaries of Legislation, Brussels

http//europa.eu.int/scalplus/leg/en/lvb/l21248.htm, accessed 09/06/2004

FCAI (2003), VFACTS Report on Vehicle Retail Sales, December 2003, Melbourne

FCAI (2002), VFACTS Report on Vehicle Retail Sales, December 2002, Melbourne

FCAI (2001), VFACTS Report on Vehicle Retail Sales, December 2001, Melbourne

FCAI (2000), VFACTS Report on Vehicle Retail Sales, December 2000, Melbourne

FCAI (1999), VFACTS Report on Vehicle Retail Sales, December 1999, Melbourne

Fildes, B., Fitzharris M., Koppel, S., and Vulcan, A.P., (2002), Benefits of seat belt reminder systems, Report No. CR211a, Clayton

Haworth, N. and M. Symmons (2003), A Benefit-Cost Analysis of Heavy Vehicle UP, MUARC, Melbourne

Haworth, N. and M. Symmons (2002), Review of Commercial vehicle Safety – Stage 2: Update of Crash Statistics, VicRoads, Melbourne

House of Representatives (2004),  National Road Safety - Eyes on the Road Ahead, Inquiry into National Road Safety, Standing Committee on Transport and Regional Services, “The Neville Report 3”, The Parliament of the Commonwealth of Australia, Canberra

House of Representatives (2000),  Beyond the Midnight Oil – An Inquiry into Managing Fatigue in Transport,  Standing Committee on Communication, Transport and the Arts, “The Neville Report 2”, The Parliament of the Commonwealth of Australia, Canberra

Institution of Engineers, Australia (2004), Policy on Road Safety, National Committee on Transport, Institution of Engineers, Australia, Canberra

Lambert, J. and G. Rechnitzer (2002), Review of Commercial vehicle Safety: Stage 1: Frontal, Side and Rear-UP, VicRoads, Melbourne

Newstead, S., L. Watson, A. Delaney and M. Cameron (2004), Crashworthiness and Aggressivity of the Australian Light Vehicle Fleet by Major Vehicle Type, Report No. 227, Monash University Accident Research Centre, June

National Transport Commission (2003), National Heavy Vehicle Safety Strategy 2003–2010, Melbourne

National Transport Commission (2005), Length Limits for B-doubles – Regulatory Impact Statement, Melbourne

National Transport Commission (2006), Package to Accelerate the Delivery of Safety, Environment and Productivity Improvements for Heavy Vehicles – Regulatory Impact Statement, Melbourne

Office of Regulation Review (1998), A Guide to Regulation, (second edition), Office of Regulation Review, Productivity Commission, Canberra

Ogden, K.W. and H.W. Tan (1988), Commercial vehicle involvement in urban road accidents in Australia (CEWP 88/1), Department of Civil Engineering, Monash University, Melbourne

O’Neill, B., D. Mohan, J. Breen, M.J. Koonstra, M. Mackay, I. Roberts and G.A. Ryan (2002), Traffic Injury Prevention, 3, 190-194

Rechnitzer, G. (1993), Commercial vehicle involved crash study- Report on fatal and injury crashes of cars and other road users with the front and sides of heavy vehicles, Vicroads, Melbourne

Rechnitzer, G. (1997), Design Principles for under-ride guard and crash test results

Robinson, B.J. and B.S. Riley. (1991), Improving HGV Safety – Front Underrun Guards and Anti-locking Braking Systems, Proceedings of the 13th International Technical Conference on Experimental Safety Vehicles, 1275-1284, November 4-7, 1991, Paris France

Scania (2004), Proceedings of the Scania Road Safety Conference, Focus on the Driver, Scania CV, AB, Sweden

Scania (2004), Scania updates design for front bumpers in Scania World Magazine

http://www.scania.com/news/Scania_World_magazine/no_3/scania_world/underrun.as...  Accessed 9/06/2004

Scania (2003), Front UP, Scania CV AB, Sweden

Sweatman, P.F., K.W Haworth, N. Corben and G. Rechnitzer (1995), Heavy Vehicle Crashes in Urban Areas, Federal Office of Road Safety, Canberra

Transport Canada (2001), Heavy Commercial Vehicle Collisions 1994-98, Road Safety and Motor Vehicle Regulation Directorate,

Vicroads (2004), National Heavy Vehicle Accreditation Scheme, Melbourne

# Abbreviations

| ADR | Australian Design Rule |
| --- | --- |
| ACA | Australian Communications Authority |
| ACCC | Australian Consumer and Competition Commission |
| AGCC | Arab Gulf Cooperation Council |
| ANCAP | Australian New Car Assessment Program |
| ARSTA | Australian Road Transport Suppliers Association |
| ATA | Australian Commercial vehicle Association |
| ATSB | Australian Transport Safety Bureau |
| AVSR | Australian Vehicle Standards Regulations |
| COAG | Council of Australian Governments |
| Cth | Commonwealth |
| DOTARS | Department of Transport and Regional Services |
| ECE | Economic Commission for Europe |
| EEC | European Economic Community (also EC or EU) |
| EEVC | European Enhanced Vehicle-safety Committee |
| EU | European Union (also EC or EEC) |
| FAPM | Federation of Automotive Product Manufacturers |
| FCAI | Federal Chamber of Automotive Industries |
| FMVSS | Federal Motor Vehicle Safety Standards |
| FORS | Federal Office of Road Safety |
| GVM | Gross Vehicle Mass |
| IRTAD | International Road Traffic and Accident Database |
| MTAA | Motor Traders Association of Australia |
| MUARC | Monash University Accident Research Centre |
| MVSA | Motor Vehicle Standards Act |
| NA category vehicle | Goods vehicle with GVM not exceeding 3.5 tonnes |
| NB category vehicle | Goods vehicle with GVM exceeding 3.5 tonnes |
| NC category vehicle | but not exceeding 12 tonnes |
| NTC | National Transport Commission |
| OECD | Organisation for Economic Cooperation and Development |
| RTA | Roads and Traffic Authority |
| TIC | Commercial vehicle Industry Council |
| TPA | Trade Practices Act |
| TC category trailer | A trailer with GTM exceeding 3.5 tonnes but not exceeding 10 tonnes |
| TD category trailer | A trailer with GTM exceeding 10 tonnes |
| UNECE | United Nations Economic Commission for Europe |
| VicRoads | Organisation providing roads and road safety administration in Victoria |

# Glossary

| Administrative cost | Cost incurred by DOTARS for administering an ADR |
| --- | --- |
| Aggressively | Aggresivity as a safety performance concept is the risk of injury that a vehicle poses to other road users with which it impacts, including other vehicle occupants and vulnerable road users such as motorcylists, bicyclists and pedestrians. |
| Articulated vehicle | A combination of a prime mover and semi-trailer |
| B-Double | A combination of vehicles consisting of a prime mover towing 2 semi-trailers |
| Combination vehicle | Either a combination of a rigid goods vehicle and one trailer (other than a semi-trailer); or an articulated vehicle |
| Heavy commercial Vehicle | Vehicles exceeding a GVM of 3.5 tonnes |
| Compliance cost | Cost incurred by vehicle manufacturers in preparing vehicles to comply with an ADR. |
| Crashworthiness | Crashworthiness as a safety performance concept is the relative safety of a vehicle in protecting its occupants in the event of a crash. It is a measure of the risk of death or serious injury to a driver or vehicle occupant when the vehicle is involved in a crash. |
| Δ (Delta) V | The closing velocity between two objects that collide. |
| Gross Profit Margin | The gross profit margin is defined as: 100 * income Operating tax before profits Operating . The average profit margin is slightly over-estimated because the operating profit before tax for non-employing businesses includes the returns to labour of working proprietors. The average gross profit margin for all industries in 1999/2000 was 7.0 per cent (ABS 2001c). |
| GCM | The mass specified for a vehicle by the manufacturer as being the maximum of the sum of the gross vehicle mass of the drawing vehicle plus the sum of the axle loads of any vehicle capable of being drawn as a trailer |
| GVM | The maximum laden mass of a vehicle as specified by the manufacturer of the completed vehicle |
| Laden mass | The mass of a vehicle and its load borne on the surface on which it is standing or-running. |
| Mercosur | The Southern Common Market created in 1991 by Argentina, Brazil, Paraguay and Uraguay. |
| Prime mover | A motor vehicle with no significant load carrying area and which is built to tow a semi-trailer |
| Rigid vehicle | A motor vehicle which has a significant load carrying area. It may also be equipped with a tow bar or other coupling on the rear of the vehicle |
| Road train | A combination of vehicles other than a B-Double consisting of a motor vehicle towing at least 2 trailers |
| Semi-trailer | A trailer that has one axle group or single axle towards the rear and a means of attachment to a Prime mover that would result in some of the load being imposed on the prime mover |
| Total combination mass | The combined mass of the laden or unladen trailer and the towing vehicle |
| Underrun collision | An underrun collision occurs when a passenger car or motorcycle slides underneath the front, side, or rear end of a heavy commercial vehicle. |
| Vehicle compatibility | Vehicle mass, stiffness and geometry affect compatibility. Incompatibility is greatest between a passenger car and articulated heavy commercial vehicle |

## Appendix 1: VEHICE CATEGORIES in the australian design rules

###### DETAILS OF HEAVY VEHICLE CATEGORIES

GOODS VEHICLES

A motor vehicle constructed primarily for the carriage of goods and having at least 4 wheels; or 3 wheels and a ‘Gross Vehicle Mass‘ exceeding 1.0 tonne.

A vehicle constructed for both the carriage of persons and the carriage of goods shall be considered to be primarily for the carriage of goods if the number of seating positions times 68 kg is less than 50 percent of the difference between the ‘Gross Vehicle Mass‘ and the ‘Unladen Mass‘. The equipment and installations carried on certain special-purpose vehicles not designed for the carriage of passengers (crane vehicles, workshop vehicles, publicity vehicles, etc.) are regarded as being equivalent to goods for the purposes of this definition. A goods vehicle comprising 2 or more non-separable but articulated units shall be considered as a single vehicle.

LIGHT GOODS VEHICLE (NA)

A goods vehicle with a ‘Gross Vehicle Mass‘ not exceeding 3.5 tonnes.

MEDIUM GOODS VEHICLE (NB)

A goods vehicle with a ‘Gross Vehicle Mass‘ exceeding 3.5 tonnes but not exceeding 12.0 tonnes.

HEAVY GOODS VEHICLE (NC)

A goods vehicle with a ‘Gross Vehicle Mass‘ exceeding 12.0 tonnes.

TRAILERS

A vehicle without motive power constructed to be drawn behind a motor vehicle.

VERY LIGHT TRAILER (TA)

A single-axle trailer with a ‘Gross Trailer Mass‘ not exceeding 0.75 tonne.

LIGHT TRAILER (TB)

A trailer with a ‘Gross Trailer Mass‘ not exceeding 3.5 tonnes, other than a trailer of Category TA.

MEDIUM TRAILER (TC)

A trailer with a ‘Gross Trailer Mass‘ exceeding 3.5 tonnes but not exceeding 10 tonnes.

HEAVY TRAILER (TD)

A trailer with a ‘Gross Trailer Mass‘ exceeding 10 tonnes.

## Appendix  2: The heavy commercial vehicle assembly and wholesaling industry in australia

### Background

The heavy commercial vehicle assembly and wholesaling segment of the motor vehicle manufacturing industry in Australia comprises of three sub segments: the first being heavy commercial vehicle assemblers, the second category comprising of importers, the third category comprises of suppliers of engines, transmissions, braking systems, trailers and suspension assemblies that are used in the assembly of a heavy commercial vehicle.  Industry revenue for 2003-04 was $14.94 billion.

The size of the trailer market for freight trailers is estimated at $2 billion annually with numerous small businesses operating in the market.

Locally built heavy commercial vehicles accounted for an estimated 15.5 per cent of the total number retailed in 2003 with the remainder 84.5 per cent imported mainly from Japan and Europe.  All local assemblers and wholesalers are foreign owned and vehicles are sourced from all over the world.  As such, the industry displays a high level of globalization.

### Annual Sales Volume

The heavy commercial vehicle market in terms of annual sales is very small compared to other OECD countries and many developing economies.  Sales for 2002 and 2003 is shown in Table 18.

Table 18 : Annual sales for heavy commercial vehicles exceeding 7 tonnes GVM

| Heavy commercial vehicle type | 2001 | 2002 | 2003 | 2004 |
| --- | --- | --- | --- | --- |
| Rigid commercial vehicle, | 8721 | 10,010 | 12,507 | N/A |
| Prime mover | 1620 | 2041 | 2556 |  |
| Trailer | N/A | N/A | N/A | N/A |

Source: VFACTS

A number of vehicles are supplied from the plants of European, North American and Japanese manufacturers. Table 19 shows the sales distribution for 2003 based on country of

manufacture and demonstrates that the European Union is a key supplier of prime movers along with Australian made trucks such as Kenworth, Mack and International.

Table 19: Number of new heavy commercial vehicles sold during 2003

| Country of manufacture | Rigid commercial vehicles | Prime movers | Trailers | Total Rigid + Prime movers |
| --- | --- | --- | --- | --- |
| Australia | 1377 | 2800 | N/A | 4177 |
| European Union | 1552 | 1866 | Nil* | 3418 |
| Japan | 8900 | 240 | Nil* | 9140 |
| USA | 300 | 1044 | Nil* | 1344 |
| Total | 12,129 | 5950 |  | 18,079 |

Source: VFACTS

*Trailers from Japan, Europe and the USA are rarely supplied to the Australian market.

### Types of Vehicles

Rigid heavy commercial vehicles offer a load carrying area and may be equipped with a tow bar or other coupling on the rear of the vehicle.  Articulated heavy commercial vehicles consist of a prime mover (towing vehicle) which has no significant load carrying area but linked with a turntable device to a semi-trailer.  In all thirteen types of vehicles are normally registered across Australian states and territories.

The various types of heavy commercial vehicles operating in Australia are detailed below. In summary, there are five main operating classes of heavy commercial vehicles. These are:

- Rigid commercial vehicles

- Rigid commercial vehicles with trailers

- Semi-trailers

- B-Doubles

- Road trains

A B-Double combination consists of a prime mover towing two semi-trailers.  The first trailer includes a turntable, which links to the second trailer, rather than using a dolly to link the trailers as in road train configurations.  A road train comprises of a prime mover hauling two or more trailers and employing a dolly or a rigid heavy commercial vehicle hauling two or more trailers.  Such a classification of the heavy commercial vehicle market is useful for costing heavy commercial vehicle UP devices.

Articulated heavy trucks

- Three Axle Semi-Trailer

Maximum Mass Limit (tonnes) 24 (no increase permitted)
Annual Charge ($) 1,763
Width=2.5m
Height=4.3m
Length=19m

- Five Axle Semi-Trailer

Maximum Mass Limit (tonnes) 39.0 (40.0)
Annual Charge ($) 4,406
Width=2.5m
Height=4.3m
Length=19m

- Six Axle Semi-Trailer

Maximum Mass Limit (tonnes) 42.5 (45.5)
Annual Charge ($) 4,737
Width=2.5m
Height=4.3m
Length=19m

- Seven Axle B-Double

Maximum Mass Limit (tonnes) 55.5 (57)
Annual Charge ($) 6,830
Width=2.5m
Height=4.3m
Length=25m

- Eight Axle B-Double

Maximum Mass Limit (tonnes) 59.0 (62.5)
Annual Charge ($) 7,161
Width=2.5m
Height=4.3m
Length=25m

- Nine Axle B-Double

Maximum Mass Limit (tonnes) 62.5 (68)
Annual Charge ($) 7,492
Width=2.5m
Height=4.3m
Length=25m

- Double Road Train

Maximum Mass Limit (tonnes) 79.0 (85.7)
Annual Charge ($) 8,154
Width=2.5m
Height=4.3m
Length=36.5m

- Vehicle: Triple Road Train

Maximum Mass Limit (tonnes) 115.5 (125.2)
Annual Charge ($) 9,809
Width=2.5m
Height=4.3m
Length=53.5m

Rigid Trucks

- Two Axle Rigid Commercial vehicle

Maximum Mass Limit (tonnes): 15 (no increase permitted)
Annual Charge ($);
Up to 12t: $331
Up to 15t: $551 
Width=2.5m
Height=4.3m
Length=12.5m

- Three Axle Rigid Commercial vehicle

Maximum Mass Limit (tonnes): 22.5 (23)
Annual Charge ($);
Up to 16.5t: $661
Up to 22.5t: $881
Width=2.5m
Height=4.3m
Length=12.5m

- Four Axle Twin-Steer Rigid Commercial vehicle

Maximum Mass Limit (tonnes): 26.5* (27)
Annual Charge ($);
Up to 20t: $ 992
Up to 26.5t: $2,203
Width=2.5m
Height=4.3m
Length=12.5m

* If load-sharing twin-steer, mass is 27.5t (28)

- Two Axle Rigid Commercial vehicle with Two Axle Dog Trailer

Maximum Mass Limit (tonnes): 30.0 (no increase permitted)
Annual Charge ($) 1,268
Width=2.5m
Height=4.3m
Length=19m

- Three Axle Rigid Commercial vehicle with Three Axle Dog Trailer

Maximum Mass Limit (tonnes): 42.5* (no increase permitted)
Annual Charge ($);
Up to 42.5t: $3,196
Over 42.5t: $5,178
Width=2.5m
Height=4.3m
Length=19m

Source: National Transport Commission, Melbourne

## Appendix 3: SOURCES OF data collection

Several types of data collection sources have been used for estimating the cost of underrun trauma, underrun exposure rate, underrun fatality rate and injury severity. They include:

- ATSB National Fatal Road Crash Database

- ATSB Monthly Road Fatality Database;

- State crash databases;

- Exposure data; and

- Special Reports and Journal Articles

These databases are described below:

databases for road crashes

atsb national fatal road crash database

The Australian Transport Safety Bureau (ATSB) Monthly Road Fatality Database and the National Fatal Road Crash Database (FCD) combine information from crash databases and coronial records for all fatal crashes. The FCD is available for a range of years (for example 1992, 1994, 1996, 1997) but is generally not available for several years after the occurrence of the crash. Thus, it is a source of detailed but not timely data on a relatively small sample of crashes.

state crash databases

Each state and territory operates and manages a database of information about road crashes occurring within their jurisdiction. The databases are compiled from Police report forms with some enhancement by the state road authorities. The categories of crashes covered by the crash databases differ. All of the databases include crashes resulting in injury but some jurisdictions do not include non-injury crashes (for example Victoria). Other jurisdictions include non-injury crashes where the extent of property damage is above a certain threshold or a vehicle needs to be towed away. There is some concern about under reporting of minor crashes.

exposure data

Exposure data describes the amount and type of use of vehicles. Thus, they provide denominator data in the calculation of crash rates. The most commonly used source of information for vehicle exposure is the Australian Bureau of Statistics’ Survey of Motor Vehicle Use. The Survey provides information on the number and types of vehicles registered in each state and territory and how far they have travelled in the 12 months of the Survey period.

special reports and journal articles

A number of special reports and journal articles have been published that provide information about commercial vehicle underrun crashes, occupants killed and strategies for mitigating the risk of injuries from underrun collisions. These are included in the bibliography.

quality of underrun crash data

The quality of statistics should be judged with their ability to satisfy users’ information needs. Statistics on vehicle occupants killed or hospitalised in terms of underrun collisions should provide an accurate and timely measure of the crash events to which they relate. They need to be:

- Relevant, that is record the wearing status of the occupants and the circumstances under which the fatalities or hospitalisations occurred;

- Accurate and reliable, that is not be subject to large number of unknowns, errors or revisions;

- Timely, this is available after a year of occurrence of crashes;

- Comprehensive in coverage;

- Easily accessible

## Appendix 4: review of selected studies on Underrun Protection devices

Review of Literature

Frontal Underrun Collisions

Swedish Studies:

Swedish laboratory tests have shown that  Underrun Protection (UP) devices significantly reduce the risk of injury, especially combined with the use of seatbelts in passenger cars (Hogstrom et al, 1974). However, it is not possible, on the basis of these tests, to state any exact figures for the effect on the severity of injury of equipping all heavy commercial vehicles with UP devices.

Hogstrom et al (1974) of Volvo analyzed 187 collisions which occurred in the period 1970- 72 between cars and heavy commercial vehicles and found that 28 per cent were frontal impacts from the side or from the rear. In another study Fosser (1979) analyzed the distribution of points of impacts in 581 collisions in Sweden and found that in 44 per cent of crashes, other road users (passenger cars, motorcycles and pedestrians) hit the heavy commercial vehicle between the wheels on the side or from the rear. In continuing research, Hogstrom et al (1986) reviewed Fosser’s (1979) findings by studying over 1000 heavy commercial vehicle crashes in Sweden and noticed that the front of the heavy commercial vehicle is involved in some 77 per cent of fatal crashes.

Netherlands Studies

Goudsward et al (1991) studied commercial vehicle-passenger car crashes across Europe and found that 65 per cent of the fatally injured were passenger caroccupants numbering in excess of 7000 people and 60 per cent (4200 people) of these fatally injured passenger car occupants were killed in commercial vehicle front to car front collisions. The average relative speed in case of frontal crash injury cases (∆ v for the car) was estimated by Goudsward to be 55 km per hour with 25 per cent of collisions taking place with the sides of the commercial vehicle and 15 per cent with the rear of the commercial vehicle.

German Studies

In the late seventies Danner and Langweider (1981) studied 1559 multiple vehicle crashes involving cars and heavy commercial vehicles and found that the high mass of the commercial vehicle was not the sole factor in the severity of car-commercial vehicle crashes but frontal aggressivity of the commercial vehicle contributed significantly to serious injuries. They suggested that aggresivity could be reduced by engineering means. Danner et al also estimated impact speeds and found that in 50 per cent of the frontal crashes the impact speed was 50 km per hour. In commercial vehicles crashing into the sides of cars 70 per cent of crashes took place at speeds less than 30 km per hour.  In case of cars crashing into the rear of commercial vehicles 70 per cent of the crashes were at 40 km per hour.

British Studies:

Distribution of impact positions in 226 car-commercial vehicle crashes across Britain was analyzed by Mackay and Walton (1984). They found that 63 per cent of the crashes were with the front of the commercial vehicle, 11 per cent with the sides of the commercial vehicle and 18 per cent with the rear of the commercial vehicle.

Gloyns and Rattenbury (1989) found a higher proportion of frontal crashes than Mackay and Walton. According to Gloyns et al (1989) 75 per cent of passenger car fatalities involved the front of the heavy commercial vehicle. Of these 2/3 were frontal crashes of the head-on and offset type while 1/3 were heavy commercial vehicle into the side of the car. The Gloyns study produced some important information on frontal underrun crashes. The typical fatal frontal crash is offset with high levels of intrusion in majority of cases. In 70 per cent of the cases intrusion extended into the passenger compartment of the car with occupants suffering severe head and chest injuries. Gloyns estimated that front and rear UP devices would reduce fatalities by 17 per cent.

In a review of a sample of police reports on fatal crashes involving heavy commercial vehicles Thomas and Clift 91988) found that underrun was involved in some 88 per cent of their sample, and in 75 per cent of the cases the energy absorbing capacity of the car’s main chassis members was not utilized. They found that high levels of intrusion were common in frontal collisions, and in 58 per cent of the cases the A pillar was contacted.

Robinson and Riley (1991) studied 111 fatal crashes occurring in 1976 where cars drove under heavy commercial vehicles and concluded that UP devices at the front of the heavy commercial vehicle could certainly have prevented 11 deaths, probably have prevented 32 deaths and possibly have prevented 59 deaths. Unlike the Gloyns study it can be concluded that a mid point estimate of 32 per cent (32 fatalities prevented out of 111 fatalities) is the best estimate of the effects of UP devices.

Side and Rear Underrun Collisions

Australian Studies

Mc Lean (1966) in a study of 59 crashes involving heavy commercial vehicles in Adelaide suggested fitting rear and side UP devices for heavy commercial vehicles to reduce the injury potential for underrun collisions.

Swedish Studies

Hogstrom et al (1986) in a previously discussed study involving 100 commercial vehicles in Sweden suggested that side UP devices would have an injury reducing potential in 35 per cent of crashes involving vulnerable road users.

British Studies

The Riley et al (1981) 1976 study in Britain reviewed 740 fatal crashes and found 300 fatalities involved vulnerable road users. Two thirds of these fatalities (100 persons) involved vulnerable road users impacting with the sides of heavy commercial vehicles with 98 persons run over by the rear wheels of the heavy commercial vehicle. Riley et al estimated that side UP devices would save 40 motor cyclists/cyclists and 14 pedestrians.

German Studies

A significant number of side impacts were observed by Langweider and Danner (1987) in 1559 commercial vehicle involved crashes. They described these side impacts as “swiping” and noted that such impacts could take place during overtaking manoeuvres. The injury causing mechanism is not the speed but the danger of the subsequent fall into the space between the front and rear axle, resulting in being run over by the commercial vehicle’s wheels. They found that side UP devices would influence around 50 per cent of serious and fatal injury cases to motorcyclists and cyclists. In particular, these guards would totally avoid the falls between the wheels. They recommended that side panels should be designed with flat surfaces covering the whole area. This contrasts with other designs which employ side rails with gaps between the upper and lower rails, which can present their own hazards as people can still be caught between the rails.

In a continuing study, Langweider and Danner examined 110 commercial vehicle crashes with pedestrians and found that 42 per cent were with the front of the commercial vehicle while 33 per cent were with the side. They recommended that the design of the front and sides should present flat surfaces, without protruding edges, and particularly noted the need for this between the commercial vehicle’s cabin and the load tray. They also noted that two-thirds of commercial vehicle crashes are at speeds less than 30 km per hour and that the suggested measures of incorporating front and side UP devices would be effective.

## Appendix 5: METHODOLOGY OF BENEFIT-COST ANALYSIS

Benefit-cost analysis is a useful tool for evaluating the feasibility of implementing new technology, but it does not replace the decision process itself. Benefit-Cost Ratios show whether the returns (benefits) on a project outweigh the resources outlaid (cost) and what this difference is. Although a ratio greater than one suggests that a project should be pursued and less than one suggests that it should not, there may be other factors to consider. The goal of benefit-cost analysis is to provide information to assist with the decision.

When benefits and costs are spread over a period of time (for example the initial investment and maintenance necessary in the following years or the number of fatalities prevented following implementation of an initial investment) they have to be compared to one another in an objective manner. Although several methods exist, the method used in this analysis is the Net Present Value (NPV) method. Using this method, the flow of benefits and costs are reduced to one specific moment in time (this moment is the moment of initial investment), and both benefits and costs are discounted. The time period that the benefits are assumed to be generated over is the life of the vehicle. Although the expected heavy commercial vehicle life was assumed as being 15 years, a range from 10 to 25 years was used in the calculations.

Choosing the discount rate is important: the higher the discount rate the lower the impact of future benefits and costs when the projects are appraised. 7 per cent was used as a base discount rate. This was typical of similar studies on Underrun Protection (UP) devices in the Australian context.

However, a range of discount rates was established beginning with the view that the discount rate should be the interest rate of the ten-year Commonwealth Treasury bond. When discount rates are adjusted to fall in with inflation and taxes, they are a good indicator for the compensation consumers ask for postponing their own consumption. If this view is followed a discount rate of 4 per cent (real rate) should be used. This was the lower value of the established range.

An alternative view is that discount rates of about 12-14 per cent should be used for calculating net benefit, as consumers rather than governments finance the installation of safety devices in their vehicles. The auto finance rate in the country depends on the credit risk of a consumer, tenure of the loan and varies from 10.5 per cent to 15 per cent.

To obtain an inter temporal comparison of benefits and costs, discount rates of 4 per cent, 5 per cent, 6 per cent, 7 per cent and 12 per cent were applied for the analysis.

The methodology that was used to calculate the benefits and costs for the options presented is outlined below:

1. Estimate the number of (rigid and articulated) trucks in the fleet in the next year;

- Note the number of underrun protected (UP) and non UP vehicles in fleet the last year,

- Reduce these by a 3% assumed fleet attrition rate,

- Note the number of vehicles that were registered in the last year,

- Multiply this by 0.8 to remove the influence of European vehicles assumed to be already fitted with; and

- Add this to the last year’s reduced UP  fleet to get the size of the UP fleet and the total fleet for the next year.

2. Estimate the unit cost of front UP.

3. Estimate the unit cost of rear UP.

4. Estimate the unit cost of side UP;

- Note the proportion of each type (rigid and articulated) and length of trucks in the fleet this year’

- Estimate the unit cost of side UP per vehicle metre,

- Multiply  this by the length of different types of truck and trailers,

- Calculate a weighted average unit cost (rigid and articulated) by proportioning this out by the relative numbers of different trucks and trailers in the fleet.

5. Estimate the effectiveness of the different UP types;

- Note the reported effectiveness of UP under studies at various speeds to reduce fatal, serious and minor injuries,

- Average the effectiveness at various speeds,

- Both increase and decrease the effectiveness to give a number of alternative scenarios (A,B,C,) for sensitivity analysis,

- Add an extra scenario to represent energy absorbing UP (D).

6. Estimate the overall cost of underrun crashes per year;

- Summarise the 1990-99 FCD data and other estimates, for underrun crashes with rigid and articulated heavy commercial vehicles over 7.5 tonnes, in to the number of fatal, serious and minor injuries,

- Proportion  injuries relating to front, side or rear underrun using State crash databases,

- Note the cost of a single fatality, serious injury and minor injury for passenger vehicles and splitting this in to trauma cost (injuries) and non-trauma cost (property),

- Multiply the non-trauma cost by 1.5 for the cost of a single heavy vehicle fatality,

- Convert this to 2005 dollars,

- Multiply this by the summarised injury data on numbers to get an overall cost.

7. Calculate the possible overall yearly benefit from installing UP devices to the whole fleet;

- Multiply the yearly injury numbers and types (fatal, serious, minor) by the effectiveness of the underrun devices for each effectiveness scenario,

- Cascade any reduction in injury down to the next level ie fatal injuries saved become serious injuries, serious injuries saved become minor injuries (note that minor injuries are not cascaded to injury free),

- Take the reduced injury numbers away from the original injury numbers to get the net reduction in injuries.

8. Calculate the Benefit-Cost Ratio for installing UP progressively to the whole fleet through new registrations for each UP effectiveness scenario.

Two methods were used.

(a). Fleet registration and crash profile

This method calculates the cost to fit UP to new vehicles registered within a year, and compares this to the accumulation of benefits that these new vehicles then generate over their life. The benefits are discounted back to the starting year for comparison. This Benefit-Cost ratio represents a steady state in the fleet. This steady state is achieved once the initial group of vehicles have moved through their life (having provided all their benefits) and are beginning to exit the fleet. At this point, the costs become equivalent to the yearly cost to fit UP to new vehicles. The benefits become equivalent to the yearly benefits flowing from all vehicles in the fleet, at various stages in their lives, that are fitted with UP.

Note: this method was taken from Fildes (2002). It has been extended by assuming that the heavy commercial vehicle fleet has the same or similar registration and crash profile as the remainder of the fleet and by calculating additional multipliers representing different discount rates. The safety device in this case is UP. It is the main method used. A detailed explanation of the method can be found in the above reference and has not been repeated here. However, a summary table of the multipliers used is shown below, followed by a general description.

Multipliers

|  | Discount Rate (%) |
| --- | --- |
| Discount Period (yrs) | 4 | 5 | 6 | 7 | 12 |
| 10 | 0.4190 | 0.4000 | 0.3823 | 0.3659 | 0.2988 |
| 15 | 0.5769 | 0.5396 | 0.5059 | 0.4755 | 0.3600 |
| 20 | 0.6593 | 0.6093 | 0.5649 | 0.5255 | 0.3825 |
| 25 | 0.6829 | 0.6283 | 0.5803 | 0.5380 | 0.3870 |

- Establish a general profile of the vehicle fleet made up of, for any given year of vehicle age up to 20 years old, the number of new registrations as a proportion of the cumulative fleet over the entire period, divided in to the number of fatal or injury crashes as a proportion of the cumulative number of fatal or injury crashes over the same period,

- For any given year after year zero (first registration), reduce the proportions by the generic time discount factor of (1 + d)n,

- Add the proportions up for each year that the safety device of interest has been fitted,

- Multiply the final result by the estimated net saving in injuries established at point 7,

- Calculate the cost to fit the safety device of interest to newly registered vehicles,

- Calculate the Net Present Values of the benefits and costs.

- Calculate the Benefit-Cost Ratios.

(b). Fleet registration approximation

This method calculates the cost to fit UP to new vehicles registered over a period, set at 10, 15 or 25 years (coinciding with the expected life of a vehicle). It then, compares this cost to the accumulation of benefits that new vehicles generate over this period, whatever their age at the time. Both the costs and benefits are discounted back to the starting year of the period for comparison. T

This Benefit-Cost ratio represents costs and benefits that occur from the beginning of the period up until steady state in the fleet. This steady state is achieved once the initial group of vehicles have moved through their life (having provided all their benefits) and are beginning to exit the fleet.

This results of this method differ from the method in (a) mainly in that the costs and benefits are cumulative from the start of the period. The results would then be expected to be more conservative because they include the later years where costs have been incurred but benefits are yet to be gained.

Note: this method was used to provide a sensitivity comparison to the method above.

- For a given year, calculate the proportion of vehicles in the fleet fitted with UP, assuming they are only fitted to new vehicles (the figures only apply to rigid or articulated trucks).

- For a given year, multiply the overall cost of installing UP with the calculated proportion of the fleet. Adjust the cost using Present Values.

- For a given year, multiply the possible overall benefit from installing UP with the calculated proportion of the fleet.  Adjust the benefit using Present Values.

- For a given year, calculate the cumulative Net Present Values of the benefits and costs.

- For a given year calculate the cumulative Benefit-Cost Ratio.

Regardless of the method used, a starting point is summarising the Fatal Crash Database (FCD) data by the number of persons involved in road crashes between 1990-1999. A dataset for fatalities arising from heavy commercial vehicle (greater than 7.5 tonnes GVM) underrun collisions was composed from the FCD. The number of persons involved in serious and minor injuries were obtained from New South Wales and Queensland road crash databases and statistical reports published by state road safety agencies. The data set on serious injuries built up from state crash data and recent reports from the ATSB may have underestimated the true potential of the problem. Estimates for serious injuries can be validated if state road safety agencies are able to respond to questions raised in Section 4 of the analysis by providing data for serious injuries resulting from underrun collisions.

There are a number of on-going studies as well as past studies on the effectiveness of UP in preventing fatalities and serious injuries.  Appendix 4 provides a review of these studies but some key features of these studies are in Table 20.

Table 20:  Studies on heavy commercial vehicle underruns and effectiveness of UP devices

| Study | Type of UP device | Effectiveness in fatal crashes | Effectiveness in serious injury crashes |
| --- | --- | --- | --- |
| Mclean (1966) | Rear and side UP to be fitted | Considerably reduces injuries |  |
| Riley (1983) | Rear UP | 35% |  |
| Hogstrom and Svensson (1986) | Side UP would have positive effect on 35% of crashes involving cyclists and motor cyclists | 35% |  |
| Langweider and Danner (1987) | Side UP would prevent 50% of serious and fatal injuries to riders of motorcycles | 50% |  |
| Robinson and Riley (1991) | Energy absorbing front UP device | 36% |  |
| Rechnitzer and Foong (1993) | Rear UP and improved rear-end visibility | 40% |  |
| Rechnitzer (1993) | Front and side UP | 15% front (car-commercial vehicle) 20% side (pedestrian-commercial vehicle) 20% side (motorcycle-commercial vehicle) | 30% front (car-commercial vehicle) 30% side (pedestrian-commercial vehicle) 30% side (motorcycle-commercial vehicle) |

According to Rechnitzer (1993), rigid rear underrun systems are highly effective for speeds up to 60 kilometres per hour since they then engage the car’s safety systems.  Rear UP of the energy absorbing type is effective in collisions at speeds up to 90 kilometres per hour when occupants are restrained occupants and in airbag-equipped cars.

As the effectiveness of UP depends on ∆V, structural characteristics of the front ends of the passenger car and the heavy commercial vehicle to absorb energy, heavy vehicle height, overlap area of car-commercial vehicle, mass of heavy commercial vehicle, angle of impact, a number of effectiveness rates have to be used.  To estimate the benefits from the provision of UP, effectiveness rates based on, past studies, current research on heavy commercial vehicle-car compatibility, modelling results and judgement are used as shown in Table 21.

Table 21: Effectiveness  rates of  UP used  in estimating benefits

| Type of impact | Type of UP | Road user protected | Speed range | Injuries |
| --- | --- | --- | --- | --- |
|  |  |  |  | Fatal | Serious |
|  |  |  |  | Reduced by xx to serious | Reduced by xx to minor |
| Frontal | Rigid UP | Car occupants | 55-60 km/h | 20% | 30% |
| Frontal | Energy absorbing UP |  | Up to 75 km/h | 30% | 30% |
| Side | Rigid UP | Motor cyclists, pedestrians, bicyclists | Up to 35 km/h | 19% | 30% |
| Rear | Rigid UP |  | Up to 45 km/h | 32% | 30% |
|  | Energy absorbing UP | Car occupants | Up to 60 km/h | 42% | 30% |

Source: Rechnitzer, 1993, Haworth, 2002, Various studies

## Appendix  6: RESULTS OF BENEFIT-COST ANALYSIS

1. Estimate the number of (rigid and articulated) trucks in the fleet in the next year;

- Note the number of underrun protected (UP) and non UP vehicles in fleet the last year,

- Reduce these by a 3% assumed fleet attrition rate,

- Note the number of vehicles that were registered in the last year,

- Multiply this by 0.8 to remove the influence of European vehicles assumed to be already fitted with; and

- Add this to the last year’s reduced UP  fleet to get the size of the UP fleet and the total fleet for the next year.

| Heavy vehicle type | No. of vehicles on previous year's register (units) | Annual attrition (units) | Estimated no. of registrations annually adjusted for European trucks (units) | Estimated no. of vehicles on succeeding year's register (units) |
| --- | --- | --- | --- | --- |
| Rigid | 190,409 | 5,712 | 9,698 | 194,394 |
| Articulated | 61,778 | 1,853 | 2,354 | 62,278 |
| All trucks | 252,187 | 7,566 | 12,051 | 256,673 |

Source: ABS, NRTC Cost Allocation Model

2. Estimate the unit cost of a front UP device.

| Front UP device | Cost ($) | Model Production Run (units) | Unit cost ($) |
| --- | --- | --- | --- |
| ECE Program (Euro 300,0000) | $4,000,000 | 100,000 |  |
| Unit Program cost (amortised from above estimates) |  |  | $40.00 |
| ECE Program Materials |  |  | $275.00 |
| ECE Program Production |  |  | $75.00 |
| ECE Program Control |  |  | $25.00 |
| Product Liability |  |  | $25.00 |
| Total |  |  | $440.00 |

Source: VBG (component supplier), Sweden and Scania, Sweden

3. Estimate the unit cost of a rear UP device.

| Rear UP device | Cost ($) |  | Unit cost |
| --- | --- | --- | --- |
| ECE Program |  |  |  |
| Aluminum Beam (Euro 154 + 20%) | $308.00 |  |  |
| Mounting brackets (Euro 231 +20%) | $465.00 |  |  |
| ECE Program Production |  |  |  |
| ECE Program Control |  |  |  |
| Product Liability |  |  |  |
| Total | $773.00 |  | $773.00 |

Source: VBG (component supplier), Sweden and Scania, Sweden

4. Estimate the unit cost of a side UP device;

- Estimate the unit cost of a side UP device per vehicle metre,

- Note the proportion of each type (rigid and articulated) and length of trucks in the fleet this year’

- Multiply  this by the length of different types of truck and trailers,

- Calculate a weighted average unit cost (rigid and articulated) by proportioning this out by the relative numbers of different trucks and trailers in the fleet.

| Side UP device (19m) | Cost ($) | Unit cost | Cost/LM |
| --- | --- | --- | --- |
| ECE Program |  |  | 34.00 |
| Unit Program cost |  |  |  |
| ECE Program Materials |  |  |  |
| ECE Program Production |  |  |  |
| ECE Program Control |  |  |  |
| Product Liability |  |  |  |
| Total (Euro 780 + 20% shipping) | $1,560.00 | $1,560.00 | $45.88 |

Source: VBG (component supplier), Sweden and Scania, Sweden

| Summary of cost of UP for heavy trucks | length (m) | Cost SUP | Cost FUP | Cost RUP | Total | Proportion summary | Average cost SUPS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 axle semi-trailer | 19 | $872 | $440 | $773 | $2,085 | 0.05 | $44 |
| 5 axle semi-trailer | 19 | $872 | $440 | $773 | $2,085 | 0.2 | $174 |
| 6 axle semi-trailer | 19 | $872 | $440 | $773 | $2,085 | 0.4 | $349 |
| 7 axle B-Double | 25 | $1,147 | $440 | $773 | $2,360 | 0.05 | $57 |
| 8 axle B-Double | 25 | $1,147 | $440 | $773 | $2,360 | 0.05 | $57 |
| 9 axle B-Double | 25 | $1,147 | $440 | $773 | $2,360 | 0.15 | $172 |
| Double Road Train | 36.5 | $1,675 | $440 | $773 | $2,888 | 0.05 | $84 |
| Triple Road Train | 53.5 | $2,455 | $440 | $773 | $3,668 | 0.05 | $123 |
| 2 axle rigid truck | 12.5 | $574 | $440 | $773 | $1,787 | 0.4 | $229 |
| 3 axle rigid truck | 12.5 | $574 | $440 | $773 | $1,787 | 0.3 | $172 |
| 4 axle Twin-Steer rigid truck | 12.5 | $574 | $440 | $773 | $1,787 | 0.1 | $57 |
| 2 axle rigid truck with 2 axle dog trailer | 19 | $872 | $440 | $773 | $2,085 | 0.15 | $131 |
| 3 axle rigid truck with 3 axle dog trailer | 19 | $872 | $440 | $773 | $2,085 | 0.05 | $44 |
|  |  |  |  |  | Fleet average (SUPS) | $846.53 |

5. Estimate the effectiveness of the different UP device types;

- Note the reported effectiveness of devices under studies at various speeds to reduce fatal, serious and minor injuries,

- Average the effectiveness at various speeds,

- Both increase and decrease the effectiveness to give a number of alternative scenarios (A,B,C,) for sensitivity analysis,

- Add an extra scenario to represent energy absorbing UP devices (D).

| Scenario A - Low effectiveness |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rigid UP Effectiveness |  |  |  |  |  |  |  |  |  |
| Fatal injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  |  | 55% | 55% | 30% | 10% | 0% |  |
| Proportion of front underruns |  |  |  | 15% | 15% | 25% | 35% | 20% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 25% |
| Side UP (ECE R73) effectiveness |  |  |  | 35% | 20% | 10% | 0% | 0% |  |
| Proportion of side underruns |  |  |  | 25% | 45% | 25% | 5% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 20% |
| Rear UP (ECE R58) effectiveness |  |  |  | 40% | 35% | 25% | 0% | 0% |  |
| Proportion of rear underruns |  |  |  | 45% | 40% | 10% | 5% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 35% |
| Serious injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  | 70% | 40% | 35% | 35% | 0% | 0% |  |
| Proportion of front underruns |  |  | 5% | 30% | 45% | 10% | 0% | 0% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 35% |
| Side UP (ECE R73) effectiveness |  |  | 40% | 35% | 15% | 10% | 0% | 0% |  |
| Proportion of side underruns |  |  | 20% | 50% | 30% | 0% | 0% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 30% |
| Rear UP (ECE R58) effectiveness |  |  | 60% | 45% | 38% | 10% | 0% | 0% |  |
| Proportion of rear underruns |  |  | 25% | 45% | 30% | 5% | 0% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 45% |

| Scenario B - Most likely effectiveness |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rigid UP Effectiveness |  |  |  |  |  |  |  |  |  |
| Fatal injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  |  | 65% | 60% | 35% | 15% | 0% |  |
| Proportion of front underruns |  |  |  | 15% | 15% | 25% | 35% | 20% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 30% |
| Side UP (ECE R73) effectiveness |  |  |  | 40% | 25% | 15% | 0% | 0% |  |
| Proportion of side underruns |  |  |  | 25% | 45% | 25% | 5% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 25% |
| Rear UP (ECE R58) effectiveness |  |  |  | 45% | 40% | 30% | 0% | 0% |  |
| Proportion of rear underruns |  |  |  | 45% | 40% | 10% | 5% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 39% |
| Serious injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  | 75% | 45% | 40% | 40% | 0% | 0% |  |
| Proportion of front underruns |  |  | 5% | 30% | 45% | 10% | 0% | 0% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 39% |
| Side UP (ECE R73) effectiveness |  |  | 50% | 40% | 20% | 15% | 0% | 0% |  |
| Proportion of side underruns |  |  | 20% | 50% | 30% | 0% | 0% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 36% |
| Rear UP (ECE R58) effectiveness |  |  | 65% | 50% | 45% | 15% | 0% | 0% |  |
| Proportion of rear underruns |  |  | 25% | 45% | 30% | 5% | 0% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 50% |

| Scenario C - High effectiveness |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rigid UP Effectiveness |  |  |  |  |  |  |  |  |  |
| Fatal injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  |  | 70% | 65% | 45% | 20% | 0% |  |
| Proportion of front underruns |  |  |  | 15% | 15% | 25% | 35% | 20% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 35% |
| Side UP (ECE R73) effectiveness |  |  |  | 45% | 30% | 20% | 0% | 0% |  |
| Proportion of side underruns |  |  |  | 25% | 45% | 25% | 5% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 30% |
| Rear UP (ECE R58) effectiveness |  |  |  | 50% | 45% | 35% | 0% | 0% |  |
| Proportion of rear underruns |  |  |  | 45% | 40% | 10% | 5% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 44% |
| Serious injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  | 80% | 50% | 45% | 45% | 5% | 0% |  |
| Proportion of front underruns |  |  | 5% | 30% | 45% | 10% | 0% | 0% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 44% |
| Side UP (ECE R73) effectiveness |  |  | 55% | 45% | 25% | 20% | 0% | 0% |  |
| Proportion of side underruns |  |  | 20% | 50% | 30% | 0% | 0% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 41% |
| Rear UP (ECE R58) effectiveness |  |  | 70% | 55% | 50% | 20% | 0% | 0% |  |
| Proportion of rear underruns |  |  | 25% | 45% | 30% | 5% | 0% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 55% |

| Scenario D - Energy absorbing |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Energy Absorbing UP Effectiveness |  |  |  |  |  |  |  |  |  |
| Fatal injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  |  | 75% | 70% | 50% | 25% | 0% |  |
| Proportion of front underruns |  |  |  | 15% | 15% | 25% | 35% | 20% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 39% |
| Side UP (ECE R73) effectiveness |  |  |  | 50% | 35% | 25% | 0% | 0% |  |
| Proportion of side underruns |  |  |  | 25% | 45% | 25% | 5% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 35% |
| Rear UP (ECE R58) effectiveness |  |  |  | 55% | 50% | 40% | 10% | 0% |  |
| Proportion of rear underruns |  |  |  | 45% | 40% | 10% | 5% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 49% |
| Serious injury | speed | 20km/h | 30km/h | 40km/h | 50km/h | 60km/h | 70km/h | 100km/h |  |
|  | g |  |  | 15 | 20 | 25 | 35 | 50 |  |
| Front UP (ECE R93) effectiveness |  |  | 85% | 55% | 50% | 55% | 15% | 0% |  |
| Proportion of front underruns |  |  | 5% | 30% | 45% | 10% | 0% | 0% |  |
| Weighted average front underrun effectiveness |  |  |  |  |  |  |  |  | 49% |
| Side UP (ECE R73) effectiveness |  |  | 60% | 50% | 30% | 25% | 0% | 0% |  |
| Proportion of side underruns |  |  | 20% | 50% | 30% | 0% | 0% | 0% |  |
| Weighted average side underrun effectiveness |  |  |  |  |  |  |  |  | 46% |
| Rear UP (ECE R58) effectiveness |  |  | 75% | 60% | 55% | 25% | 0% | 0% |  |
| Proportion of rear underruns |  |  | 25% | 45% | 30% | 5% | 0% | 0% |  |
| Weighted average rear underrun effectiveness |  |  |  |  |  |  |  |  | 60% |

Summary of effectiveness of UP devices

| Scenario A - Low |  |  |  |
| --- | --- | --- | --- |
| Rigid UP | Front | Side | Rear |
| Fatal injury | 25% | 20% | 35% |
| Serious injury | 35% | 30% | 45% |
| Scenario B - Most Likely |  |  |  |
| Rigid UP | Front | Side | Rear |
| Fatal injury | 30% | 25% | 39% |
| Serious injury | 39% | 36% | 50% |
| Scenario C - High |  |  |  |
| Rigid UP | Front | Side | Rear |
| Fatal injury | 35% | 30% | 44% |
| Serious injury | 44% | 41% | 55% |
| Scenario D - Energy Absorbing UP | Front | Side | Rear |
| Fatal injury | 39% | 35% | 49% |
| Serious injury | 49% | 46% | 60% |

Source: Haworth (2002), Rechnitzer (1993), VC-COMPAT studies, Elvik.

6. Estimate the overall cost of underrun crashes per year;

- Summarise the 1990-99 FCD data and other estimates, for underrun crashes with rigid and articulated heavy commercial vehicles over 7.5 tonnes, in to the number of fatal, serious and minor injuries,

- Proportion  injuries relating to front, side or rear underrun using State crash databases,

- Note the cost of a single fatality, serious injury and minor injury for passenger vehicles and split this in to trauma cost (injuries) and non-trauma cost (property),

- Multiply the non-trauma cost by 1.5 for the cost of a single heavy vehicle fatality,

- Convert this to 2005 dollars,

- Multiply this by the summarised injury data on numbers to get an overall cost.

| UNDERRUN CRASHES Resulting in |
| --- |
| FATALITIES | 1990 | 1992 | 1994 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | Average |
| With cars and 4WDs |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 19 | 11 | 25 | 13 | 12 | 22 | 18 | NA | NA | NA | NA | 17 |
| Artic Truck | 55 | 10 | 39 | 16 | 7 | 16 | 26 | NA | NA | NA | NA | 24 |
| With motorcycle/bicycle |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 3 | 1 | 3 | 3 | 4 | 3 | 4 | NA | NA | NA | NA | 3 |
| Artic Truck | 9 | 1 | 0 | 2 | 4 | 5 | 7 | NA | NA | NA | NA | 4 |
| Rigid Truck Total | 22 | 12 | 28 | 16 | 16 | 25 | 22 | NA | NA | NA | NA | 20 |
| Artic Truck Total | 64 | 11 | 39 | 18 | 11 | 21 | 33 | NA | NA | NA | NA | 28 |
| TOTAL FATALITIES | 86 | 23 | 67 | 34 | 27 | 46 | 55 | NA | NA | NA | NA | 48 |
| SERIOUS INURIES | 1990 | 1992 | 1994 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | Average |
| With cars and 4WDs |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 128 | 74 | 169 | 88 | 81 | 149 | 122 | NA | NA | NA | NA | 116 |
| Artic Truck | 371 | 68 | 263 | 108 | 47 | 108 | 176 | NA |  |  |  | 163 |
| With motorcycle/bicycle |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 20 | 7 | 20 | 20 | 27 | 20 | 27 | NA | NA | NA | NA | 20 |
| Artic Truck | 61 | 7 | 0 | 14 | 27 | 34 | 47 | NA | NA | NA | NA | 27 |
| Rigid Truck Total | 149 | 81 | 189 | 108 | 108 | 169 | 149 | NA | NA | NA | NA | 136 |
| Artic Truck Total | 432 | 74 | 263 | 122 | 74 | 142 | 223 | NA | NA | NA | NA | 190 |
| TOTAL SERIOUS INJURIES | 581 | 155 | 452 | 230 | 182 | 311 | 371 | NA | NA | NA | NA | 326 |
| MINOR INURIES | 1990 | 1992 | 1994 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | Average |
| With cars and 4WDs |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 295 | 171 | 388 | 202 | 186 | 342 | 279 | NA | NA | NA | NA | 266 |
| Artic Truck | 854 | 155 | 605 | 248 | 109 | 248 | 404 | NA | NA | NA | NA | 375 |
| With motorcycle/bicycle |  |  |  |  |  |  |  |  |  |  |  |  |
| Rigid Truck | 47 | 16 | 47 | 47 | 62 | 47 | 62 | NA | NA | NA | NA | 47 |
| Artic Truck | 140 | 16 | 0 | 31 | 62 | 78 | 109 | NA | NA | NA | NA | 62 |
| Rigid Truck Total | 342 | 186 | 435 | 248 | 248 | 388 | 342 | NA | NA | NA | NA | 313 |
| Artic Truck Total | 994 | 171 | 605 | 279 | 171 | 326 | 512 | NA | NA | NA | NA | 437 |
| TOTAL MINOR INJURIES | 1335 | 357 | 1040 | 528 | 419 | 714 | 854 | NA | NA | NA | NA | 750 |

ource: ATSB FCD, 1990 – 99

| BREAK-UP OF UNDERRUN INJURIES |
| --- |
| FATAL INJURIES |  |  |  |  |  |
| Crash type | Total | Front | Side | Rear | Front/side |
| Proportions |  | 66% | 18% | 7% | 10% |
| Rigid Truck | 20 | 13 | 4 | 1 | 2 |
| Proportions |  | 65% | 15% | 5% | 15% |
| Articulated Truck | 28 | 18 | 4 | 1 | 4 |
| SERIOUS INJURIES |  |  |  |  |  |
| Crash type | Total | Front | Side | Rear | Front/side |
| Proportions |  | 66% | 18% | 7% | 10% |
| Rigid Truck | 136 | 90 | 24 | 10 | 14 |
| Proportions |  | 65% | 15% | 5% | 15% |
| Articulated Truck | 190 | 123 | 28 | 9 | 28 |
| MINOR INJURIES |  |  |  |  |  |
| Crash type | Total | Front | Side | Rear | Front/side |
| Proportions |  | 66% | 18% | 7% | 10% |
| Rigid Truck | 313 | 206 | 56 | 22 | 31 |
| Proportions |  | 65% | 15% | 5% | 15% |
| Articulated Truck | 437 | 284 | 66 | 22 | 66 |

Source: ATSB FCD, 1996 - 99, Serious injuries estimated from Haworth et al (2002) and NSW, VIC and QLD databases. Minor injuries from Haworth et al (2002)

| UNIT COST OF HEAVY VEHICLE CRASHES |
| --- |
|  | in 1995 dollars | in 1995 dollars | in 2005 dollars |
| Crash | Passenger vehicle | Passenger vehicle (per person injured) | Passenger vehicle (other than person) | Heavy vehicle (per person injured) | Heavy vehicle (other than person) | Heavy vehicle (per person injured) | Heavy vehicle (other than person) |
| Fatal | $1,652,994 | $1,500,000 | $152,994 | $1,500,000 | $229,491 | $2,220,366 | $301,994 |
| Serious | $407,990 | $325,000 | $82,990 | $325,000 | $124,485 | $481,079 | $163,814 |
| Minor | $13,776 | $11,611 | $2,165 | $11,611 | $3,248 | $17,187 | $4,273 |
| Property damage | $5,808 | $0 | $5,808 | $0 | $8,712 | $0 | $11,464 |

Source: BTE Report 102 and other reports/studies

Note: Heavy vehicle crashes cost 50% more than passenger car crashes (Neville Inquiry). There are two components in the cost resulting from a heavy vehicle crash, one relates to the injury to persons and other relates to heavy vehicle damages and immobility. The BTRE Report provides a value (fatal, serious and minor injuries) while Sweatman et al, 1995, Carney, 1991 and the Neville Inquiry provide values for the second component. They range from 1.5 to 2 times that for a passenger vehicle crash. This analysis uses a value of 1.5 times that of a passenger vehicle crash. Heavy vehicle (other than person) = 1.5 times (Passenger vehicle (other than person))

| ESTIMATED COST OF UNDERRUN CRASHES (2005$) |
| --- |
| PERSONS (Trauma) Rigid Trucks |  |  |  |
| Injury | Front | Side | Rear | Total |
| Fatal | $33,990,638 | $8,050,414 | $3,130,717 | $45,171,769 |
| Serious | $49,711,308 | $11,773,731 | $4,578,673 | $66,063,712 |
| Minor | $386,956 | $72,554 | $24,185 | $483,695 |
| All injuries | $84,088,902 | $19,896,699 | $7,733,575 | $111,719,176 |
| Articulated Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |
| Fatal | $49,989,964 | $9,373,118 | $3,124,373 | $62,487,455 |
| Serious | $73,110,323 | $13,708,185 | $4,569,395 | $91,387,903 |
| Minor | $6,007,486 | $1,126,404 | $375,468 | $1,126,404 |
| All injuries | $129,107,773 | $24,207,707 | $8,069,236 | $155,001,762 |
| All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |
| Fatal | $83,980,602 | $17,423,533 | $6,255,089 | $107,659,224 |
| Serious | $122,821,631 | $25,481,916 | $9,148,068 | $157,451,615 |
| Minor | $6,394,442 | $1,198,958 | $399,653 | $1,610,098 |
| All injuries | $213,196,675 | $44,104,407 | $15,802,810 | $266,720,938 |

| OTHER THAN PERSONS (Non-Trauma) Rigid Trucks |  |  |  |
| --- | --- | --- | --- |
| Injury | Front | Side | Rear | Total |
| Fatal | $4,623,104 | $1,094,946 | $425,812 | $6,143,862 |
| Serious | $16,927,345 | $4,009,108 | $2,227,282 | $23,163,735 |
| Minor | $96,215 | $18,040 | $6,013 | $120,268 |
| All injuries | $21,646,664 | $5,122,094 | $2,659,108 | $29,427,865 |
| Articulated Trucks |  |  |  |
| Injury | Front | Side | Rear | Total |
| Fatal | $6,799,190 | $1,274,848 | $424,949 | $8,498,988 |
| Serious | $24,895,012 | $4,667,815 | $1,555,938 | $31,118,765 |
| Minor | $560,149 | $375,468 | $1,126,404 | $2,062,021 |
| All injuries | $32,254,352 | $6,318,131 | $3,107,291 | $41,679,774 |
| All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |
| Fatal | $11,422,295 | $2,369,794 | $850,762 | $14,642,850 |
| Serious | $41,822,357 | $8,676,923 | $3,783,220 | $54,282,500 |
| Minor | $656,364 | $393,508 | $1,132,417 | $2,182,289 |
| All injuries | $53,901,015 | $11,440,225 | $5,766,399 | $71,107,639 |

Note: Estimated cost of underrun crashes = cost of injuries to persons and costs to other than persons

(includes truck damage and immobility)

7. Calculate the possible overall yearly benefit from installing UP devices to the whole fleet;

- Multiply the yearly injury numbers and types (fatal, serious, minor) by the effectiveness of the UP devices for each effectiveness scenario,

- Cascade any reduction in injury down to the next level ie fatal injuries saved become serious injuries, serious injuries saved become minor injuries (note that minor injuries are not cascaded to injury free),

- Take the reduced injury numbers away from the original injury numbers to get the net reduction in injuries.

- Repeat the process, but include non-injury (non-trauma) costs.

The four effectiveness rates for UP devices A, B, C and D above where combined with two benefit levels, Level 0 and Level 1. This gave eight possibilities in all. Level 0 benefit estimates were for trauma (injury reduction) alone while Level 1 benefit estimates included trauma and non-trauma related items such as reduced level of property damage, mobility of the truck after an underrun incident:

Scenario A0

| Benefit from UP (no. of lives and injuries saved) |  | Benefit from UP (injuries saved in $) |
| --- | --- | --- |
| Rigid Trucks |  | Rigid Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 4 | 1 | 0 | 5 |  | Fatal | $8,497,660 | $1,630,209 | $1,080,097 | $11,207,966 |
| Serious | 32 | 7 | 4 | 42 |  | Serious | $15,419,711 | $3,178,907 | $1,822,021 | $20,420,640 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 36 | 7 | 4 | 47 |  | All injuries | $23,917,371 | $4,809,116 | $2,902,118 | $31,628,606 |
| Articulated Trucks |  | Articulated Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 6 | 1 | 0 | 7 |  | Fatal | $12,497,491 | $1,898,056 | $1,077,909 | $15,473,456 |
| Serious | 47 | 8 | 4 | 59 |  | Serious | $22,677,739 | $3,701,210 | $1,818,329 | $28,197,278 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 53 | 9 | 4 | 66 |  | All injuries | $35,175,230 | $5,599,267 | $2,896,238 | $43,670,734 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 9 | 2 | 1 | 12 |  | Fatal | $20,995,151 | $3,528,265 | $2,158,006 | $26,681,422 |
| Serious | 79 | 14 | 8 | 101 |  | Serious | $38,097,450 | $6,880,117 | $3,640,350 | $48,617,918 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 89 | 16 | 9 | 113 |  | All injuries | $59,092,601 | $10,408,383 | $5,798,356 | $75,299,340 |

Scenario B0

| Benefit from UP (no. of lives and injuries saved) |  | Benefit from UP (injuries saved in $) |
| --- | --- | --- |
| Rigid Trucks |  | Rigid Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 5 | 1 | 1 | 6 |  | Fatal | $10,119,940 | $2,012,604 | $1,228,806 | $13,361,350 |
| Serious | 36 | 8 | 4 | 48 |  | Serious | $17,415,696 | $3,802,479 | $2,044,898 | $23,263,073 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 41 | 9 | 5 | 54 |  | All injuries | $27,535,636 | $5,815,083 | $3,273,705 | $36,624,423 |
| Articulated Trucks |  | Articulated Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 7 | 1 | 1 | 8 |  | Fatal | $14,883,376 | $2,343,280 | $1,226,316 | $18,452,972 |
| Serious | 53 | 9 | 4 | 67 |  | Serious | $25,613,229 | $4,427,236 | $2,040,755 | $32,081,220 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 60 | 10 | 5 | 75 |  | All injuries | $40,496,605 | $6,770,516 | $3,267,071 | $50,534,192 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 11 | 2 | 1 | 14 |  | Fatal | $25,003,316 | $4,355,883 | $2,455,123 | $31,814,321 |
| Serious | 89 | 17 | 8 | 115 |  | Serious | $43,028,925 | $8,229,715 | $4,085,653 | $55,344,293 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 101 | 19 | 10 | 129 |  | All injuries | $68,032,240 | $12,585,598 | $6,540,776 | $87,158,615 |

Scenario C0

| Benefit from UP (no. of lives and injuries saved) |  | Benefit from UP ( injuries saved in $) |
| --- | --- | --- |
| Rigid Trucks |  | Rigid Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 5 | 1 | 1 | 7 |  | Fatal | $11,896,723 | $2,394,998 | $1,377,515 | $15,669,237 |
| Serious | 40 | 9 | 5 | 54 |  | Serious | $19,378,204 | $4,308,313 | $2,241,612 | $25,928,130 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 46 | 10 | 5 | 61 |  | All injuries | $31,274,928 | $6,703,312 | $3,619,127 | $41,597,366 |
| Articulated Trucks |  | Articulated Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 8 | 1 | 1 | 10 |  | Fatal | $17,496,487 | $2,788,503 | $1,374,724 | $21,659,714 |
| Serious | 59 | 10 | 5 | 74 |  | Serious | $28,499,487 | $5,016,180 | $2,237,069 | $35,752,737 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 67 | 12 | 5 | 84 |  | All injuries | $45,995,974 | $7,804,683 | $3,611,794 | $57,412,451 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 13 | 2 | 1 | 17 |  | Fatal | $29,393,211 | $5,183,501 | $2,752,239 | $37,328,951 |
| Serious | 100 | 19 | 9 | 128 |  | Serious | $47,877,691 | $9,324,494 | $4,478,681 | $61,680,866 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 113 | 22 | 11 | 145 |  | All injuries | $77,270,902 | $14,507,995 | $7,230,921 | $99,009,817 |

Scenario D0

| Benefit from UP (no. of lives and injuries saved) |  | Benefit from UP (Injuries saved in $) |
| --- | --- | --- |
| Rigid Trucks |  | Rigid Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 6 | 1 | 1 | 8 |  | Fatal | $13,287,249 | $2,777,393 | $1,541,878 | $17,606,520 |
| Serious | 45 | 10 | 5 | 60 |  | Serious | $21,700,576 | $4,814,148 | $2,434,934 | $28,949,657 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 51 | 11 | 6 | 68 |  | All injuries | $34,987,826 | $7,591,541 | $3,976,811 | $46,556,178 |
| Articulated Trucks |  | Articulated Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 9 | 1 | 1 | 11 |  | Fatal | $19,541,531 | $3,233,726 | $1,538,754 | $24,314,011 |
| Serious | 66 | 12 | 5 | 83 |  | Serious | $31,914,994 | $5,605,125 | $2,430,000 | $39,950,119 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 75 | 13 | 6 | 94 |  | All injuries | $51,456,526 | $8,838,851 | $3,968,753 | $64,264,129 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | 15 | 3 | 1 | 19 |  | Fatal | $32,828,781 | $6,011,119 | $3,080,632 | $41,920,531 |
| Serious | 111 | 22 | 10 | 143 |  | Serious | $53,615,570 | $10,419,272 | $4,864,933 | $68,899,776 |
| Minor |  |  |  |  |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | 126 | 24 | 11 | 162 |  | All injuries | $86,444,351 | $16,430,391 | $7,945,565 | $110,820,307 |

Scenario A1

| Benefit from UP (other than injuries saved in $) |  | Total Benefits from UP |
| --- | --- | --- |
| Rigid Trucks |  |  |  |  |  | Rigid Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $1,155,776 | $221,727 | $146,905 | $1,524,408 |  | Fatal | $9,653,436 | $1,851,935 | $1,227,002 | $12,732,373 |
| Serious | $5,877,550 | $1,202,732 | $1,000,156 | $8,080,438 |  | Serious | $21,297,262 | $4,381,640 | $2,822,177 | $28,501,078 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $7,033,326 | $1,424,459 | $1,147,061 | $9,604,846 |  | All injuries | $30,950,697 | $6,233,575 | $4,049,179 | $41,233,452 |
| Articulated Trucks |  |  |  |  |  | Articulated Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $1,699,798 | $258,157 | $146,608 | $2,104,562 |  | Fatal | $14,197,289 | $2,156,213 | $1,224,516 | $17,578,018 |
| Serious | $8,644,101 | $1,400,344 | $698,690 | $10,743,136 |  | Serious | $31,321,840 | $5,101,555 | $2,517,020 | $38,940,414 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $10,343,899 | $1,658,501 | $845,298 | $12,847,698 |  | All injuries | $45,519,129 | $7,257,768 | $3,741,536 | $56,518,432 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $2,855,574 | $479,883 | $293,513 | $3,628,970 |  | Fatal | $23,850,724 | $4,008,149 | $2,451,519 | $30,310,391 |
| Serious | $14,521,652 | $2,603,077 | $1,698,846 | $18,823,575 |  | Serious | $52,619,102 | $9,483,194 | $5,339,196 | $67,441,493 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $17,377,225 | $3,082,960 | $1,992,359 | $22,452,544 |  | All injuries | $76,469,826 | $13,491,343 | $7,790,715 | $97,751,884 |

Scenario B1

| Benefit from UP (other than injuries saved in $) |  | Total Benefits from UP |
| --- | --- | --- |
| Rigid Trucks |  |  |  |  |  | Rigid Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $1,376,424 | $273,736 | $167,131 | $1,817,292 |  | Fatal | $11,496,364 | $2,286,340 | $1,395,938 | $15,178,642 |
| Serious | $6,676,897 | $1,443,279 | $1,124,247 | $9,244,423 |  | Serious | $24,092,593 | $5,245,758 | $3,169,146 | $32,507,496 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $8,053,321 | $1,717,015 | $1,291,379 | $11,061,715 |  | All injuries | $35,588,957 | $7,532,098 | $4,565,083 | $47,686,138 |
| Articulated Trucks |  |  |  |  |  | Articulated Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $2,024,304 | $318,712 | $166,793 | $2,509,809 |  | Fatal | $16,907,680 | $2,661,992 | $1,393,109 | $20,962,781 |
| Serious | $9,819,699 | $1,680,413 | $785,378 | $12,285,491 |  | Serious | $35,432,928 | $6,107,650 | $2,826,133 | $44,366,711 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $11,844,004 | $1,999,125 | $952,171 | $14,795,300 |  | All injuries | $52,340,609 | $8,769,641 | $4,219,242 | $65,329,492 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $3,400,729 | $592,448 | $333,924 | $4,327,101 |  | Fatal | $28,404,044 | $4,948,332 | $2,789,047 | $36,141,423 |
| Serious | $16,496,596 | $3,123,692 | $1,909,626 | $21,529,914 |  | Serious | $59,525,521 | $11,353,407 | $5,995,279 | $76,874,207 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $19,897,325 | $3,716,141 | $2,243,550 | $25,857,015 |  | All injuries | $87,929,566 | $16,301,739 | $8,784,325 | $113,015,630 |

Scenario C1

| Benefit from UP (other than injuries saved in $) |  | Total Benefits from UP |
| --- | --- | --- |
| Rigid Trucks |  |  |  |  |  | Rigid Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $1,618,087 | $325,746 | $187,357 | $2,131,190 |  | Fatal | $13,514,810 | $2,720,745 | $1,564,873 | $17,800,427 |
| Serious | $7,476,244 | $1,643,734 | $1,235,611 | $10,355,589 |  | Serious | $26,854,448 | $5,952,048 | $3,477,223 | $36,283,719 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $9,094,330 | $1,969,481 | $1,422,969 | $12,486,780 |  | All injuries | $40,369,258 | $8,672,792 | $5,042,096 | $54,084,146 |
| Articulated Trucks |  |  |  |  |  | Articulated Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $2,379,717 | $379,267 | $186,978 | $2,945,962 |  | Fatal | $19,876,204 | $3,167,770 | $1,561,702 | $24,605,676 |
| Serious | $10,995,297 | $1,913,804 | $863,175 | $13,772,276 |  | Serious | $39,494,784 | $6,929,985 | $3,100,245 | $49,525,013 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $13,375,014 | $2,293,071 | $1,050,153 | $16,718,238 |  | All injuries | $59,370,988 | $10,097,755 | $4,661,947 | $74,130,689 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $3,997,803 | $705,014 | $374,335 | $5,077,152 |  | Fatal | $33,391,014 | $5,888,515 | $3,126,574 | $42,406,103 |
| Serious | $18,471,541 | $3,557,538 | $2,098,787 | $24,127,866 |  | Serious | $66,349,232 | $12,882,032 | $6,577,468 | $85,808,732 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $22,469,344 | $4,262,552 | $2,473,122 | $29,205,018 |  | All injuries | $99,740,246 | $18,770,547 | $9,704,042 | $128,214,835 |

Scenario D1

| Benefit from UP (other than injuries saved in $) |  | Total Benefits from UP |
| --- | --- | --- |
| Rigid Trucks |  |  |  |  |  | Rigid Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $1,807,214 | $377,756 | $209,713 | $2,394,682 |  | Fatal | $15,094,463 | $3,155,149 | $1,751,590 | $20,001,203 |
| Serious | $8,369,632 | $1,844,190 | $1,346,975 | $11,560,797 |  | Serious | $30,070,208 | $6,658,337 | $3,781,909 | $40,510,454 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $10,176,845 | $2,221,946 | $1,556,688 | $13,955,479 |  | All injuries | $45,164,671 | $9,813,487 | $5,533,499 | $60,511,657 |
| Articulated Trucks |  | Articulated Trucks |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $2,657,865 | $439,823 | $209,288 | $3,306,976 |  | Fatal | $22,199,397 | $3,673,548 | $1,748,041 | $27,620,986 |
| Serious | $12,309,201 | $2,147,195 | $940,972 | $15,397,368 |  | Serious | $44,224,195 | $7,752,320 | $3,370,972 | $55,347,486 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $14,967,066 | $2,587,017 | $1,150,260 | $18,704,343 |  | All injuries | $66,423,592 | $11,425,868 | $5,119,013 | $82,968,472 |
| All Trucks |  |  |  |  |  | All Trucks |  |  |  |  |
| Injury | Front | Side | Rear | Total |  | Injury | Front | Side | Rear | Total |
| Fatal | $4,465,079 | $817,579 | $419,000 | $5,701,658 |  | Fatal | $37,293,860 | $6,828,698 | $3,499,632 | $47,622,189 |
| Serious | $20,678,832 | $3,991,384 | $2,287,948 | $26,958,164 |  | Serious | $74,294,402 | $14,410,657 | $7,152,881 | $95,857,940 |
| Minor | $0 | $0 | $0 | $0 |  | Minor | $0 | $0 | $0 | $0 |
| All injuries | $25,143,911 | $4,808,963 | $2,706,948 | $32,659,822 |  | All injuries | $111,588,262 | $21,239,355 | $10,652,512 | $143,480,129 |

8. Calculate the Benefit-Cost Ratio for installing UP devices progressively to the whole fleet through new registrations for each device effectiveness scenario.

Two methods were used.

(a). Fleet registration and crash profile

- Establish a general profile of the vehicle fleet made up of, for any given year of vehicle age up to 20 years old, the number of new registrations as a proportion of the cumulative fleet over the entire period, divided in to the number of fatal or injury crashes as a proportion of the cumulative number of fatal or injury crashes over the same period,

- For any given year after year zero (first registration), reduce the proportions by the generic time discount factor of (1 + d)n,

- Add the proportions up for each year that the safety device of interest has been fitted,

- Multiply the final result by the estimated net saving in injuries established at point 7,

- Calculate the cost to fit the safety device of interest to newly registered vehicles,

- Calculate the Net Present Values of the benefits and costs.

- Calculate the Benefit-Cost Ratios.

Scenario A0

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $10,020,559 | $4,266,944 | 2.348 |  | $2,014,855 | $6,140,292 | 0.328 |  | $1,215,888 | $7,496,245 | 0.1622 |
| 10 | 5% | 0.4000 | $9,566,236 | $4,266,944 | 2.242 |  | $1,923,503 | $6,140,292 | 0.313 |  | $1,160,761 | $7,496,245 | 0.1548 |
| 10 | 6% | 0.3823 | $9,143,998 | $4,266,944 | 2.143 |  | $1,838,603 | $6,140,292 | 0.299 |  | $1,109,527 | $7,496,245 | 0.1480 |
| 10 | 7% | 0.3659 | $8,751,078 | $4,266,944 | 2.051 |  | $1,759,598 | $6,140,292 | 0.287 |  | $1,061,850 | $7,496,245 | 0.1417 |
| 10 | 12% | 0.2988 | $7,146,901 | $4,266,944 | 1.675 |  | $1,437,042 | $6,140,292 | 0.234 |  | $867,200 | $7,496,245 | 0.1157 |
| 15 | 4% | 0.5769 | $13,798,050 | $4,266,944 | 3.234 |  | $2,774,403 | $6,140,292 | 0.452 |  | $1,674,247 | $7,496,245 | 0.2233 |
| 15 | 5% | 0.5396 | $12,905,965 | $4,266,944 | 3.025 |  | $2,595,030 | $6,140,292 | 0.423 |  | $1,566,002 | $7,496,245 | 0.2089 |
| 15 | 6% | 0.5059 | $12,100,674 | $4,266,944 | 2.836 |  | $2,433,108 | $6,140,292 | 0.396 |  | $1,468,288 | $7,496,245 | 0.1959 |
| 15 | 7% | 0.4755 | $11,372,089 | $4,266,944 | 2.665 |  | $2,286,610 | $6,140,292 | 0.372 |  | $1,379,882 | $7,496,245 | 0.1841 |
| 15 | 12% | 0.3600 | $8,609,060 | $4,266,944 | 2.018 |  | $1,731,042 | $6,140,292 | 0.282 |  | $1,044,618 | $7,496,245 | 0.1394 |
| 20 | 4% | 0.6593 | $15,769,620 | $4,266,944 | 3.696 |  | $3,170,831 | $6,140,292 | 0.516 |  | $1,913,476 | $7,496,245 | 0.2553 |
| 20 | 5% | 0.6093 | $14,572,500 | $4,266,944 | 3.415 |  | $2,930,123 | $6,140,292 | 0.477 |  | $1,768,218 | $7,496,245 | 0.2359 |
| 20 | 6% | 0.5649 | $13,511,849 | $4,266,944 | 3.167 |  | $2,716,856 | $6,140,292 | 0.442 |  | $1,639,519 | $7,496,245 | 0.2187 |
| 20 | 7% | 0.5255 | $12,569,095 | $4,266,944 | 2.946 |  | $2,527,294 | $6,140,292 | 0.412 |  | $1,525,126 | $7,496,245 | 0.2035 |
| 20 | 12% | 0.3825 | $9,147,823 | $4,266,944 | 2.144 |  | $1,839,372 | $6,140,292 | 0.300 |  | $1,109,991 | $7,496,245 | 0.1481 |
| 25 | 4% | 0.6829 | $16,333,898 | $4,266,944 | 3.828 |  | $3,284,291 | $6,140,292 | 0.535 |  | $1,981,945 | $7,496,245 | 0.2644 |
| 25 | 5% | 0.6283 | $15,027,776 | $4,266,944 | 3.522 |  | $3,021,667 | $6,140,292 | 0.492 |  | $1,823,461 | $7,496,245 | 0.2432 |
| 25 | 6% | 0.5803 | $13,879,989 | $4,266,944 | 3.253 |  | $2,790,879 | $6,140,292 | 0.455 |  | $1,684,189 | $7,496,245 | 0.2247 |
| 25 | 7% | 0.5380 | $12,867,419 | $4,266,944 | 3.016 |  | $2,587,279 | $6,140,292 | 0.421 |  | $1,561,324 | $7,496,245 | 0.2083 |
| 25 | 12% | 0.3870 | $9,255,341 | $4,266,944 | 2.169 |  | $1,860,991 | $6,140,292 | 0.303 |  | $1,123,037 | $7,496,245 | 0.1498 |
| Articulated Trucks | Front |  | Side |  | Rear |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $14,737,216 | $1,035,584 | 14.231 |  | $2,345,901 | $2,494,539 | 0.940 |  | $1,213,424 | $1,819,333 | 0.6670 |
| 10 | 5% | 0.4000 | $14,069,044 | $1,035,584 | 13.586 |  | $2,239,540 | $2,494,539 | 0.898 |  | $1,158,409 | $1,819,333 | 0.6367 |
| 10 | 6% | 0.3823 | $13,448,060 | $1,035,584 | 12.986 |  | $2,140,690 | $2,494,539 | 0.858 |  | $1,107,279 | $1,819,333 | 0.6086 |
| 10 | 7% | 0.3659 | $12,870,193 | $1,035,584 | 12.428 |  | $2,048,704 | $2,494,539 | 0.821 |  | $1,059,698 | $1,819,333 | 0.5825 |
| 10 | 12% | 0.2988 | $10,510,933 | $1,035,584 | 10.150 |  | $1,673,152 | $2,494,539 | 0.671 |  | $865,443 | $1,819,333 | 0.4757 |
| 15 | 4% | 0.5769 | $20,292,765 | $1,035,584 | 19.595 |  | $3,230,245 | $2,494,539 | 1.295 |  | $1,670,854 | $1,819,333 | 0.9184 |
| 15 | 5% | 0.5396 | $18,980,778 | $1,035,584 | 18.329 |  | $3,021,400 | $2,494,539 | 1.211 |  | $1,562,828 | $1,819,333 | 0.8590 |
| 15 | 6% | 0.5059 | $17,796,438 | $1,035,584 | 17.185 |  | $2,832,874 | $2,494,539 | 1.136 |  | $1,465,313 | $1,819,333 | 0.8054 |
| 15 | 7% | 0.4755 | $16,724,909 | $1,035,584 | 16.150 |  | $2,662,306 | $2,494,539 | 1.067 |  | $1,377,086 | $1,819,333 | 0.7569 |
| 15 | 12% | 0.3600 | $12,661,327 | $1,035,584 | 12.226 |  | $2,015,456 | $2,494,539 | 0.808 |  | $1,042,501 | $1,819,333 | 0.5730 |
| 20 | 4% | 0.6593 | $23,192,348 | $1,035,584 | 22.395 |  | $3,691,806 | $2,494,539 | 1.480 |  | $1,909,598 | $1,819,333 | 1.0496 |
| 20 | 5% | 0.6093 | $21,431,747 | $1,035,584 | 20.695 |  | $3,411,550 | $2,494,539 | 1.368 |  | $1,764,635 | $1,819,333 | 0.9699 |
| 20 | 6% | 0.5649 | $19,871,849 | $1,035,584 | 19.189 |  | $3,163,242 | $2,494,539 | 1.268 |  | $1,636,197 | $1,819,333 | 0.8993 |
| 20 | 7% | 0.5255 | $18,485,343 | $1,035,584 | 17.850 |  | $2,942,535 | $2,494,539 | 1.180 |  | $1,522,035 | $1,819,333 | 0.8366 |
| 20 | 12% | 0.3825 | $13,453,685 | $1,035,584 | 12.991 |  | $2,141,586 | $2,494,539 | 0.859 |  | $1,107,742 | $1,819,333 | 0.6089 |
| 25 | 4% | 0.6829 | $24,022,232 | $1,035,584 | 23.197 |  | $3,823,909 | $2,494,539 | 1.533 |  | $1,977,929 | $1,819,333 | 1.0872 |
| 25 | 5% | 0.6283 | $22,101,321 | $1,035,584 | 21.342 |  | $3,518,134 | $2,494,539 | 1.410 |  | $1,819,766 | $1,819,333 | 1.0002 |
| 25 | 6% | 0.5803 | $20,413,272 | $1,035,584 | 19.712 |  | $3,249,427 | $2,494,539 | 1.303 |  | $1,680,776 | $1,819,333 | 0.9238 |
| 25 | 7% | 0.5380 | $18,924,087 | $1,035,584 | 18.274 |  | $3,012,376 | $2,494,539 | 1.208 |  | $1,558,161 | $1,819,333 | 0.8564 |
| 25 | 12% | 0.3870 | $13,611,812 | $1,035,584 | 13.144 |  | $2,166,757 | $2,494,539 | 0.869 |  | $1,120,762 | $1,819,333 | 0.6160 |

Scenario B0

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $11,536,488 | $4,266,944 | 2.704 |  | $2,436,320 | $6,140,292 | 0.397 |  | $1,371,570 | $7,496,245 | 0.1830 |
| 10 | 5% | 0.4000 | $11,013,434 | $4,266,944 | 2.581 |  | $2,325,860 | $6,140,292 | 0.379 |  | $1,309,384 | $7,496,245 | 0.1747 |
| 10 | 6% | 0.3823 | $10,527,319 | $4,266,944 | 2.467 |  | $2,223,200 | $6,140,292 | 0.362 |  | $1,251,590 | $7,496,245 | 0.1670 |
| 10 | 7% | 0.3659 | $10,074,957 | $4,266,944 | 2.361 |  | $2,127,669 | $6,140,292 | 0.347 |  | $1,197,809 | $7,496,245 | 0.1598 |
| 10 | 12% | 0.2988 | $8,228,097 | $4,266,944 | 1.928 |  | $1,737,642 | $6,140,292 | 0.283 |  | $978,236 | $7,496,245 | 0.1305 |
| 15 | 4% | 0.5769 | $15,885,445 | $4,266,944 | 3.723 |  | $3,354,750 | $6,140,292 | 0.546 |  | $1,888,617 | $7,496,245 | 0.2519 |
| 15 | 5% | 0.5396 | $14,858,404 | $4,266,944 | 3.482 |  | $3,137,856 | $6,140,292 | 0.511 |  | $1,766,512 | $7,496,245 | 0.2357 |
| 15 | 6% | 0.5059 | $13,931,287 | $4,266,944 | 3.265 |  | $2,942,063 | $6,140,292 | 0.479 |  | $1,656,287 | $7,496,245 | 0.2209 |
| 15 | 7% | 0.4755 | $13,092,480 | $4,266,944 | 3.068 |  | $2,764,921 | $6,140,292 | 0.450 |  | $1,556,562 | $7,496,245 | 0.2076 |
| 15 | 12% | 0.3600 | $9,911,454 | $4,266,944 | 2.323 |  | $2,093,139 | $6,140,292 | 0.341 |  | $1,178,370 | $7,496,245 | 0.1572 |
| 20 | 4% | 0.6593 | $18,155,277 | $4,266,944 | 4.255 |  | $3,834,102 | $6,140,292 | 0.624 |  | $2,158,476 | $7,496,245 | 0.2879 |
| 20 | 5% | 0.6093 | $16,777,055 | $4,266,944 | 3.932 |  | $3,543,044 | $6,140,292 | 0.577 |  | $1,994,620 | $7,496,245 | 0.2661 |
| 20 | 6% | 0.5649 | $15,555,947 | $4,266,944 | 3.646 |  | $3,285,165 | $6,140,292 | 0.535 |  | $1,849,443 | $7,496,245 | 0.2467 |
| 20 | 7% | 0.5255 | $14,470,571 | $4,266,944 | 3.391 |  | $3,055,951 | $6,140,292 | 0.498 |  | $1,720,403 | $7,496,245 | 0.2295 |
| 20 | 12% | 0.3825 | $10,531,723 | $4,266,944 | 2.468 |  | $2,224,130 | $6,140,292 | 0.362 |  | $1,252,114 | $7,496,245 | 0.1670 |
| 25 | 4% | 0.6829 | $18,804,921 | $4,266,944 | 4.407 |  | $3,971,296 | $6,140,292 | 0.647 |  | $2,235,712 | $7,496,245 | 0.2982 |
| 25 | 5% | 0.6283 | $17,301,207 | $4,266,944 | 4.055 |  | $3,653,736 | $6,140,292 | 0.595 |  | $2,056,936 | $7,496,245 | 0.2744 |
| 25 | 6% | 0.5803 | $15,979,780 | $4,266,944 | 3.745 |  | $3,374,672 | $6,140,292 | 0.550 |  | $1,899,832 | $7,496,245 | 0.2534 |
| 25 | 7% | 0.5380 | $14,814,026 | $4,266,944 | 3.472 |  | $3,128,484 | $6,140,292 | 0.510 |  | $1,761,236 | $7,496,245 | 0.2349 |
| 25 | 12% | 0.3870 | $10,655,507 | $4,266,944 | 2.497 |  | $2,250,271 | $6,140,292 | 0.366 |  | $1,266,830 | $7,496,245 | 0.1690 |
| Articulated Trucks | Front |  | Side |  | Rear |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $16,966,690 | $1,035,584 | 16.384 |  | $2,836,614 | $2,494,539 | 1.137 |  | $1,368,791 | $1,819,333 | 0.7524 |
| 10 | 5% | 0.4000 | $16,197,436 | $1,035,584 | 15.641 |  | $2,708,005 | $2,494,539 | 1.086 |  | $1,306,731 | $1,819,333 | 0.7182 |
| 10 | 6% | 0.3823 | $15,482,508 | $1,035,584 | 14.951 |  | $2,588,478 | $2,494,539 | 1.038 |  | $1,249,054 | $1,819,333 | 0.6865 |
| 10 | 7% | 0.3659 | $14,817,219 | $1,035,584 | 14.308 |  | $2,477,250 | $2,494,539 | 0.993 |  | $1,195,382 | $1,819,333 | 0.6570 |
| 10 | 12% | 0.2988 | $12,101,047 | $1,035,584 | 11.685 |  | $2,023,141 | $2,494,539 | 0.811 |  | $976,254 | $1,819,333 | 0.5366 |
| 15 | 4% | 0.5769 | $23,362,693 | $1,035,584 | 22.560 |  | $3,905,944 | $2,494,539 | 1.566 |  | $1,884,790 | $1,819,333 | 1.0360 |
| 15 | 5% | 0.5396 | $21,852,225 | $1,035,584 | 21.101 |  | $3,653,413 | $2,494,539 | 1.465 |  | $1,762,932 | $1,819,333 | 0.9690 |
| 15 | 6% | 0.5059 | $20,488,716 | $1,035,584 | 19.785 |  | $3,425,452 | $2,494,539 | 1.373 |  | $1,652,931 | $1,819,333 | 0.9085 |
| 15 | 7% | 0.4755 | $19,255,085 | $1,035,584 | 18.593 |  | $3,219,205 | $2,494,539 | 1.291 |  | $1,553,408 | $1,819,333 | 0.8538 |
| 15 | 12% | 0.3600 | $14,576,756 | $1,035,584 | 14.076 |  | $2,437,048 | $2,494,539 | 0.977 |  | $1,175,983 | $1,819,333 | 0.6464 |
| 20 | 4% | 0.6593 | $26,700,930 | $1,035,584 | 25.783 |  | $4,464,055 | $2,494,539 | 1.790 |  | $2,154,102 | $1,819,333 | 1.1840 |
| 20 | 5% | 0.6093 | $24,673,981 | $1,035,584 | 23.826 |  | $4,125,175 | $2,494,539 | 1.654 |  | $1,990,578 | $1,819,333 | 1.0941 |
| 20 | 6% | 0.5649 | $22,878,100 | $1,035,584 | 22.092 |  | $3,824,927 | $2,494,539 | 1.533 |  | $1,845,695 | $1,819,333 | 1.0145 |
| 20 | 7% | 0.5255 | $21,281,840 | $1,035,584 | 20.551 |  | $3,558,052 | $2,494,539 | 1.426 |  | $1,716,916 | $1,819,333 | 0.9437 |
| 20 | 12% | 0.3825 | $15,488,984 | $1,035,584 | 14.957 |  | $2,589,561 | $2,494,539 | 1.038 |  | $1,249,577 | $1,819,333 | 0.6868 |
| 25 | 4% | 0.6829 | $27,656,360 | $1,035,584 | 26.706 |  | $4,623,791 | $2,494,539 | 1.854 |  | $2,231,182 | $1,819,333 | 1.2264 |
| 25 | 5% | 0.6283 | $25,444,850 | $1,035,584 | 24.571 |  | $4,254,054 | $2,494,539 | 1.705 |  | $2,052,768 | $1,819,333 | 1.1283 |
| 25 | 6% | 0.5803 | $23,501,430 | $1,035,584 | 22.694 |  | $3,929,139 | $2,494,539 | 1.575 |  | $1,895,982 | $1,819,333 | 1.0421 |
| 25 | 7% | 0.5380 | $21,786,958 | $1,035,584 | 21.038 |  | $3,642,502 | $2,494,539 | 1.460 |  | $1,757,667 | $1,819,333 | 0.9661 |
| 25 | 12% | 0.3870 | $15,671,033 | $1,035,584 | 15.133 |  | $2,619,997 | $2,494,539 | 1.050 |  | $1,264,263 | $1,819,333 | 0.6949 |

Scenario C0

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $11,536,488 | $4,266,944 | 2.704 |  | $2,436,320 | $6,140,292 | 0.397 |  | $1,371,570 | $7,496,245 | 0.1830 |
| 10 | 5% | 0.4000 | $11,013,434 | $4,266,944 | 2.581 |  | $2,325,860 | $6,140,292 | 0.379 |  | $1,309,384 | $7,496,245 | 0.1747 |
| 10 | 6% | 0.3823 | $10,527,319 | $4,266,944 | 2.467 |  | $2,223,200 | $6,140,292 | 0.362 |  | $1,251,590 | $7,496,245 | 0.1670 |
| 10 | 7% | 0.3659 | $10,074,957 | $4,266,944 | 2.361 |  | $2,127,669 | $6,140,292 | 0.347 |  | $1,197,809 | $7,496,245 | 0.1598 |
| 10 | 12% | 0.2988 | $8,228,097 | $4,266,944 | 1.928 |  | $1,737,642 | $6,140,292 | 0.283 |  | $978,236 | $7,496,245 | 0.1305 |
| 15 | 4% | 0.5769 | $15,885,445 | $4,266,944 | 3.723 |  | $3,354,750 | $6,140,292 | 0.546 |  | $1,888,617 | $7,496,245 | 0.2519 |
| 15 | 5% | 0.5396 | $14,858,404 | $4,266,944 | 3.482 |  | $3,137,856 | $6,140,292 | 0.511 |  | $1,766,512 | $7,496,245 | 0.2357 |
| 15 | 6% | 0.5059 | $13,931,287 | $4,266,944 | 3.265 |  | $2,942,063 | $6,140,292 | 0.479 |  | $1,656,287 | $7,496,245 | 0.2209 |
| 15 | 7% | 0.4755 | $13,092,480 | $4,266,944 | 3.068 |  | $2,764,921 | $6,140,292 | 0.450 |  | $1,556,562 | $7,496,245 | 0.2076 |
| 15 | 12% | 0.3600 | $9,911,454 | $4,266,944 | 2.323 |  | $2,093,139 | $6,140,292 | 0.341 |  | $1,178,370 | $7,496,245 | 0.1572 |
| 20 | 4% | 0.6593 | $18,155,277 | $4,266,944 | 4.255 |  | $3,834,102 | $6,140,292 | 0.624 |  | $2,158,476 | $7,496,245 | 0.2879 |
| 20 | 5% | 0.6093 | $16,777,055 | $4,266,944 | 3.932 |  | $3,543,044 | $6,140,292 | 0.577 |  | $1,994,620 | $7,496,245 | 0.2661 |
| 20 | 6% | 0.5649 | $15,555,947 | $4,266,944 | 3.646 |  | $3,285,165 | $6,140,292 | 0.535 |  | $1,849,443 | $7,496,245 | 0.2467 |
| 20 | 7% | 0.5255 | $14,470,571 | $4,266,944 | 3.391 |  | $3,055,951 | $6,140,292 | 0.498 |  | $1,720,403 | $7,496,245 | 0.2295 |
| 20 | 12% | 0.3825 | $10,531,723 | $4,266,944 | 2.468 |  | $2,224,130 | $6,140,292 | 0.362 |  | $1,252,114 | $7,496,245 | 0.1670 |
| 25 | 4% | 0.6829 | $18,804,921 | $4,266,944 | 4.407 |  | $3,971,296 | $6,140,292 | 0.647 |  | $2,235,712 | $7,496,245 | 0.2982 |
| 25 | 5% | 0.6283 | $17,301,207 | $4,266,944 | 4.055 |  | $3,653,736 | $6,140,292 | 0.595 |  | $2,056,936 | $7,496,245 | 0.2744 |
| 25 | 6% | 0.5803 | $15,979,780 | $4,266,944 | 3.745 |  | $3,374,672 | $6,140,292 | 0.550 |  | $1,899,832 | $7,496,245 | 0.2534 |
| 25 | 7% | 0.5380 | $14,814,026 | $4,266,944 | 3.472 |  | $3,128,484 | $6,140,292 | 0.510 |  | $1,761,236 | $7,496,245 | 0.2349 |
| 25 | 12% | 0.3870 | $10,655,507 | $4,266,944 | 2.497 |  | $2,250,271 | $6,140,292 | 0.366 |  | $1,266,830 | $7,496,245 | 0.1690 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $19,270,737 | $1,035,584 | 18.609 |  | $3,269,895 | $2,494,539 | 1.311 |  | $1,513,218 | $1,819,333 | 0.8317 |
| 10 | 5% | 0.4000 | $18,397,020 | $1,035,584 | 17.765 |  | $3,121,641 | $2,494,539 | 1.251 |  | $1,444,610 | $1,819,333 | 0.7940 |
| 10 | 6% | 0.3823 | $17,585,006 | $1,035,584 | 16.981 |  | $2,983,857 | $2,494,539 | 1.196 |  | $1,380,847 | $1,819,333 | 0.7590 |
| 10 | 7% | 0.3659 | $16,829,372 | $1,035,584 | 16.251 |  | $2,855,639 | $2,494,539 | 1.145 |  | $1,321,512 | $1,819,333 | 0.7264 |
| 10 | 12% | 0.2988 | $13,744,348 | $1,035,584 | 13.272 |  | $2,332,167 | $2,494,539 | 0.935 |  | $1,079,263 | $1,819,333 | 0.5932 |
| 15 | 4% | 0.5769 | $26,535,307 | $1,035,584 | 25.624 |  | $4,502,561 | $2,494,539 | 1.805 |  | $2,083,662 | $1,819,333 | 1.1453 |
| 15 | 5% | 0.5396 | $24,819,720 | $1,035,584 | 23.967 |  | $4,211,457 | $2,494,539 | 1.688 |  | $1,948,947 | $1,819,333 | 1.0712 |
| 15 | 6% | 0.5059 | $23,271,049 | $1,035,584 | 22.471 |  | $3,948,675 | $2,494,539 | 1.583 |  | $1,827,339 | $1,819,333 | 1.0044 |
| 15 | 7% | 0.4755 | $21,869,892 | $1,035,584 | 21.118 |  | $3,710,924 | $2,494,539 | 1.488 |  | $1,717,314 | $1,819,333 | 0.9439 |
| 15 | 12% | 0.3600 | $16,556,255 | $1,035,584 | 15.987 |  | $2,809,296 | $2,494,539 | 1.126 |  | $1,300,065 | $1,819,333 | 0.7146 |
| 20 | 4% | 0.6593 | $30,326,871 | $1,035,584 | 29.285 |  | $5,145,920 | $2,494,539 | 2.063 |  | $2,381,391 | $1,819,333 | 1.3089 |
| 20 | 5% | 0.6093 | $28,024,666 | $1,035,584 | 27.062 |  | $4,755,278 | $2,494,539 | 1.906 |  | $2,200,612 | $1,819,333 | 1.2096 |
| 20 | 6% | 0.5649 | $25,984,907 | $1,035,584 | 25.092 |  | $4,409,168 | $2,494,539 | 1.768 |  | $2,040,442 | $1,819,333 | 1.1215 |
| 20 | 7% | 0.5255 | $24,171,878 | $1,035,584 | 23.341 |  | $4,101,530 | $2,494,539 | 1.644 |  | $1,898,075 | $1,819,333 | 1.0433 |
| 20 | 12% | 0.3825 | $17,592,362 | $1,035,584 | 16.988 |  | $2,985,105 | $2,494,539 | 1.197 |  | $1,381,425 | $1,819,333 | 0.7593 |
| 25 | 4% | 0.6829 | $31,412,046 | $1,035,584 | 30.333 |  | $5,330,055 | $2,494,539 | 2.137 |  | $2,466,603 | $1,819,333 | 1.3558 |
| 25 | 5% | 0.6283 | $28,900,217 | $1,035,584 | 27.907 |  | $4,903,843 | $2,494,539 | 1.966 |  | $2,269,364 | $1,819,333 | 1.2474 |
| 25 | 6% | 0.5803 | $26,692,884 | $1,035,584 | 25.776 |  | $4,529,299 | $2,494,539 | 1.816 |  | $2,096,035 | $1,819,333 | 1.1521 |
| 25 | 7% | 0.5380 | $24,745,590 | $1,035,584 | 23.895 |  | $4,198,878 | $2,494,539 | 1.683 |  | $1,943,126 | $1,819,333 | 1.0680 |
| 25 | 12% | 0.3870 | $17,799,132 | $1,035,584 | 17.188 |  | $3,020,190 | $2,494,539 | 1.211 |  | $1,397,661 | $1,819,333 | 0.7682 |

Scenario D0

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $14,658,700 | $85,533,505 | 0.171 |  | $3,180,595 | $85,533,505 | 0.037 |  | $1,666,148 | $150,266,817 | 0.0111 |
| 10 | 5% | 0.4000 | $13,994,088 | $85,533,505 | 0.164 |  | $3,036,390 | $85,533,505 | 0.035 |  | $1,590,606 | $150,266,817 | 0.0106 |
| 10 | 6% | 0.3246 | $11,356,873 | $85,533,505 | 0.133 |  | $2,464,176 | $85,533,505 | 0.029 |  | $1,290,853 | $150,266,817 | 0.0086 |
| 10 | 7% | 0.3131 | $10,954,526 | $85,533,505 | 0.128 |  | $2,376,876 | $85,533,505 | 0.028 |  | $1,245,121 | $150,266,817 | 0.0083 |
| 10 | 12% | 0.2260 | $7,906,707 | $85,533,505 | 0.092 |  | $1,715,571 | $85,533,505 | 0.020 |  | $898,698 | $150,266,817 | 0.0060 |
| 15 | 4% | 0.5769 | $20,184,651 | $85,533,505 | 0.236 |  | $4,379,598 | $85,533,505 | 0.051 |  | $2,294,242 | $150,266,817 | 0.0153 |
| 15 | 5% | 0.5152 | $18,025,598 | $85,533,505 | 0.211 |  | $3,911,134 | $85,533,505 | 0.046 |  | $2,048,838 | $150,266,817 | 0.0136 |
| 15 | 6% | 0.4627 | $16,188,998 | $85,533,505 | 0.189 |  | $3,512,634 | $85,533,505 | 0.041 |  | $1,840,086 | $150,266,817 | 0.0122 |
| 15 | 7% | 0.4157 | $14,544,521 | $85,533,505 | 0.170 |  | $3,155,821 | $85,533,505 | 0.037 |  | $1,653,170 | $150,266,817 | 0.0110 |
| 15 | 12% | 0.3143 | $10,995,836 | $85,533,505 | 0.129 |  | $2,385,840 | $85,533,505 | 0.028 |  | $1,249,817 | $150,266,817 | 0.0083 |
| 20 | 4% | 0.6593 | $23,068,786 | $85,533,505 | 0.270 |  | $5,005,387 | $85,533,505 | 0.059 |  | $2,622,061 | $150,266,817 | 0.0174 |
| 20 | 5% | 0.6015 | $21,044,346 | $85,533,505 | 0.246 |  | $4,566,131 | $85,533,505 | 0.053 |  | $2,391,958 | $150,266,817 | 0.0159 |
| 20 | 6% | 0.5491 | $19,211,753 | $85,533,505 | 0.225 |  | $4,168,502 | $85,533,505 | 0.049 |  | $2,183,660 | $150,266,817 | 0.0145 |
| 20 | 7% | 0.5024 | $17,579,326 | $85,533,505 | 0.206 |  | $3,814,303 | $85,533,505 | 0.045 |  | $1,998,114 | $150,266,817 | 0.0133 |
| 20 | 12% | 0.3674 | $12,855,971 | $85,533,505 | 0.150 |  | $2,789,445 | $85,533,505 | 0.033 |  | $1,461,245 | $150,266,817 | 0.0097 |
| 25 | 4% | 0.6829 | $23,894,248 | $85,533,505 | 0.279 |  | $5,184,493 | $85,533,505 | 0.061 |  | $2,715,885 | $150,266,817 | 0.0181 |
| 25 | 5% | 0.6263 | $21,911,684 | $85,533,505 | 0.256 |  | $4,754,323 | $85,533,505 | 0.056 |  | $2,490,542 | $150,266,817 | 0.0166 |
| 25 | 6% | 0.5767 | $20,176,696 | $85,533,505 | 0.236 |  | $4,377,872 | $85,533,505 | 0.051 |  | $2,293,338 | $150,266,817 | 0.0153 |
| 25 | 7% | 0.5330 | $18,646,806 | $85,533,505 | 0.218 |  | $4,045,921 | $85,533,505 | 0.047 |  | $2,119,447 | $150,266,817 | 0.0141 |
| 25 | 12% | 0.3842 | $13,441,116 | $85,533,505 | 0.157 |  | $2,916,408 | $85,533,505 | 0.034 |  | $1,527,754 | $150,266,817 | 0.0102 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $21,558,521 | $27,402,434 | 0.787 |  | $3,703,176 | $66,007,629 | 0.056 |  | $1,662,772 | $48,141,095 | 0.0345 |
| 10 | 5% | 0.4000 | $20,581,078 | $27,402,434 | 0.751 |  | $3,535,277 | $66,007,629 | 0.054 |  | $1,587,383 | $48,141,095 | 0.0330 |
| 10 | 6% | 0.3823 | $19,672,663 | $27,402,434 | 0.718 |  | $3,379,236 | $66,007,629 | 0.051 |  | $1,517,319 | $48,141,095 | 0.0315 |
| 10 | 7% | 0.3659 | $18,827,322 | $27,402,434 | 0.687 |  | $3,234,029 | $66,007,629 | 0.049 |  | $1,452,119 | $48,141,095 | 0.0302 |
| 10 | 12% | 0.2988 | $15,376,050 | $27,402,434 | 0.561 |  | $2,641,193 | $66,007,629 | 0.040 |  | $1,185,928 | $48,141,095 | 0.0246 |
| 15 | 4% | 0.5769 | $29,685,526 | $27,402,434 | 1.083 |  | $5,099,177 | $66,007,629 | 0.077 |  | $2,289,593 | $48,141,095 | 0.0476 |
| 15 | 5% | 0.5396 | $27,766,268 | $27,402,434 | 1.013 |  | $4,769,500 | $66,007,629 | 0.072 |  | $2,141,564 | $48,141,095 | 0.0445 |
| 15 | 6% | 0.5059 | $26,033,742 | $27,402,434 | 0.950 |  | $4,471,898 | $66,007,629 | 0.068 |  | $2,007,938 | $48,141,095 | 0.0417 |
| 15 | 7% | 0.4755 | $24,466,243 | $27,402,434 | 0.893 |  | $4,202,644 | $66,007,629 | 0.064 |  | $1,887,039 | $48,141,095 | 0.0392 |
| 15 | 12% | 0.3600 | $18,521,781 | $27,402,434 | 0.676 |  | $3,181,545 | $66,007,629 | 0.048 |  | $1,428,553 | $48,141,095 | 0.0297 |
| 20 | 4% | 0.6593 | $33,927,217 | $27,402,434 | 1.238 |  | $5,827,786 | $66,007,629 | 0.088 |  | $2,616,748 | $48,141,095 | 0.0544 |
| 20 | 5% | 0.6093 | $31,351,699 | $27,402,434 | 1.144 |  | $5,385,381 | $66,007,629 | 0.082 |  | $2,418,102 | $48,141,095 | 0.0502 |
| 20 | 6% | 0.5649 | $29,069,784 | $27,402,434 | 1.061 |  | $4,993,409 | $66,007,629 | 0.076 |  | $2,242,102 | $48,141,095 | 0.0466 |
| 20 | 7% | 0.5255 | $27,041,515 | $27,402,434 | 0.987 |  | $4,645,007 | $66,007,629 | 0.070 |  | $2,085,665 | $48,141,095 | 0.0433 |
| 20 | 12% | 0.3825 | $19,680,892 | $27,402,434 | 0.718 |  | $3,380,649 | $66,007,629 | 0.051 |  | $1,517,953 | $48,141,095 | 0.0315 |
| 25 | 4% | 0.6829 | $35,141,223 | $27,402,434 | 1.282 |  | $6,036,319 | $66,007,629 | 0.091 |  | $2,710,382 | $48,141,095 | 0.0563 |
| 25 | 5% | 0.6283 | $32,331,194 | $27,402,434 | 1.180 |  | $5,553,632 | $66,007,629 | 0.084 |  | $2,493,649 | $48,141,095 | 0.0518 |
| 25 | 6% | 0.5803 | $29,861,811 | $27,402,434 | 1.090 |  | $5,129,458 | $66,007,629 | 0.078 |  | $2,303,190 | $48,141,095 | 0.0478 |
| 25 | 7% | 0.5380 | $27,683,338 | $27,402,434 | 1.010 |  | $4,755,255 | $66,007,629 | 0.072 |  | $2,135,168 | $48,141,095 | 0.0444 |
| 25 | 12% | 0.3870 | $19,912,210 | $27,402,434 | 0.727 |  | $3,420,383 | $66,007,629 | 0.052 |  | $1,535,794 | $48,141,095 | 0.0319 |

Scenario A1

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $12,967,282 | $4,266,944 | 3.039 |  | $2,611,654 | $6,140,292 | 0.425 |  | $1,696,467 | $7,496,245 | 0.2263 |
| 10 | 5% | 0.4000 | $12,379,357 | $4,266,944 | 2.901 |  | $2,493,244 | $6,140,292 | 0.406 |  | $1,619,551 | $7,496,245 | 0.2160 |
| 10 | 6% | 0.3823 | $11,832,953 | $4,266,944 | 2.773 |  | $2,383,197 | $6,140,292 | 0.388 |  | $1,548,067 | $7,496,245 | 0.2065 |
| 10 | 7% | 0.3659 | $11,324,487 | $4,266,944 | 2.654 |  | $2,280,790 | $6,140,292 | 0.371 |  | $1,481,546 | $7,496,245 | 0.1976 |
| 10 | 12% | 0.2988 | $9,248,574 | $4,266,944 | 2.167 |  | $1,862,694 | $6,140,292 | 0.303 |  | $1,209,961 | $7,496,245 | 0.161 |
| 15 | 4% | 0.5769 | $17,855,611 | $4,266,944 | 4.185 |  | $3,596,181 | $6,140,292 | 0.586 |  | $2,335,992 | $7,496,245 | 0.3116 |
| 15 | 5% | 0.5396 | $16,701,193 | $4,266,944 | 3.914 |  | $3,363,677 | $6,140,292 | 0.548 |  | $2,184,963 | $7,496,245 | 0.2915 |
| 15 | 6% | 0.5059 | $15,659,092 | $4,266,944 | 3.670 |  | $3,153,794 | $6,140,292 | 0.514 |  | $2,048,628 | $7,496,245 | 0.2733 |
| 15 | 7% | 0.4755 | $14,716,253 | $4,266,944 | 3.449 |  | $2,963,903 | $6,140,292 | 0.483 |  | $1,925,280 | $7,496,245 | 0.2568 |
| 15 | 12% | 0.3600 | $11,140,706 | $4,266,944 | 2.611 |  | $2,243,776 | $6,140,292 | 0.365 |  | $1,457,502 | $7,496,245 | 0.1944 |
| 20 | 4% | 0.6593 | $20,406,956 | $4,266,944 | 4.783 |  | $4,110,030 | $6,140,292 | 0.669 |  | $2,669,776 | $7,496,245 | 0.3561 |
| 20 | 5% | 0.6093 | $18,857,801 | $4,266,944 | 4.420 |  | $3,798,025 | $6,140,292 | 0.619 |  | $2,467,105 | $7,496,245 | 0.3291 |
| 20 | 6% | 0.5649 | $17,485,247 | $4,266,944 | 4.098 |  | $3,521,588 | $6,140,292 | 0.574 |  | $2,287,538 | $7,496,245 | 0.3052 |
| 20 | 7% | 0.5255 | $16,265,260 | $4,266,944 | 3.812 |  | $3,275,878 | $6,140,292 | 0.534 |  | $2,127,931 | $7,496,245 | 0.2839 |
| 20 | 12% | 0.3825 | $11,837,902 | $4,266,944 | 2.774 |  | $2,384,194 | $6,140,292 | 0.388 |  | $1,548,714 | $7,496,245 | 0.2066 |
| 25 | 4% | 0.6829 | $21,137,170 | $4,266,944 | 4.954 |  | $4,257,098 | $6,140,292 | 0.693 |  | $2,765,307 | $7,496,245 | 0.3689 |
| 25 | 5% | 0.6283 | $19,446,960 | $4,266,944 | 4.558 |  | $3,916,684 | $6,140,292 | 0.638 |  | $2,544,183 | $7,496,245 | 0.3394 |
| 25 | 6% | 0.5803 | $17,961,645 | $4,266,944 | 4.209 |  | $3,617,536 | $6,140,292 | 0.589 |  | $2,349,864 | $7,496,245 | 0.3135 |
| 25 | 7% | 0.5380 | $16,651,311 | $4,266,944 | 3.902 |  | $3,353,630 | $6,140,292 | 0.546 |  | $2,178,437 | $7,496,245 | 0.2906 |
| 25 | 12% | 0.3870 | $11,977,038 | $4,266,944 | 2.807 |  | $2,412,216 | $6,140,292 | 0.393 |  | $1,566,917 | $7,496,245 | 0.2090 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $19,070,955 | $1,035,584 | 18.416 |  | $3,040,756 | $2,494,539 | 1.219 |  | $1,567,575 | $1,819,333 | 0.8616 |
| 10 | 5% | 0.4000 | $18,206,296 | $1,035,584 | 17.581 |  | $2,902,891 | $2,494,539 | 1.164 |  | $1,496,503 | $1,819,333 | 0.8226 |
| 10 | 6% | 0.3823 | $17,402,700 | $1,035,584 | 16.805 |  | $2,774,762 | $2,494,539 | 1.112 |  | $1,430,450 | $1,819,333 | 0.7862 |
| 10 | 7% | 0.3659 | $16,654,901 | $1,035,584 | 16.083 |  | $2,655,530 | $2,494,539 | 1.065 |  | $1,368,983 | $1,819,333 | 0.7525 |
| 10 | 12% | 0.2988 | $13,601,859 | $1,035,584 | 13.134 |  | $2,168,739 | $2,494,539 | 0.869 |  | $1,118,032 | $1,819,333 | 0.615 |
| 15 | 4% | 0.5769 | $26,260,212 | $1,035,584 | 25.358 |  | $4,187,042 | $2,494,539 | 1.678 |  | $2,158,511 | $1,819,333 | 1.1864 |
| 15 | 5% | 0.5396 | $24,562,411 | $1,035,584 | 23.718 |  | $3,916,338 | $2,494,539 | 1.570 |  | $2,018,956 | $1,819,333 | 1.1097 |
| 15 | 6% | 0.5059 | $23,029,795 | $1,035,584 | 22.238 |  | $3,671,971 | $2,494,539 | 1.472 |  | $1,892,980 | $1,819,333 | 1.0405 |
| 15 | 7% | 0.4755 | $21,643,165 | $1,035,584 | 20.899 |  | $3,450,880 | $2,494,539 | 1.383 |  | $1,779,003 | $1,819,333 | 0.9778 |
| 15 | 12% | 0.3600 | $16,384,614 | $1,035,584 | 15.822 |  | $2,612,434 | $2,494,539 | 1.047 |  | $1,346,766 | $1,819,333 | 0.7403 |
| 20 | 4% | 0.6593 | $30,012,469 | $1,035,584 | 28.981 |  | $4,785,318 | $2,494,539 | 1.918 |  | $2,466,935 | $1,819,333 | 1.3560 |
| 20 | 5% | 0.6093 | $27,734,131 | $1,035,584 | 26.781 |  | $4,422,050 | $2,494,539 | 1.773 |  | $2,279,662 | $1,819,333 | 1.2530 |
| 20 | 6% | 0.5649 | $25,715,518 | $1,035,584 | 24.832 |  | $4,100,194 | $2,494,539 | 1.644 |  | $2,113,738 | $1,819,333 | 1.1618 |
| 20 | 7% | 0.5255 | $23,921,285 | $1,035,584 | 23.099 |  | $3,814,114 | $2,494,539 | 1.529 |  | $1,966,258 | $1,819,333 | 1.0808 |
| 20 | 12% | 0.3825 | $17,409,980 | $1,035,584 | 16.812 |  | $2,775,923 | $2,494,539 | 1.113 |  | $1,431,048 | $1,819,333 | 0.7866 |
| 25 | 4% | 0.6829 | $31,086,394 | $1,035,584 | 30.018 |  | $4,956,550 | $2,494,539 | 1.987 |  | $2,555,208 | $1,819,333 | 1.4045 |
| 25 | 5% | 0.6283 | $28,600,606 | $1,035,584 | 27.618 |  | $4,560,205 | $2,494,539 | 1.828 |  | $2,350,884 | $1,819,333 | 1.2922 |
| 25 | 6% | 0.5803 | $26,416,156 | $1,035,584 | 25.508 |  | $4,211,907 | $2,494,539 | 1.688 |  | $2,171,329 | $1,819,333 | 1.1935 |
| 25 | 7% | 0.5380 | $24,489,050 | $1,035,584 | 23.648 |  | $3,904,641 | $2,494,539 | 1.565 |  | $2,012,926 | $1,819,333 | 1.1064 |
| 25 | 12% | 0.3870 | $17,614,607 | $1,035,584 | 17.009 |  | $2,808,549 | $2,494,539 | 1.126 |  | $1,447,868 | $1,819,333 | 0.7958 |

Scenario B1

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $14,910,553 | $4,266,944 | 3.494 |  | $3,155,691 | $6,140,292 | 0.514 |  | $1,912,613 | $7,496,245 | 0.2551 |
| 10 | 5% | 0.4000 | $14,234,523 | $4,266,944 | 3.336 |  | $3,012,615 | $6,140,292 | 0.491 |  | $1,825,897 | $7,496,245 | 0.2436 |
| 10 | 6% | 0.3823 | $13,606,235 | $4,266,944 | 3.189 |  | $2,879,643 | $6,140,292 | 0.469 |  | $1,745,305 | $7,496,245 | 0.2328 |
| 10 | 7% | 0.3659 | $13,021,570 | $4,266,944 | 3.052 |  | $2,755,904 | $6,140,292 | 0.449 |  | $1,670,309 | $7,496,245 | 0.2228 |
| 10 | 12% | 0.2988 | $10,634,561 | $4,266,944 | 2.492 |  | $2,250,714 | $6,140,292 | 0.367 |  | $1,364,121 | $7,496,245 | 0.1820 |
| 15 | 4% | 0.5769 | $20,531,446 | $4,266,944 | 4.812 |  | $4,345,305 | $6,140,292 | 0.708 |  | $2,633,619 | $7,496,245 | 0.3513 |
| 15 | 5% | 0.5396 | $19,204,027 | $4,266,944 | 4.501 |  | $4,064,368 | $6,140,292 | 0.662 |  | $2,463,348 | $7,496,245 | 0.3286 |
| 15 | 6% | 0.5059 | $18,005,757 | $4,266,944 | 4.220 |  | $3,810,764 | $6,140,292 | 0.621 |  | $2,309,643 | $7,496,245 | 0.3081 |
| 15 | 7% | 0.4755 | $16,921,626 | $4,266,944 | 3.966 |  | $3,581,317 | $6,140,292 | 0.583 |  | $2,170,579 | $7,496,245 | 0.2896 |
| 15 | 12% | 0.3600 | $12,810,248 | $4,266,944 | 3.002 |  | $2,711,179 | $6,140,292 | 0.442 |  | $1,643,202 | $7,496,245 | 0.2192 |
| 20 | 4% | 0.6593 | $23,465,134 | $4,266,944 | 5.499 |  | $4,966,195 | $6,140,292 | 0.809 |  | $3,009,931 | $7,496,245 | 0.4015 |
| 20 | 5% | 0.6093 | $21,683,824 | $4,266,944 | 5.082 |  | $4,589,196 | $6,140,292 | 0.747 |  | $2,781,438 | $7,496,245 | 0.3710 |
| 20 | 6% | 0.5649 | $20,105,580 | $4,266,944 | 4.712 |  | $4,255,174 | $6,140,292 | 0.693 |  | $2,578,992 | $7,496,245 | 0.3440 |
| 20 | 7% | 0.5255 | $18,702,765 | $4,266,944 | 4.383 |  | $3,958,280 | $6,140,292 | 0.645 |  | $2,399,050 | $7,496,245 | 0.3200 |
| 20 | 12% | 0.3825 | $13,611,926 | $4,266,944 | 3.190 |  | $2,880,848 | $6,140,292 | 0.469 |  | $1,746,035 | $7,496,245 | 0.2329 |
| 25 | 4% | 0.6829 | $24,304,779 | $4,266,944 | 5.696 |  | $5,143,898 | $6,140,292 | 0.838 |  | $3,117,634 | $7,496,245 | 0.4159 |
| 25 | 5% | 0.6283 | $22,361,274 | $4,266,944 | 5.241 |  | $4,732,572 | $6,140,292 | 0.771 |  | $2,868,336 | $7,496,245 | 0.3826 |
| 25 | 6% | 0.5803 | $20,653,371 | $4,266,944 | 4.840 |  | $4,371,109 | $6,140,292 | 0.712 |  | $2,649,259 | $7,496,245 | 0.3534 |
| 25 | 7% | 0.5380 | $19,146,670 | $4,266,944 | 4.487 |  | $4,052,229 | $6,140,292 | 0.660 |  | $2,455,991 | $7,496,245 | 0.3276 |
| 25 | 12% | 0.3870 | $13,771,913 | $4,266,944 | 3.228 |  | $2,914,707 | $6,140,292 | 0.475 |  | $1,766,557 | $7,496,245 | 0.2357 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $21,928,922 | $1,035,584 | 21.175 |  | $3,674,179 | $2,494,539 | 1.473 |  | $1,767,718 | $1,819,333 | 0.9716 |
| 10 | 5% | 0.4000 | $20,934,684 | $1,035,584 | 20.215 |  | $3,507,595 | $2,494,539 | 1.406 |  | $1,687,571 | $1,819,333 | 0.9276 |
| 10 | 6% | 0.3823 | $20,010,662 | $1,035,584 | 19.323 |  | $3,352,776 | $2,494,539 | 1.344 |  | $1,613,085 | $1,819,333 | 0.8866 |
| 10 | 7% | 0.3659 | $19,150,798 | $1,035,584 | 18.493 |  | $3,208,706 | $2,494,539 | 1.286 |  | $1,543,770 | $1,819,333 | 0.8485 |
| 10 | 12% | 0.2988 | $15,640,228 | $1,035,584 | 15.103 |  | $2,620,512 | $2,494,539 | 1.050 |  | $1,260,778 | $1,819,333 | 0.6930 |
| 15 | 4% | 0.5769 | $30,195,558 | $1,035,584 | 29.158 |  | $5,059,250 | $2,494,539 | 2.028 |  | $2,434,102 | $1,819,333 | 1.3379 |
| 15 | 5% | 0.5396 | $28,243,325 | $1,035,584 | 27.273 |  | $4,732,154 | $2,494,539 | 1.897 |  | $2,276,730 | $1,819,333 | 1.2514 |
| 15 | 6% | 0.5059 | $26,481,031 | $1,035,584 | 25.571 |  | $4,436,883 | $2,494,539 | 1.779 |  | $2,134,669 | $1,819,333 | 1.1733 |
| 15 | 7% | 0.4755 | $24,886,601 | $1,035,584 | 24.031 |  | $4,169,737 | $2,494,539 | 1.672 |  | $2,006,140 | $1,819,333 | 1.1027 |
| 15 | 12% | 0.3600 | $18,840,007 | $1,035,584 | 18.193 |  | $3,156,633 | $2,494,539 | 1.265 |  | $1,518,717 | $1,819,333 | 0.8348 |
| 20 | 4% | 0.6593 | $34,510,126 | $1,035,584 | 33.324 |  | $5,782,153 | $2,494,539 | 2.318 |  | $2,781,905 | $1,819,333 | 1.5291 |
| 20 | 5% | 0.6093 | $31,890,357 | $1,035,584 | 30.795 |  | $5,343,212 | $2,494,539 | 2.142 |  | $2,570,722 | $1,819,333 | 1.4130 |
| 20 | 6% | 0.5649 | $29,569,236 | $1,035,584 | 28.553 |  | $4,954,310 | $2,494,539 | 1.986 |  | $2,383,613 | $1,819,333 | 1.3102 |
| 20 | 7% | 0.5255 | $27,506,120 | $1,035,584 | 26.561 |  | $4,608,636 | $2,494,539 | 1.847 |  | $2,217,303 | $1,819,333 | 1.2187 |
| 20 | 12% | 0.3825 | $20,019,033 | $1,035,584 | 19.331 |  | $3,354,178 | $2,494,539 | 1.345 |  | $1,613,759 | $1,819,333 | 0.8870 |
| 25 | 4% | 0.6829 | $35,744,990 | $1,035,584 | 34.517 |  | $5,989,054 | $2,494,539 | 2.401 |  | $2,881,448 | $1,819,333 | 1.5838 |
| 25 | 5% | 0.6283 | $32,886,682 | $1,035,584 | 31.757 |  | $5,510,146 | $2,494,539 | 2.209 |  | $2,651,037 | $1,819,333 | 1.4571 |
| 25 | 6% | 0.5803 | $30,374,872 | $1,035,584 | 29.331 |  | $5,089,294 | $2,494,539 | 2.040 |  | $2,448,556 | $1,819,333 | 1.3459 |
| 25 | 7% | 0.5380 | $28,158,970 | $1,035,584 | 27.191 |  | $4,718,020 | $2,494,539 | 1.891 |  | $2,269,930 | $1,819,333 | 1.2477 |
| 25 | 12% | 0.3870 | $20,254,325 | $1,035,584 | 19.558 |  | $3,393,601 | $2,494,539 | 1.360 |  | $1,632,727 | $1,819,333 | 0.8974 |

Scenario C1

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $16,913,336 | $4,266,944 | 3.964 |  | $3,633,603 | $6,140,292 | 0.592 |  | $2,112,465 | $7,496,245 | 0.2818 |
| 10 | 5% | 0.4000 | $16,146,501 | $4,266,944 | 3.784 |  | $3,468,859 | $6,140,292 | 0.565 |  | $2,016,688 | $7,496,245 | 0.2690 |
| 10 | 6% | 0.3823 | $15,433,821 | $4,266,944 | 3.617 |  | $3,315,749 | $6,140,292 | 0.540 |  | $1,927,675 | $7,496,245 | 0.2572 |
| 10 | 7% | 0.3659 | $14,770,625 | $4,266,944 | 3.462 |  | $3,173,270 | $6,140,292 | 0.517 |  | $1,844,842 | $7,496,245 | 0.2461 |
| 10 | 12% | 0.2988 | $12,062,993 | $4,266,944 | 2.827 |  | $2,591,572 | $6,140,292 | 0.422 |  | $1,506,661 | $7,496,245 | 0.2010 |
| 15 | 4% | 0.5769 | $23,289,226 | $4,266,944 | 5.458 |  | $5,003,377 | $6,140,292 | 0.815 |  | $2,908,810 | $7,496,245 | 0.3880 |
| 15 | 5% | 0.5396 | $21,783,508 | $4,266,944 | 5.105 |  | $4,679,894 | $6,140,292 | 0.762 |  | $2,720,747 | $7,496,245 | 0.3629 |
| 15 | 6% | 0.5059 | $20,424,287 | $4,266,944 | 4.787 |  | $4,387,883 | $6,140,292 | 0.715 |  | $2,550,981 | $7,496,245 | 0.3403 |
| 15 | 7% | 0.4755 | $19,194,535 | $4,266,944 | 4.498 |  | $4,123,688 | $6,140,292 | 0.672 |  | $2,397,386 | $7,496,245 | 0.3198 |
| 15 | 12% | 0.3600 | $14,530,918 | $4,266,944 | 3.405 |  | $3,121,772 | $6,140,292 | 0.508 |  | $1,814,903 | $7,496,245 | 0.2421 |
| 20 | 4% | 0.6593 | $26,616,966 | $4,266,944 | 6.238 |  | $5,718,297 | $6,140,292 | 0.931 |  | $3,324,443 | $7,496,245 | 0.4435 |
| 20 | 5% | 0.6093 | $24,596,391 | $4,266,944 | 5.764 |  | $5,284,204 | $6,140,292 | 0.861 |  | $3,072,074 | $7,496,245 | 0.4098 |
| 20 | 6% | 0.5649 | $22,806,157 | $4,266,944 | 5.345 |  | $4,899,596 | $6,140,292 | 0.798 |  | $2,848,475 | $7,496,245 | 0.3800 |
| 20 | 7% | 0.5255 | $21,214,917 | $4,266,944 | 4.972 |  | $4,557,740 | $6,140,292 | 0.742 |  | $2,649,730 | $7,496,245 | 0.3535 |
| 20 | 12% | 0.3825 | $15,440,277 | $4,266,944 | 3.619 |  | $3,317,136 | $6,140,292 | 0.540 |  | $1,928,481 | $7,496,245 | 0.2573 |
| 25 | 4% | 0.6829 | $27,569,391 | $4,266,944 | 6.461 |  | $5,922,913 | $6,140,292 | 0.965 |  | $3,443,400 | $7,496,245 | 0.4594 |
| 25 | 5% | 0.6283 | $25,364,836 | $4,266,944 | 5.944 |  | $5,449,294 | $6,140,292 | 0.887 |  | $3,168,053 | $7,496,245 | 0.4226 |
| 25 | 6% | 0.5803 | $23,427,527 | $4,266,944 | 5.490 |  | $5,033,089 | $6,140,292 | 0.820 |  | $2,926,084 | $7,496,245 | 0.3903 |
| 25 | 7% | 0.5380 | $21,718,447 | $4,266,944 | 5.090 |  | $4,665,916 | $6,140,292 | 0.760 |  | $2,712,621 | $7,496,245 | 0.3619 |
| 25 | 12% | 0.3870 | $15,621,753 | $4,266,944 | 3.661 |  | $3,356,124 | $6,140,292 | 0.547 |  | $1,951,147 | $7,496,245 | 0.2603 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $24,874,410 | $1,035,584 | 24.020 |  | $4,230,613 | $2,494,539 | 1.696 |  | $1,953,196 | $1,819,333 | 1.0736 |
| 10 | 5% | 0.4000 | $23,746,627 | $1,035,584 | 22.931 |  | $4,038,801 | $2,494,539 | 1.619 |  | $1,864,640 | $1,819,333 | 1.0249 |
| 10 | 6% | 0.3823 | $22,698,490 | $1,035,584 | 21.919 |  | $3,860,535 | $2,494,539 | 1.548 |  | $1,782,338 | $1,819,333 | 0.9797 |
| 10 | 7% | 0.3659 | $21,723,129 | $1,035,584 | 20.977 |  | $3,694,647 | $2,494,539 | 1.481 |  | $1,705,750 | $1,819,333 | 0.9376 |
| 10 | 12% | 0.2988 | $17,741,021 | $1,035,584 | 17.131 |  | $3,017,374 | $2,494,539 | 1.210 |  | $1,393,066 | $1,819,333 | 0.7657 |
| 15 | 4% | 0.5769 | $34,251,419 | $1,035,584 | 33.074 |  | $5,825,445 | $2,494,539 | 2.335 |  | $2,689,500 | $1,819,333 | 1.4783 |
| 15 | 5% | 0.5396 | $32,036,963 | $1,035,584 | 30.936 |  | $5,448,813 | $2,494,539 | 2.184 |  | $2,515,616 | $1,819,333 | 1.3827 |
| 15 | 6% | 0.5059 | $30,037,958 | $1,035,584 | 29.006 |  | $5,108,824 | $2,494,539 | 2.048 |  | $2,358,650 | $1,819,333 | 1.2964 |
| 15 | 7% | 0.4755 | $28,229,364 | $1,035,584 | 27.259 |  | $4,801,220 | $2,494,539 | 1.925 |  | $2,216,635 | $1,819,333 | 1.2184 |
| 15 | 12% | 0.3600 | $21,370,592 | $1,035,584 | 20.636 |  | $3,634,688 | $2,494,539 | 1.457 |  | $1,678,068 | $1,819,333 | 0.9224 |
| 20 | 4% | 0.6593 | $39,145,519 | $1,035,584 | 37.800 |  | $6,657,828 | $2,494,539 | 2.669 |  | $3,073,796 | $1,819,333 | 1.6895 |
| 20 | 5% | 0.6093 | $36,173,863 | $1,035,584 | 34.931 |  | $6,152,412 | $2,494,539 | 2.466 |  | $2,840,455 | $1,819,333 | 1.5613 |
| 20 | 6% | 0.5649 | $33,540,970 | $1,035,584 | 32.388 |  | $5,704,613 | $2,494,539 | 2.287 |  | $2,633,714 | $1,819,333 | 1.4476 |
| 20 | 7% | 0.5255 | $31,200,736 | $1,035,584 | 30.129 |  | $5,306,588 | $2,494,539 | 2.127 |  | $2,449,954 | $1,819,333 | 1.3466 |
| 20 | 12% | 0.3825 | $22,707,985 | $1,035,584 | 21.928 |  | $3,862,150 | $2,494,539 | 1.548 |  | $1,783,083 | $1,819,333 | 0.9801 |
| 25 | 4% | 0.6829 | $40,546,249 | $1,035,584 | 39.153 |  | $6,896,063 | $2,494,539 | 2.764 |  | $3,183,785 | $1,819,333 | 1.7500 |
| 25 | 5% | 0.6283 | $37,304,014 | $1,035,584 | 36.022 |  | $6,344,627 | $2,494,539 | 2.543 |  | $2,929,197 | $1,819,333 | 1.6100 |
| 25 | 6% | 0.5803 | $34,454,818 | $1,035,584 | 33.271 |  | $5,860,039 | $2,494,539 | 2.349 |  | $2,705,472 | $1,819,333 | 1.4871 |
| 25 | 7% | 0.5380 | $31,941,276 | $1,035,584 | 30.844 |  | $5,432,538 | $2,494,539 | 2.178 |  | $2,508,102 | $1,819,333 | 1.3786 |
| 25 | 12% | 0.3870 | $22,974,881 | $1,035,584 | 22.185 |  | $3,907,543 | $2,494,539 | 1.566 |  | $1,804,041 | $1,819,333 | 0.9916 |

Scenario D1

| Rigid Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $18,922,449 | $85,533,505 | 0.221 |  | $4,111,515 | $85,533,505 | 0.048 |  | $2,318,347 | $150,266,817 | 0.0154 |
| 10 | 5% | 0.4000 | $18,064,523 | $85,533,505 | 0.211 |  | $3,925,102 | $85,533,505 | 0.046 |  | $2,213,235 | $150,266,817 | 0.0147 |
| 10 | 6% | 0.3246 | $14,660,225 | $85,533,505 | 0.171 |  | $3,185,409 | $85,533,505 | 0.037 |  | $1,796,146 | $150,266,817 | 0.0120 |
| 10 | 7% | 0.3131 | $14,140,850 | $85,533,505 | 0.165 |  | $3,072,557 | $85,533,505 | 0.036 |  | $1,732,513 | $150,266,817 | 0.0115 |
| 10 | 12% | 0.2260 | $10,206,516 | $85,533,505 | 0.119 |  | $2,217,696 | $85,533,505 | 0.026 |  | $1,250,485 | $150,266,817 | 0.0083 |
| 15 | 4% | 0.5769 | $26,055,723 | $85,533,505 | 0.305 |  | $5,661,449 | $85,533,505 | 0.066 |  | $3,192,303 | $150,266,817 | 0.0212 |
| 15 | 5% | 0.5152 | $23,268,670 | $85,533,505 | 0.272 |  | $5,055,872 | $85,533,505 | 0.059 |  | $2,850,838 | $150,266,817 | 0.0190 |
| 15 | 6% | 0.4627 | $20,897,863 | $85,533,505 | 0.244 |  | $4,540,737 | $85,533,505 | 0.053 |  | $2,560,371 | $150,266,817 | 0.0170 |
| 15 | 7% | 0.4157 | $18,775,059 | $85,533,505 | 0.220 |  | $4,079,489 | $85,533,505 | 0.048 |  | $2,300,289 | $150,266,817 | 0.0153 |
| 15 | 12% | 0.3143 | $14,194,175 | $85,533,505 | 0.166 |  | $3,084,144 | $85,533,505 | 0.036 |  | $1,739,046 | $150,266,817 | 0.0116 |
| 20 | 4% | 0.6593 | $29,778,761 | $85,533,505 | 0.348 |  | $6,470,400 | $85,533,505 | 0.076 |  | $3,648,444 | $150,266,817 | 0.0243 |
| 20 | 5% | 0.6015 | $27,165,476 | $85,533,505 | 0.318 |  | $5,902,579 | $85,533,505 | 0.069 |  | $3,328,268 | $150,266,817 | 0.0221 |
| 20 | 6% | 0.5491 | $24,799,841 | $85,533,505 | 0.290 |  | $5,388,568 | $85,533,505 | 0.063 |  | $3,038,435 | $150,266,817 | 0.0202 |
| 20 | 7% | 0.5024 | $22,692,593 | $85,533,505 | 0.265 |  | $4,930,700 | $85,533,505 | 0.058 |  | $2,780,258 | $150,266,817 | 0.0185 |
| 20 | 12% | 0.3674 | $16,595,364 | $85,533,505 | 0.194 |  | $3,605,880 | $85,533,505 | 0.042 |  | $2,033,236 | $150,266,817 | 0.0135 |
| 25 | 4% | 0.6829 | $30,844,324 | $85,533,505 | 0.361 |  | $6,701,928 | $85,533,505 | 0.078 |  | $3,778,995 | $150,266,817 | 0.0251 |
| 25 | 5% | 0.6263 | $28,285,095 | $85,533,505 | 0.331 |  | $6,145,852 | $85,533,505 | 0.072 |  | $3,465,442 | $150,266,817 | 0.0231 |
| 25 | 6% | 0.5767 | $26,045,454 | $85,533,505 | 0.305 |  | $5,659,218 | $85,533,505 | 0.066 |  | $3,191,045 | $150,266,817 | 0.0212 |
| 25 | 7% | 0.5330 | $24,070,569 | $85,533,505 | 0.281 |  | $5,230,110 | $85,533,505 | 0.061 |  | $2,949,086 | $150,266,817 | 0.0196 |
| 25 | 12% | 0.3842 | $17,350,708 | $85,533,505 | 0.203 |  | $3,770,003 | $85,533,505 | 0.044 |  | $2,125,780 | $150,266,817 | 0.0141 |

| Articulated Trucks | Front |  | Side |  | Rear |
| --- | --- | --- | --- | --- | --- |
| Period | Rate | Multiplier | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |  | PV Benefits | Cost | BCR |
| 10 | 4% | 0.4190 | $27,829,209 | $27,402,434 | 1.016 |  | $4,787,047 | $66,007,629 | 0.073 |  | $2,144,691 | $48,141,095 | 0.0446 |
| 10 | 5% | 0.4000 | $26,567,458 | $27,402,434 | 0.970 |  | $4,570,007 | $66,007,629 | 0.069 |  | $2,047,453 | $48,141,095 | 0.0425 |
| 10 | 6% | 0.3823 | $25,394,815 | $27,402,434 | 0.927 |  | $4,368,294 | $66,007,629 | 0.066 |  | $1,957,082 | $48,141,095 | 0.0407 |
| 10 | 7% | 0.3659 | $24,303,591 | $27,402,434 | 0.887 |  | $4,180,587 | $66,007,629 | 0.063 |  | $1,872,985 | $48,141,095 | 0.0389 |
| 10 | 12% | 0.2988 | $19,848,454 | $27,402,434 | 0.724 |  | $3,414,236 | $66,007,629 | 0.052 |  | $1,529,645 | $48,141,095 | 0.0318 |
| 15 | 4% | 0.5769 | $38,320,101 | $27,402,434 | 1.398 |  | $6,591,640 | $66,007,629 | 0.100 |  | $2,953,184 | $48,141,095 | 0.0613 |
| 15 | 5% | 0.5396 | $35,842,592 | $27,402,434 | 1.308 |  | $6,165,471 | $66,007,629 | 0.093 |  | $2,762,252 | $48,141,095 | 0.0574 |
| 15 | 6% | 0.5059 | $33,606,129 | $27,402,434 | 1.226 |  | $5,780,765 | $66,007,629 | 0.088 |  | $2,589,896 | $48,141,095 | 0.0538 |
| 15 | 7% | 0.4755 | $31,582,694 | $27,402,434 | 1.153 |  | $5,432,704 | $66,007,629 | 0.082 |  | $2,433,958 | $48,141,095 | 0.0506 |
| 15 | 12% | 0.3600 | $23,909,178 | $27,402,434 | 0.873 |  | $4,112,742 | $66,007,629 | 0.062 |  | $1,842,589 | $48,141,095 | 0.0383 |
| 20 | 4% | 0.6593 | $43,795,565 | $27,402,434 | 1.598 |  | $7,533,503 | $66,007,629 | 0.114 |  | $3,375,157 | $48,141,095 | 0.0701 |
| 20 | 5% | 0.6093 | $40,470,910 | $27,402,434 | 1.477 |  | $6,961,612 | $66,007,629 | 0.105 |  | $3,118,939 | $48,141,095 | 0.0648 |
| 20 | 6% | 0.5649 | $37,525,259 | $27,402,434 | 1.369 |  | $6,454,915 | $66,007,629 | 0.098 |  | $2,891,929 | $48,141,095 | 0.0601 |
| 20 | 7% | 0.5255 | $34,907,032 | $27,402,434 | 1.274 |  | $6,004,540 | $66,007,629 | 0.091 |  | $2,690,152 | $48,141,095 | 0.0559 |
| 20 | 12% | 0.3825 | $25,405,437 | $27,402,434 | 0.927 |  | $4,370,122 | $66,007,629 | 0.066 |  | $1,957,900 | $48,141,095 | 0.0407 |
| 25 | 4% | 0.6829 | $45,362,686 | $27,402,434 | 1.655 |  | $7,803,072 | $66,007,629 | 0.118 |  | $3,495,929 | $48,141,095 | 0.0726 |
| 25 | 5% | 0.6283 | $41,735,310 | $27,402,434 | 1.523 |  | $7,179,108 | $66,007,629 | 0.109 |  | $3,216,381 | $48,141,095 | 0.0668 |
| 25 | 6% | 0.5803 | $38,547,662 | $27,402,434 | 1.407 |  | $6,630,784 | $66,007,629 | 0.100 |  | $2,970,721 | $48,141,095 | 0.0617 |
| 25 | 7% | 0.5380 | $35,735,540 | $27,402,434 | 1.304 |  | $6,147,056 | $66,007,629 | 0.093 |  | $2,754,002 | $48,141,095 | 0.0572 |
| 25 | 12% | 0.3870 | $25,704,038 | $27,402,434 | 0.938 |  | $4,421,485 | $66,007,629 | 0.067 |  | $1,980,912 | $48,141,095 | 0.0411 |

(b). Fleet registration approximation

Note: this method was used to provide a sensitivity comparison to the method above.

- For a given year, calculate the proportion of vehicles in the fleet fitted with devices, assuming they are only fitted to new vehicles (the figures only apply to rigid or articulated trucks).

- For a given year, multiply the overall cost of installing devices with the calculated proportion of the fleet. Adjust the cost using Present Values.

- For a given year, multiply the possible overall benefit from installing devices with the calculated proportion of the fleet.  Adjust the benefit using Present Values.

- For a given year, calculate the cumulative Net Present Values of the benefits and costs.

- For a given year calculate the cumulative Benefit-Cost Ratio.

| Scenario B1 Alternative Method - rigid vehicles |
| --- |
| Best Case 4% Discount rate |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Number of fleet fitted with UP (,000) | 0.0 | 9.7 | 19.4 | 29.1 | 38.8 | 48.5 | 58.2 | 67.9 | 77.6 | 87.3 | 97.0 | 106.7 | 116.4 |
| Percentage of fleet fitted with UP (%) | 0% | 5% | 10% | 15% | 20% | 25% | 30% | 35% | 40% | 45% | 50% | 55% | 60% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 1.8 | 3.6 | 5.3 | 7.1 | 8.9 | 10.7 | 12.4 | 14.2 | 16.0 | 17.8 | 19.5 | 21.3 |
| Present Value (PV) of the Benefit | 0.0 | 1.7 | 3.3 | 4.7 | 6.1 | 7.3 | 8.4 | 9.4 | 10.4 | 11.2 | 12.0 | 12.7 | 13.3 |
| Cumulative PV of the Benefit | 0.0 | 1.7 | 5.0 | 9.7 | 15.8 | 23.1 | 31.5 | 41.0 | 51.3 | 62.6 | 74.6 | 87.2 | 100.5 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 4.3 | 4.1 | 3.9 | 3.8 | 3.6 | 3.5 | 3.4 | 3.2 | 3.1 | 3.0 | 2.9 | 2.8 | 2.7 |
| Cumulative PV of the Cost | 4.3 | 8.4 | 12.3 | 16.1 | 19.8 | 23.3 | 26.6 | 29.9 | 33.0 | 36.0 | 38.9 | 41.6 | 44.3 |
| Net Present Value (NPV) | -4.3 | -6.7 | -7.3 | -6.4 | -4.0 | -0.2 | 4.9 | 11.1 | 18.3 | 26.6 | 35.7 | 45.6 | 56.2 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.7 | 1.9 | 2.1 | 2.3 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.4 | 0.8 | 1.1 | 1.5 | 1.9 | 2.3 | 2.6 | 3.0 | 3.4 | 3.8 | 4.1 | 4.5 |
| Present Value (PV) of the Benefit | 0.0 | 0.4 | 0.7 | 1.0 | 1.3 | 1.5 | 1.8 | 2.0 | 2.2 | 2.4 | 2.5 | 2.7 | 2.8 |
| Cumulative PV of the Benefit | 0.0 | 0.4 | 1.1 | 2.1 | 3.3 | 4.9 | 6.7 | 8.7 | 10.9 | 13.2 | 15.8 | 18.5 | 21.3 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 8.2 | 7.9 | 7.6 | 7.3 | 7.0 | 6.7 | 6.5 | 6.2 | 6.0 | 5.8 | 5.5 | 5.3 | 5.1 |
| Cumulative PV of the Cost | 8.2 | 16.1 | 23.7 | 31.0 | 38.0 | 44.8 | 51.2 | 57.5 | 63.5 | 69.2 | 74.8 | 80.1 | 85.3 |
| Net Present Value (NPV) | -8.2 | -15.7 | -22.6 | -28.9 | -34.7 | -39.9 | -44.6 | -48.8 | -52.6 | -56.0 | -59.0 | -61.7 | -64.0 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.2 | 0.5 | 0.7 | 0.9 | 1.1 | 1.4 | 1.6 | 1.8 | 2.0 | 2.3 | 2.5 | 2.7 |
| Present Value (PV) of the Benefit | 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 0.9 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 |
| Cumulative PV of the Benefit | 0.0 | 0.2 | 0.6 | 1.2 | 2.0 | 3.0 | 4.0 | 5.3 | 6.6 | 8.0 | 9.6 | 11.2 | 12.9 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 7.5 | 7.2 | 6.9 | 6.7 | 6.4 | 6.2 | 5.9 | 5.7 | 5.5 | 5.3 | 5.1 | 4.9 | 4.7 |
| Cumulative PV of the Cost | 7.5 | 14.7 | 21.6 | 28.3 | 34.7 | 40.9 | 46.8 | 52.5 | 58.0 | 63.2 | 68.3 | 73.2 | 77.8 |
| Net Present Value (NPV) | -7.5 | -14.5 | -21.0 | -27.1 | -32.7 | -37.9 | -42.8 | -47.2 | -51.4 | -55.2 | -58.7 | -62.0 | -65.0 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 |

| Year | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of fleet fitted with UP (,000) | 126.1 | 135.8 | 145.5 | 155.2 | 164.9 | 174.6 | 184.3 | 194.0 | 203.6 | 213.3 | 223.0 | 232.7 | 242.4 |
| Percentage of fleet fitted with UP (%) | 65% | 70% | 75% | 80% | 85% | 90% | 95% | 100% | 105% | 110% | 115% | 120% | 125% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 23.1 | 24.9 | 26.6 | 28.4 | 30.2 | 32.0 | 33.7 | 35.5 | 37.3 | 39.1 | 40.8 | 42.6 | 44.4 |
| Present Value (PV) of the Benefit | 13.9 | 14.4 | 14.8 | 15.2 | 15.5 | 15.8 | 16.0 | 16.2 | 16.4 | 16.5 | 16.6 | 16.6 | 16.6 |
| Cumulative PV of the Benefit | 114.4 | 128.8 | 143.5 | 158.7 | 174.2 | 190.0 | 206.0 | 222.2 | 238.6 | 255.0 | 271.6 | 288.2 | 304.9 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 2.6 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2.0 | 1.9 | 1.9 | 1.8 | 1.7 | 1.7 | 1.6 |
| Cumulative PV of the Cost | 46.9 | 49.3 | 51.7 | 54.0 | 56.2 | 58.3 | 60.3 | 62.3 | 64.1 | 65.9 | 67.7 | 69.3 | 70.9 |
| Net Present Value (NPV) | 67.5 | 79.4 | 91.8 | 104.7 | 118.0 | 131.7 | 145.7 | 159.9 | 174.4 | 189.1 | 203.9 | 218.9 | 234.0 |
| Benefit/Cost Ratio (BCR) | 2.4 | 2.6 | 2.8 | 2.9 | 3.1 | 3.3 | 3.4 | 3.6 | 3.7 | 3.9 | 4.0 | 4.2 | 4.3 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 4.9 | 5.3 | 5.6 | 6.0 | 6.4 | 6.8 | 7.1 | 7.5 | 7.9 | 8.3 | 8.6 | 9.0 | 9.4 |
| Present Value (PV) of the Benefit | 2.9 | 3.0 | 3.1 | 3.2 | 3.3 | 3.3 | 3.4 | 3.4 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 |
| Cumulative PV of the Benefit | 24.2 | 27.3 | 30.4 | 33.6 | 36.9 | 40.2 | 43.6 | 47.0 | 50.5 | 54.0 | 57.5 | 61.0 | 64.5 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 4.9 | 4.7 | 4.6 | 4.4 | 4.2 | 4.1 | 3.9 | 3.7 | 3.6 | 3.5 | 3.3 | 3.2 | 3.1 |
| Cumulative PV of the Cost | 90.2 | 94.9 | 99.5 | 103.9 | 108.1 | 112.1 | 116.0 | 119.8 | 123.4 | 126.8 | 130.2 | 133.4 | 136.5 |
| Net Present Value (NPV) | -66.0 | -67.7 | -69.1 | -70.3 | -71.2 | -71.9 | -72.4 | -72.7 | -72.9 | -72.9 | -72.7 | -72.4 | -71.9 |
| Benefit/Cost Ratio (BCR) | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5 | 0.5 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 3.0 | 3.2 | 3.4 | 3.6 | 3.9 | 4.1 | 4.3 | 4.6 | 4.8 | 5.0 | 5.2 | 5.5 | 5.7 |
| Present Value (PV) of the Benefit | 1.8 | 1.8 | 1.9 | 1.9 | 2.0 | 2.0 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1 | 2.1 |
| Cumulative PV of the Benefit | 14.7 | 16.5 | 18.4 | 20.4 | 22.3 | 24.4 | 26.4 | 28.5 | 30.6 | 32.7 | 34.8 | 37.0 | 39.1 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 4.5 | 4.3 | 4.2 | 4.0 | 3.8 | 3.7 | 3.6 | 3.4 | 3.3 | 3.2 | 3.0 | 2.9 | 2.8 |
| Cumulative PV of the Cost | 82.4 | 86.7 | 90.8 | 94.8 | 98.7 | 102.4 | 106.0 | 109.4 | 112.7 | 115.8 | 118.9 | 121.8 | 124.6 |
| Net Present Value (NPV) | -67.7 | -70.2 | -72.4 | -74.5 | -76.3 | -78.0 | -79.5 | -80.9 | -82.1 | -83.1 | -84.0 | -84.8 | -85.5 |
| Benefit/Cost Ratio (BCR) | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 |

|  |  |  |  |  |  |  | Front | Side | Rear |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of new vehicles per year (,000) | 10 |  | Installation cost for each vehicle ($) | $440 | $847 | $773 |  |  |  |  |
| Total number of vehicles in the fleet (,000) | 194.4 |  | Benefit per year if installed on whole fleet ($m) | $35.6 | $7.5 | $4.6 |  |  |  |  |
| Discount rate | 4% |  |  |  |  |  |  |  |  |  |  |  |  |
| Summary | Front |  |  |  | Side |  |  |  | Rear |  |  |  |
| Period (years) | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 |
| Net Present Value (NPV) ($m) | 35.7 | 91.8 | 159.9 | 234.0 | -59.0 | -69.1 | -72.7 | -71.9 | -58.7 | -72.4 | -80.9 | -85.5 |
| Benefit/Cost Ratio (BCR) | 1.9 | 2.8 | 3.6 | 4.3 | 0.2 | 0.3 | 0.4 | 0.5 | 0.1 | 0.2 | 0.3 | 0.3 |

| Scenario B1 Alternative Method - rigid vehicles |
| --- |
| Likely Case 7% Discount rate |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Number of fleet fitted with UP (,000) | 0.0 | 9.7 | 19.4 | 29.1 | 38.8 | 48.5 | 58.2 | 67.9 | 77.6 | 87.3 | 97.0 | 106.7 | 116.4 |
| Percentage of fleet fitted with UP (%) | 0% | 5% | 10% | 15% | 20% | 25% | 30% | 35% | 40% | 45% | 50% | 55% | 60% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 1.8 | 3.6 | 5.3 | 7.1 | 8.9 | 10.7 | 12.4 | 14.2 | 16.0 | 17.8 | 19.5 | 21.3 |
| Present Value (PV) of the Benefit | 0.0 | 1.7 | 3.1 | 4.3 | 5.4 | 6.3 | 7.1 | 7.7 | 8.3 | 8.7 | 9.0 | 9.3 | 9.5 |
| Cumulative PV of the Benefit | 0.0 | 1.7 | 4.8 | 9.1 | 14.5 | 20.9 | 28.0 | 35.7 | 44.0 | 52.7 | 61.7 | 71.0 | 80.4 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 4.3 | 4.0 | 3.7 | 3.5 | 3.3 | 3.0 | 2.8 | 2.7 | 2.5 | 2.3 | 2.2 | 2.0 | 1.9 |
| Cumulative PV of the Cost | 4.3 | 8.3 | 12.0 | 15.5 | 18.7 | 21.8 | 24.6 | 27.3 | 29.7 | 32.1 | 34.2 | 36.3 | 38.2 |
| Net Present Value (NPV) | -4.3 | -6.6 | -7.2 | -6.4 | -4.2 | -0.9 | 3.3 | 8.4 | 14.2 | 20.6 | 27.4 | 34.7 | 42.3 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.1 | 1.3 | 1.5 | 1.6 | 1.8 | 2.0 | 2.1 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.4 | 0.8 | 1.1 | 1.5 | 1.9 | 2.3 | 2.6 | 3.0 | 3.4 | 3.8 | 4.1 | 4.5 |
| Present Value (PV) of the Benefit | 0.0 | 0.4 | 0.7 | 0.9 | 1.1 | 1.3 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2.0 | 2.0 |
| Cumulative PV of the Benefit | 0.0 | 0.4 | 1.0 | 1.9 | 3.1 | 4.4 | 5.9 | 7.6 | 9.3 | 11.1 | 13.1 | 15.0 | 17.0 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 8.2 | 7.7 | 7.2 | 6.7 | 6.3 | 5.9 | 5.5 | 5.1 | 4.8 | 4.5 | 4.2 | 3.9 | 3.6 |
| Cumulative PV of the Cost | 8.2 | 15.9 | 23.1 | 29.8 | 36.0 | 41.9 | 47.3 | 52.5 | 57.2 | 61.7 | 65.9 | 69.8 | 73.4 |
| Net Present Value (NPV) | -8.2 | -15.5 | -22.0 | -27.8 | -32.9 | -37.5 | -41.4 | -44.9 | -47.9 | -50.6 | -52.8 | -54.8 | -56.4 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.2 | 0.5 | 0.7 | 0.9 | 1.1 | 1.4 | 1.6 | 1.8 | 2.0 | 2.3 | 2.5 | 2.7 |
| Present Value (PV) of the Benefit | 0.0 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.1 | 1.2 | 1.2 | 1.2 |
| Cumulative PV of the Benefit | 0.0 | 0.2 | 0.6 | 1.2 | 1.9 | 2.7 | 3.6 | 4.6 | 5.6 | 6.8 | 7.9 | 9.1 | 10.3 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 7.5 | 7.0 | 6.5 | 6.1 | 5.7 | 5.3 | 5.0 | 4.7 | 4.4 | 4.1 | 3.8 | 3.6 | 3.3 |
| Cumulative PV of the Cost | 7.5 | 14.5 | 21.0 | 27.2 | 32.9 | 38.2 | 43.2 | 47.9 | 52.3 | 56.3 | 60.1 | 63.7 | 67.0 |
| Net Present Value (NPV) | -7.5 | -14.3 | -20.4 | -26.0 | -31.0 | -35.6 | -39.6 | -43.3 | -46.6 | -49.6 | -52.2 | -54.6 | -56.7 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 |

| Year | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of fleet fitted with UP (,000) | 126.1 | 135.8 | 145.5 | 155.2 | 164.9 | 174.6 | 184.3 | 194.0 | 203.6 | 213.3 | 223.0 | 232.7 | 242.4 |
| Percentage of fleet fitted with UP (%) | 65% | 70% | 75% | 80% | 85% | 90% | 95% | 100% | 105% | 110% | 115% | 120% | 125% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 23.1 | 24.9 | 26.6 | 28.4 | 30.2 | 32.0 | 33.7 | 35.5 | 37.3 | 39.1 | 40.8 | 42.6 | 44.4 |
| Present Value (PV) of the Benefit | 9.6 | 9.6 | 9.7 | 9.6 | 9.6 | 9.5 | 9.3 | 9.2 | 9.0 | 8.8 | 8.6 | 8.4 | 8.2 |
| Cumulative PV of the Benefit | 90.0 | 99.6 | 109.3 | 118.9 | 128.5 | 137.9 | 147.2 | 156.4 | 165.4 | 174.2 | 182.9 | 191.3 | 199.4 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 1.8 | 1.7 | 1.5 | 1.4 | 1.4 | 1.3 | 1.2 | 1.1 | 1.0 | 1.0 | 0.9 | 0.8 | 0.8 |
| Cumulative PV of the Cost | 39.9 | 41.6 | 43.1 | 44.6 | 45.9 | 47.2 | 48.4 | 49.5 | 50.5 | 51.5 | 52.4 | 53.2 | 54.0 |
| Net Present Value (NPV) | 50.1 | 58.0 | 66.2 | 74.3 | 82.5 | 90.7 | 98.9 | 106.9 | 114.9 | 122.8 | 130.5 | 138.0 | 145.4 |
| Benefit/Cost Ratio (BCR) | 2.3 | 2.4 | 2.5 | 2.7 | 2.8 | 2.9 | 3.0 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 4.9 | 5.3 | 5.6 | 6.0 | 6.4 | 6.8 | 7.1 | 7.5 | 7.9 | 8.3 | 8.6 | 9.0 | 9.4 |
| Present Value (PV) of the Benefit | 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 1.9 | 1.9 | 1.9 | 1.8 | 1.8 | 1.7 |
| Cumulative PV of the Benefit | 19.0 | 21.1 | 23.1 | 25.2 | 27.2 | 29.2 | 31.2 | 33.1 | 35.0 | 36.9 | 38.7 | 40.5 | 42.2 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 3.4 | 3.2 | 3.0 | 2.8 | 2.6 | 2.4 | 2.3 | 2.1 | 2.0 | 1.9 | 1.7 | 1.6 | 1.5 |
| Cumulative PV of the Cost | 76.8 | 80.0 | 83.0 | 85.8 | 88.4 | 90.8 | 93.1 | 95.2 | 97.2 | 99.0 | 100.7 | 102.4 | 103.9 |
| Net Present Value (NPV) | -57.8 | -58.9 | -59.9 | -60.6 | -61.2 | -61.6 | -61.9 | -62.1 | -62.2 | -62.1 | -62.0 | -61.9 | -61.7 |
| Benefit/Cost Ratio (BCR) | 0.2 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 3.0 | 3.2 | 3.4 | 3.6 | 3.9 | 4.1 | 4.3 | 4.6 | 4.8 | 5.0 | 5.2 | 5.5 | 5.7 |
| Present Value (PV) of the Benefit | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.1 | 1.1 | 1.1 | 1.0 |
| Cumulative PV of the Benefit | 11.5 | 12.8 | 14.0 | 15.3 | 16.5 | 17.7 | 18.9 | 20.1 | 21.2 | 22.4 | 23.5 | 24.5 | 25.6 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 3.1 | 2.9 | 2.7 | 2.5 | 2.4 | 2.2 | 2.1 | 1.9 | 1.8 | 1.7 | 1.6 | 1.5 | 1.4 |
| Cumulative PV of the Cost | 70.1 | 73.1 | 75.8 | 78.3 | 80.7 | 82.9 | 85.0 | 86.9 | 88.7 | 90.4 | 92.0 | 93.5 | 94.9 |
| Net Present Value (NPV) | -58.6 | -60.3 | -61.8 | -63.1 | -64.2 | -65.2 | -66.1 | -66.8 | -67.5 | -68.1 | -68.5 | -68.9 | -69.3 |
| Benefit/Cost Ratio (BCR) | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.3 | 0.3 | 0.3 |

|  |  |  |  |  |  |  | Front | Side | Rear |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of new vehicles per year (,000) | 10 |  | Installation cost for each vehicle ($) | $440 | $847 | $773 |  |  |  |  |
| Total number of vehicles in the fleet (,000) | 194.4 |  | Benefit per year if installed on whole fleet ($m) | $35.6 | $7.5 | $4.6 |  |  |  |  |
| Discount rate | 7% |  |  |  |  |  |  |  |  |  |  |  |  |
| Summary | Front |  |  |  | Side |  |  |  | Rear |  |  |  |
| Period (years) | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 |
| Net Present Value (NPV) ($m) | 27.4 | 66.2 | 106.9 | 145.4 | -52.8 | -59.9 | -62.1 | -61.7 | -52.2 | -61.8 | -66.8 | -69.3 |
| Benefit/Cost Ratio (BCR) | 1.8 | 2.5 | 3.2 | 3.7 | 0.2 | 0.3 | 0.3 | 0.4 | 0.1 | 0.2 | 0.2 | 0.3 |

| Scenario B1 Alternative Method - rigid vehicles |
| --- |
| Worst Case 12% Discount rate |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Year | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Number of fleet fitted with UP (,000) | 0.0 | 9.7 | 19.4 | 29.1 | 38.8 | 48.5 | 58.2 | 67.9 | 77.6 | 87.3 | 97.0 | 106.7 | 116.4 |
| Percentage of fleet fitted with UP (%) | 0% | 5% | 10% | 15% | 20% | 25% | 30% | 35% | 40% | 45% | 50% | 55% | 60% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 1.8 | 3.6 | 5.3 | 7.1 | 8.9 | 10.7 | 12.4 | 14.2 | 16.0 | 17.8 | 19.5 | 21.3 |
| Present Value (PV) of the Benefit | 0.0 | 1.6 | 2.8 | 3.8 | 4.5 | 5.0 | 5.4 | 5.6 | 5.7 | 5.8 | 5.7 | 5.6 | 5.5 |
| Cumulative PV of the Benefit | 0.0 | 1.6 | 4.4 | 8.2 | 12.7 | 17.8 | 23.2 | 28.8 | 34.5 | 40.3 | 46.0 | 51.6 | 57.1 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 4.3 | 3.8 | 3.4 | 3.0 | 2.7 | 2.4 | 2.2 | 1.9 | 1.7 | 1.5 | 1.4 | 1.2 | 1.1 |
| Cumulative PV of the Cost | 4.3 | 8.1 | 11.5 | 14.5 | 17.2 | 19.6 | 21.8 | 23.7 | 25.5 | 27.0 | 28.4 | 29.6 | 30.7 |
| Net Present Value (NPV) | -4.3 | -6.5 | -7.1 | -6.3 | -4.5 | -1.9 | 1.3 | 5.0 | 9.0 | 13.3 | 17.6 | 22.0 | 26.4 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.2 | 0.4 | 0.6 | 0.7 | 0.9 | 1.1 | 1.2 | 1.4 | 1.5 | 1.6 | 1.7 | 1.9 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.4 | 0.8 | 1.1 | 1.5 | 1.9 | 2.3 | 2.6 | 3.0 | 3.4 | 3.8 | 4.1 | 4.5 |
| Present Value (PV) of the Benefit | 0.0 | 0.3 | 0.6 | 0.8 | 1.0 | 1.1 | 1.1 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 |
| Cumulative PV of the Benefit | 0.0 | 0.3 | 0.9 | 1.7 | 2.7 | 3.8 | 4.9 | 6.1 | 7.3 | 8.5 | 9.7 | 10.9 | 12.1 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 8.2 | 7.3 | 6.5 | 5.8 | 5.2 | 4.7 | 4.2 | 3.7 | 3.3 | 3.0 | 2.6 | 2.4 | 2.1 |
| Cumulative PV of the Cost | 8.2 | 15.5 | 22.1 | 27.9 | 33.1 | 37.8 | 42.0 | 45.7 | 49.0 | 52.0 | 54.6 | 57.0 | 59.1 |
| Net Present Value (NPV) | -8.2 | -15.2 | -21.1 | -26.2 | -30.5 | -34.0 | -37.1 | -39.6 | -41.7 | -43.4 | -44.9 | -46.0 | -47.0 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 0.0 | 0.2 | 0.5 | 0.7 | 0.9 | 1.1 | 1.4 | 1.6 | 1.8 | 2.0 | 2.3 | 2.5 | 2.7 |
| Present Value (PV) of the Benefit | 0.0 | 0.2 | 0.4 | 0.5 | 0.6 | 0.6 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 |
| Cumulative PV of the Benefit | 0.0 | 0.2 | 0.6 | 1.1 | 1.6 | 2.3 | 3.0 | 3.7 | 4.4 | 5.2 | 5.9 | 6.6 | 7.3 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 7.5 | 6.7 | 6.0 | 5.3 | 4.8 | 4.3 | 3.8 | 3.4 | 3.0 | 2.7 | 2.4 | 2.2 | 1.9 |
| Cumulative PV of the Cost | 7.5 | 14.2 | 20.2 | 25.5 | 30.3 | 34.5 | 38.3 | 41.7 | 44.7 | 47.4 | 49.9 | 52.0 | 53.9 |
| Net Present Value (NPV) | -7.5 | -14.0 | -19.6 | -24.4 | -28.6 | -32.2 | -35.3 | -38.0 | -40.3 | -42.3 | -44.0 | -45.4 | -46.6 |
| Benefit/Cost Ratio (BCR) | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 |

| Year | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of fleet fitted with UP (,000) | 126.1 | 135.8 | 145.5 | 155.2 | 164.9 | 174.6 | 184.3 | 194.0 | 203.6 | 213.3 | 223.0 | 232.7 | 242.4 |
| Percentage of fleet fitted with UP (%) | 65% | 70% | 75% | 80% | 85% | 90% | 95% | 100% | 105% | 110% | 115% | 120% | 125% |
| Front UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 23.1 | 24.9 | 26.6 | 28.4 | 30.2 | 32.0 | 33.7 | 35.5 | 37.3 | 39.1 | 40.8 | 42.6 | 44.4 |
| Present Value (PV) of the Benefit | 5.3 | 5.1 | 4.9 | 4.6 | 4.4 | 4.2 | 3.9 | 3.7 | 3.5 | 3.2 | 3.0 | 2.8 | 2.6 |
| Cumulative PV of the Benefit | 62.4 | 67.4 | 72.3 | 76.9 | 81.3 | 85.5 | 89.4 | 93.1 | 96.5 | 99.8 | 102.8 | 105.6 | 108.2 |
| Installation cost of UP for new vehicles ($m) | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 | 4.3 |
| Present Value (PV) of the Cost | 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.6 | 0.5 | 0.4 | 0.4 | 0.4 | 0.3 | 0.3 | 0.3 |
| Cumulative PV of the Cost | 31.7 | 32.5 | 33.3 | 34.0 | 34.6 | 35.2 | 35.7 | 36.1 | 36.5 | 36.9 | 37.2 | 37.5 | 37.7 |
| Net Present Value (NPV) | 30.7 | 34.9 | 39.0 | 42.9 | 46.7 | 50.3 | 53.7 | 57.0 | 60.0 | 62.9 | 65.6 | 68.1 | 70.5 |
| Benefit/Cost Ratio (BCR) | 2.0 | 2.1 | 2.2 | 2.3 | 2.3 | 2.4 | 2.5 | 2.6 | 2.6 | 2.7 | 2.8 | 2.8 | 2.9 |
| Side UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 4.9 | 5.3 | 5.6 | 6.0 | 6.4 | 6.8 | 7.1 | 7.5 | 7.9 | 8.3 | 8.6 | 9.0 | 9.4 |
| Present Value (PV) of the Benefit | 1.1 | 1.1 | 1.0 | 1.0 | 0.9 | 0.9 | 0.8 | 0.8 | 0.7 | 0.7 | 0.6 | 0.6 | 0.6 |
| Cumulative PV of the Benefit | 13.2 | 14.3 | 15.3 | 16.3 | 17.2 | 18.1 | 18.9 | 19.7 | 20.4 | 21.1 | 21.8 | 22.3 | 22.9 |
| Installation cost of UP for new vehicles ($m) | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 | 8.2 |
| Present Value (PV) of the Cost | 1.9 | 1.7 | 1.5 | 1.3 | 1.2 | 1.1 | 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.5 |
| Cumulative PV of the Cost | 60.9 | 62.6 | 64.1 | 65.5 | 66.7 | 67.7 | 68.7 | 69.5 | 70.3 | 71.0 | 71.6 | 72.1 | 72.6 |
| Net Present Value (NPV) | -47.7 | -48.3 | -48.8 | -49.2 | -49.4 | -49.6 | -49.8 | -49.8 | -49.9 | -49.8 | -49.8 | -49.8 | -49.7 |
| Benefit/Cost Ratio (BCR) | 0.2 | 0.2 | 0.2 | 0.2 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 |
| Rear UP |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Benefits from percentage of fleet fitted with UP ($m) | 3.0 | 3.2 | 3.4 | 3.6 | 3.9 | 4.1 | 4.3 | 4.6 | 4.8 | 5.0 | 5.2 | 5.5 | 5.7 |
| Present Value (PV) of the Benefit | 0.7 | 0.7 | 0.6 | 0.6 | 0.6 | 0.5 | 0.5 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.3 |
| Cumulative PV of the Benefit | 8.0 | 8.7 | 9.3 | 9.9 | 10.4 | 11.0 | 11.5 | 11.9 | 12.4 | 12.8 | 13.2 | 13.5 | 13.9 |
| Installation cost of UP for new vehicles ($m) | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 |
| Present Value (PV) of the Cost | 1.7 | 1.5 | 1.4 | 1.2 | 1.1 | 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.6 | 0.5 | 0.4 |
| Cumulative PV of the Cost | 55.6 | 57.2 | 58.6 | 59.8 | 60.9 | 61.8 | 62.7 | 63.5 | 64.2 | 64.8 | 65.4 | 65.8 | 66.3 |
| Net Present Value (NPV) | -47.6 | -48.5 | -49.3 | -49.9 | -50.4 | -50.9 | -51.2 | -51.5 | -51.8 | -52.0 | -52.2 | -52.3 | -52.4 |
| Benefit/Cost Ratio (BCR) | 0.1 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 |

|  |  |  |  |  |  |  | Front | Side | Rear |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Number of new vehicles per year (,000) | 10 |  | Installation cost for each vehicle ($) | $440 | $847 | $773 |  |  |  |  |
| Total number of vehicles in the fleet (,000) | 194.4 |  | Benefit per year if installed on whole fleet ($m) | $35.6 | $7.5 | $4.6 |  |  |  |  |
| Discount rate | 12% |  |  |  |  |  |  |  |  |  |  |  |  |
| Summary | Front |  |  |  | Side |  |  |  | Rear |  |  |  |
| Period (years) | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 | 10 | 15 | 20 | 25 |
| Net Present Value (NPV) ($m) | 17.6 | 39.0 | 57.0 | 70.5 | -44.9 | -48.8 | -49.8 | -49.7 | -44.0 | -49.3 | -51.5 | -52.4 |
| Benefit/Cost Ratio (BCR) | 1.6 | 2.2 | 2.6 | 2.9 | 0.2 | 0.2 | 0.3 | 0.3 | 0.1 | 0.2 | 0.2 | 0.2 |

Summary of Benefit-Costs

| Scenario A - Low Effectiveness UP |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  | Front |  |  | Side |  |  | Rear |  |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 5.0 | 3.4 | 1.7 | 0.7 | 0.5 | 0.2 | 0.4 | 0.3 | 0.1 |
| Articulated | 30.0 | 20.9 | 10.1 | 2.0 | 1.4 | 0.7 | 1.4 | 1.0 | 0.5 |

| Scenario B - Most Likely Effectiveness UP |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  | Front |  |  | Side |  |  | Rear |  |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 5.7 | 4.0 | 1.9 | 0.8 | 0.6 | 0.3 | 0.4 | 0.3 | 0.1 |
| Articulated | 34.5 | 24.0 | 11.7 | 2.4 | 1.7 | 0.8 | 1.6 | 1.1 | 0.5 |

| Scenario C - High Effectiveness UP |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  | Front |  |  | Side |  |  | Rear |  |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 6.5 | 4.5 | 1.9 | 1.0 | 0.7 | 0.3 | 0.5 | 0.3 | 0.1 |
| Articulated | 39.2 | 27.3 | 13.3 | 2.8 | 1.9 | 0.9 | 1.7 | 1.2 | 0.6 |

| Scenario D - Energy Absorbing UP |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  | Front |  |  | Side |  |  | Rear |  |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 0.36 | 0.22 | 0.09 | 0.08 | 0.05 | 0.02 | 0.03 | 0.02 | 0.01 |
| Articulated | 1.66 | 1.15 | 0.56 | 0.12 | 0.08 | 0.04 | 0.07 | 0.05 | 0.02 |

Best Case - 25 year pay-off period @4%, costed for fatalities, injuries and other costs

Likely Case - 15 year pay-off period @7%, costed for fatalities, injuries and other costs

Worst Case - 10 year pay-off period @12%, costed for fatalities and injuries cost only

Comparison of Benefit-Costs

| Scenario B - Most Likely Effectiveness UP Device |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Front |  |  | Side |  |  | Rear |  |
|  | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case | Best Case | Likely Case | Worst Case |
| Rigid | 5.7 | 4.0 | 1.9 | 0.8 | 0.6 | 0.3 | 0.4 | 0.3 | 0.1 |
| Alternative method | 4.3 | 2.5 | 1.6 | 0.5 | 0.3 | 0.2 | 0.3 | 0.2 | 0.1 |
| Articulated | 34.5 | 24.0 | 11.7 | 2.4 | 1.7 | 0.8 | 1.6 | 1.1 | 0.5 |
| Alternative method | 19.7 | 11.6 | 7.4 | 1.7 | 1.0 | 0.6 | 0.4 | 0.5 | 0.3 |

Sensitivity of Benefit-Costs

| Scenario A - Low Effectiveness UP Device |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Front | Cost spread over (yrs) |  |  | Side | Cost spread over (yrs) |  |  | Rear | Cost spread over (yrs) |  |  |
|  | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 |
| Rigid | $ 1,078 | 108 | 72 | 54 | -$ 438 | -44 | -29 | -22 | -$ 574 | -57 | -38 | -29 |
| Articulated | $ 8,756 | 876 | 584 | 438 | $ 325 | 32 | 22 | 16 | -$ 17 | -2 | -1 | -1 |

| Scenario B - Most Likely Effectiveness UP Device |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Front | Cost spread over (yrs) |  |  | Side | Cost spread over (yrs) |  |  | Rear | Cost spread over (yrs) |  |  |
|  | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 |
| Rigid | $ 1,305 | 130 | 87 | 65 | -$ 353 | -35 | -24 | -18 | -$ 549 | -55 | -37 | -27 |
| Articulated | $10,134 | 1013 | 676 | 507 | $ 568 | 57 | 38 | 28 | $ 79 | 8 | 5 | 4 |

| Scenario C - High Effectiveness UP Device |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Front | Cost spread over (yrs) |  |  | Side | Cost spread over (yrs) |  |  | Rear | Cost spread over (yrs) |  |  |
|  | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 |
| Rigid | $ 1,539 | 154 | 103 | 77 | -$ 278 | -28 | -19 | -14 | -$ 526 | -53 | -35 | -26 |
| Articulated | $11,554 | 1155 | 770 | 578 | $ 783 | 78 | 52 | 39 | $ 169 | 17 | 11 | 8 |

| Scenario D - Energy Absorbing UP Device |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Front | Cost spread over (yrs) |  |  | Side | Cost spread over (yrs) |  |  | Rear | Cost spread over (yrs) |  |  |
|  | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 | Cost margin | 10 | 15 | 20 |
| Rigid | -$ 343 | -34 | -23 | -17 | -$ 806 | -81 | -54 | -40 | -$ 761 | -76 | -51 | -38 |
| Articulated | $ 67 | 7 | 4 | 3 | -$ 777 | -78 | -52 | -39 | -$ 734 | -73 | -49 | -37 |

Cost margin- the amount ($) that the UP cost for each vehicle would have to be adjusted by to give a Benefit-Cost Ratio (BCR) of one  (Note: these are approximate as the BCRs are based on the Likely case which is a 15 year period).

Sensitivity of Extra Load on the Axle(s) – Cost  of payload reduction where axle limits are not increased

| Annual revenue ($ million) | 20,699 | Average distance travelled laden - rigid (km per year per truck) | 13,106 |
| --- | --- | --- | --- |
| Front UP mass (kg) | 110 | Average distance travelled laden - articulated (km per year per truck) | 57,541 |
| Distribution of trucks across fleet | Proportion | Typical empty mass (tonnes) |  | Typical loaded mass | Typical payload | FUPmass reduction | Percentage payload lost |
| 2 axle rigid truck | 40% | 5 |  | 15 | 10 | 0.11 |  |
| 3 axle rigid truck | 30% | 6 |  | 23 | 17 | 0.11 |  |
| 4 axle Twin-Steer rigid truck | 10% | 8 |  | 27 | 19 | 0.11 |  |
| 2 axle rigid truck with 2 axle dog trailer | 15% | 8 |  | 30 | 22 | 0.11 |  |
| 3 axle rigid truck with 3 axle dog trailer | 5% | 10 |  | 42.5 | 32.5 | 0.11 |  |
| Total rigid truck |  |  |  |  | 101 | 0.6 | 0.55% |
| 3 axle semi-trailer | 5% | 7 |  | 24 | 17 | 0.11 |  |
| 5 axle semi-trailer | 20% | 10 |  | 40 | 30 | 0.11 |  |
| 6 axle semi-trailer | 40% | 12 |  | 45.5 | 33.5 | 0.11 |  |
| 7 axle B-Double | 5% | 12 |  | 57 | 45 | 0.11 |  |
| 8 axle B-Double | 5% | 15 |  | 62.5 | 47.5 | 0.11 |  |
| 9 axle B-Double | 15% | 18 |  | 68 | 50 | 0.11 |  |
| Double Road Train | 5% | 20 |  | 85.7 | 65.7 | 0.11 |  |
| Triple Road Train | 5% | 25 |  | 125.2 | 100.2 | 0.11 |  |
| Total articulated truck |  |  |  |  | 308 | 0.9 | 0.29% |
| Rigid plus articulated trucks, proportioned for distance travelled |  |  |  |  |  | 0.33% |
| Potential revenue loss per year ($ million) |  |  |  |  |  | 69 |

Source: ABS (2002) Year Book Australia for revenue and distance travelled, ABS (2005) for vehicle numbers and ABS, NRTC Cost Allocation Model for fleet distribution.

Sensitivity of Extra Load on the Axle(s) - Summary of Benefit-Cost ratios where axle limits are increased by 100 kg

Scenario A - Low Effectiveness UP Device

|  |  | Front |  |
| --- | --- | --- | --- |
|  | Best Case | Likely Case | Worst Case |
| Rigid | 3.3 | 2.3 | 0.9 |
| Articulated | 20.3 | 14.2 | 5.9 |

Scenario B - Most Likely Effectiveness UP Device

|  |  | Front |  |
| --- | --- | --- | --- |
|  | Best Case | Likely Case | Worst Case |
| Rigid | 4.0 | 2.8 | 1.2 |
| Articulated | 24.8 | 17.3 | 7.4 |

Best Case - 25 year pay-off period @4%, costed for fatalities, injuries and other costs

Likely Case - 15 year pay-off period @7%, costed for fatalities, injuries and other costs

Worst Case - 10 year pay-off period @12%, costed for fatalities and injuries cost only

Notes

The revised Benefit-cost ratios were calculated as follows:

- 170 000 km with 500 kg additional front axle load = $3545 =  $0.0041 per 100 kg per km per year.

- Articulated trucks, annual cost = 62 278 trucks x 57 541 km x $0.0041 = $14.69m.

- Rigid trucks, annual cost = 194 394 trucks x 13 106 km x $0.0041 = $10.44m.

- The cost used was conservative as it assumes that a rigid vehicle damages the road as much as an articulated vehicle.

- 100 kg was used instead of the worst case 110 kg as a compromise between the mass effect of a short wheelbase cab-over articulated as compared to a bonneted articulated truck or other longer wheelbase rigid trucks. Refer page 27.

Source: ABS (2005) for vehicle numbers, ABS (2002) Year Book Australia for distance travelled, and NTC (2006) for road damage cost.

## APPENDIX 7: LIST OF AFFECTED PARTIES

| Affected Party | Represented by |
| --- | --- |
| Vehicle manufacturers | Commercial Vehicle Industry Council Federal Chamber of Automotive Industries Truck Industry Council |
| Vehicle importers | Federal Chamber of Automotive Industries |
| Automotive component manufacturers | Federation of Automotive Product Manufacturers (member of the FCAI) Australian Road Transport Suppliers Association |
| After-market automotive component manufacturers | Australian Automotive After-market Association |
| Automotive design and testing services | Commercial Vehicle Industry Association of Australia |
| Vehicle certification and compliance services | Commercial Vehicle Industry Association of Australia |
| Vehicle dealers | Motor Traders Association of Australia |
| State and territory governments | ACT: Department of Urban Services NSW: Roads and Traffic Authority NT: Department of Transport and Works Queensland: Queensland Transport South Australia: Department of Transport Tasmania: Department of Transport Victoria: Vicroads, Department of Infrastructure Western Australia: Department of Transport |
| Consumers (comprising of vehicle owners, individual heavy vehicle operators, commercial institutions and pedestrian representatives) | Australian Automobile Association representing motoring clubs located in: ACT: NRMA NSW: NRMA NT: Queensland: RACQ South Australia: RACSA Tasmania: RACT Victoria: RACV Western Australia: RACWA Australian Commercial Vehicle Association Australian Motorcycle Council Australian Trucking Association Bicycle Federation of Australia Pedestrian Council of Australia |
| Services to consumers Insurance Medical treatment | Australian Medical Association Australian Transport Insurers Association Insurance Council of Australia |

## APPENDIX 8: Technical liaison Group

Australian Government

Department of Transport and Regional Services

Consumer (Motoring Clubs)

Australian Automobile Association

State and Territory Governments

Department of Urban Services, Australian Capital Territory

Roads and Traffic Authority, New South Wales

Department of Transport and Works, Northern Territory

Queensland Transport, Queensland

Transport South Australia, South Australia

Department of Energy, Infrastructure and Resources, Tasmania

Vicroads, Victoria

Department of Planning and Infrastructure, Western Australia

New Zealand Government

Land Transport Safety Authority

Industry

Australian Road Transport Suppliers Association

Australian Commercial vehicle Association

Commercial Vehicle Industry Association of Australia

Federal Chamber of Automotive Industries

Commercial vehicle Industry Council

## APPENDIX 9: UNECE R93 Front Underrun Protection

This standard is available separately from:

http://www.unece.org/trans/main/wp29/wp29regs81-100.html

## Notes

# Footnotes

This is calculated by balancing the moments about the rear axle(s) for an 80kg load ie 80kg x 5.5m/4m.

For Australia an application rate of 15 per cent is assumed (See Note 4 ). Cost was calculated by applying the 0.15 rate to the Level 1, Scenario B cost results in Appendix 6 with front, rear and side underrun systems added together, combined rigid and articulated.  Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

Under-run trauma will reduce if a high field application rate can be achieved. Overseas studies in Norway and Sweden advise that field effectiveness for self-regulation can be between 25 to 35 per cent. This rate needs to be adjusted for Australia as Swedish and Norway businesses voluntarily offer a number of safety initiatives of motor vehicles. For Australia an application rate of 15 per cent is assumed, relating mainly to the presence of European manufacturers. Note that this does not take in to account any variation in the performance of the underrun systems themselves. The benefit was calculated by applying the 0.15 rate to the Level 1, Scenario B benefit results in Appendix 6 with front, rear and side underrun systems added together, combined rigid and articulated.  Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

As the Australian certification system is based on a cost recovery model, any benefits from reduced certification costs should more correctly be allocated to business and may in turn be passed on to transport operators

Cost was calculated from the Level 1, Scenario B cost results in Appendix 6 for front underrun systems only, combined rigid and articulated.  Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

Benefit was calculated from the Level 1, Scenario B benefit results in Appendix 6 for front underrun systems only, combined rigid and articulated.  Likely case - discount rate 7% over 15 years, Most Likely effectiveness device.

As the Australian certification system is based on a cost recovery model, any benefits from reduced certification costs should more correctly be allocated to business and may in turn be passed on to transport operators.

# Endnotes

The number of crashes and fatalities for heavy vehicle under-runs was obtained for the period 1990-99.  The ATSB was unable to provide crashes and fatalities for 3 years during that period, the years being 1991, 1993 and 1995. Number of fatalities beyond 1999 was not available from the Fatal Crash Database as there is a lag in compiling data from Coroner reports.

Annually 250 pedestrians are killed. 20 per cent of fatal collisions involve heavy trucks and 20 per cent of truck involved collisions end up as under-run collisions.

these costs are difficult to estimate and are not included in under-run trauma.

Information for the period beyond 1999 was not available from the ATSB. See Appendix 4.

FMVSS, Federal Motor Vehicle Safety Standards

Regulation of the Global Forum for Automotive Technical Regulations, Geneva

Directive of the European Parliament and the Council, Brussels

Regulation of the Global Forum for Automotive Technical Regulations, Geneva

Directive of the European Parliament and the Council, Brussels

Regulation of the Global Forum for Harmonization of Automotive Technical Regulations, Geneva

Directive of the European Parliament and the Council, Brussels

Federal Motor Vehicle Safety Standard of the United States

Regulation of the National Council of Traffic – CONTRAN, Brazil

Economic Commission for Europe is an institution formed from the post World War II Bretton Woods Agreement in 1949.  The institution was set up to facilitate the economic reconstruction of war ravaged Europe.

# Text boxes

0

10

20

30

40

50

60

1990

1992

1994

1996

1997

1998

1999

Number of fatalities

Rigid truck - car

Articulated truck – car