Biodiesel and ethanol specifications and labelling requirements – final proposals for comment

## Proposed Biodiesel Specifications

Biodiesel Specifications

B100 as a final fuel or as a blending component must conform to the parameters set out in the following table:

| Property | Unit | Minimum | Maximum | Test Method |
| --- | --- | --- | --- | --- |
| Ester content | % mass | 96.5 | - | EN 14103 |
| Density at 15ºC | kg/m³ | 860 | 900 | ASTM D 1298 |
| Viscosity at 40ºC | mm²/s | 2.00 | 5.00 | ASTM D 445 |
| Flash point | ºC | 100 | - | ASTM D 93 |
| Sulphur content | mg/kg | - | 10.0 | IP 497 or ASTM D 5453 |
| Carbon residue (on 100% distillation residue) or Carbon residue (on 10% distillation residue) | % mass % mass | - - | 0.050 0.30 | ASTM D 4530 ISO 10370 |
| Cetane number |  | 51.0 | - | ASTM D 613 |
| Sulfated ash content | % mass | - | 0.02 | ASTM D 874 |
| Water content | mg/kg | - | 500 | ASTM D 6304 |
| Total contamination | mg/kg | - | 24.0 | IP 440 |
| Copper strip corrosion (3 h at 50ºC) | rating | class 1 | ASTM D 130 |
| Oxidation stability, 110ºC | hours | 6.00 | - | EN 14112 |
| Acid value | mg KOH/g | - | 0.50 | ASTM D 664 |
| Iodine Value | g iodine/100 g | - | 140 | EN 14111 |
| Linolenic acid methyl ester | % mass | - | 12.0 | EN 14103 |
| Methanol content | % mass | - | 0.20 | EN 14110 |
| Monoglyceride content | % mass | - | 0.80 | ASTM D 6584 |
| Diglyceride content | % mass | - | 0.20 | ASTM D 6584 |
| Triglyceride content | % mass | - | 0.20 | ASTM D 6584 |
| Free glycerol | % mass | - | 0.02 | ASTM D 6584 |
| Total glycerol | % mass | - | 0.25 | ASTM D 6584 |
| Group l metals (Na+K) Group ll metals (Ca+Mg) | mg/kg mg/kg | - - | 5.00 5.00 | EN 14108 and EN 14109 EN 14538 |
| Phosphorus content | mg/kg | - | 10.0 | ASTM D 4951 |

All Biodiesel Blends

All biodiesel blends (retail and non-retail) will need to meet the following specifications included in Schedule 3 of the Petroleum Products Specifications Regulations 2002 (PPSR):

- Cetane Number (51.0 minimum, ASTM D613 or ASTM D6890)

- Colour (3.0 maximum, ASTM D1500)

- Sulphur (50.0 mg/kg maximum, 10.0 mg/kg maximum from 1 January 2009, IP 497 or ASTM D 5453)

- Lubricity (460 µm maximum, IP 450)

- Viscosity (2.0 – 4.5 mm² per second at 40ºC, ASTM D445)

- Flash Point (61ºC minimum, ASTM D93)

- Total Contamination (24.0 mg/kg maximum, IP 440)

Biodiesel blends that are not intended for retail sale must also meet the following specifications:

- Acid Value: 0.1 + 100*X / 250 mg KOH/g maximum (where X is the percentage by volume of biodiesel in the blend), ASTM D 664

- Water Content: 200 + 300*X mg/kg maximum (where X is the percentage by volume of biodiesel in the blend), ASTM D 6304

Retail Biodiesel Blends

Biodiesel blends for retail sale will need to meet all of the specifications in Schedule 3 of the PPSR.

It is proposed that the following amendments be made to Schedule 3 of the PPSR:

- Addition of FAME content – 5.0% by volume maximum (to be reviewed indicatively 2010) which must meet the B100 specifications;

- Particulates to change to Total Contamination – test method IP 440 (limit to remain the same at 24 mg/kg);

- Cold flow properties – Summer in Auckland/Northland Cloud Point 6ºC maximum;

- Cetane number test method – to include ASTM D 6890 for cetane number and a note that ASTM D 976 is not suitable for biodiesel blends; and

- Density test method to be changed from ASTM D 1298 to ASTM D 4052

Proposed Ethanol Specifications

Ethanol Specifications for Blending

(1) The ethanol must contain denaturant.

(2) The ethanol must contain corrosion inhibitor.

(3) The ethanol must conform to the parameters set out in the following table:

| Property | Unit | Limit | Test Method |
| --- | --- | --- | --- |
| Ethanol and higher alcohols (C3 - C5) | volume %, min | 97.0 | ASTM D 5501 |
| Higher alcohols (C3 – C5) | volume %, max | 2.0 | ASTM D 5501 |
| Methanol | volume %, max | 0.5 | ASTM D 5501 |
| Denaturant1 | volume % | 1.0 minimum 1.5 maximum | ASTM D 5501 |
| Water content | volume %, max | 1.0 | ASTM E 203 |
| Solvent-washed gum | mg/100 ml, max | 5.0 | ASTM D 381 |
| Inorganic Chloride content | mg/L, max | 32 | ASTM D 512C (as modified in ASTM D 4806) |
| Copper content | mg/kg, max | 0.1 | ASTM D 1688A (as modified in ASTM D 4806) |
| Sulphate | mg/kg, max | 4 | ASTM D 7318, ASTM D 7319, and ASTM D 7328 |
| Sulphur | mg/kg, max | 30 | IP 497c or ASTM D 5453 |
| Acidity (as acetic acid CH3COOH) | mass %, max | 0.007 | ASTM D 1613 |
| pHe |  | 6.5 – 9.0 | ASTM D 6423 |
| Appearance |  | Clear and bright without particles | ASTM D 4806 |

- The denaturant contained in ethanol must be unleaded regular grade or premium grade petrol with the following minimum characteristics:

    - End point - 210ºC maximum

    - Sulphur - 50 mg/kg maximum

    - Clear and bright

Proposed Ethanol Labelling Requirements

Retail Petrol/Ethanol Blends up to E10

All petrol/ethanol blends not for retail sale do not need to be labelled

Petrol/ethanol blends that contain 1% or less ethanol by volume do not need to be labelled as to their ethanol content.

It is proposed that the following labelling requirements apply to retail sales of petrol/ethanol blends that contain over 1% ethanol by volume:

- the maximum percentage of ethanol by volume must be clearly displayed; and

- the words “May not be suitable for all vehicles/engines.  Check with the manufacturer before use” must be displayed.

# Footnotes

Allowable viscosity 6.00 mm²/s maximum when biodiesel used as a blending component with petroleum diesel.

ASTM D1600 shall be used to obtain the 10% distillation residue.

Allowable cetane number 47.0 minimum when biodiesel used as a blending component with petroleum diesel.

Allowable oxidation stability is 10.0 hours minimum for when biodiesel used as a blending component with petroleum diesel for retail sale.